Electronics for Pedestrians
Ralph J. Steinhagen, CERN
– Tutorial I/II –
“In theory, 'theory' and 'praxis' are the same, in praxis they aren't”

---
Quick getting started with Qucs
- QUCS – Quite universal circuit simulator:	http://qucs.sourceforge.net/
  - similar to SpiceTM & derivatives but open-source
  - DC, AC, S-parameter, harmonic balance analysis,	noise analysis, RF structures, etc.
- If you haven't it already: Linux, Mac & Windows version available at: http://qucs.sourceforge.net/download.html
  - Linux: install from your favourite repository, we use version 0.0.17 but earlier should work as well.
  - Mac: you may need the following steps to temporarily disable security settings: http://osxdaily.com/2012/07/27/app-cant-be-opened-because-it-is-from-an-unidentified-developer/
  - Windows installation (+ dependent packages) should be straight forward

---
Quick getting started with Qucs
Project → New Project → <type and confirm project name>
  - This creates a new projects and switches to 'Content' tab
Now you can start editing your schematic. The available components can be found in the 'components' tab.
  - there is a sub-menu for different categories of components	→ feel free and encouraged to browse
  - more precise parts and pre-configured elements can be found in:	Tools → 'Component Library' (or via 'Ctrl + 4')
1)
2)

---
Quick getting started with Qucs
Design and simulate a simple voltage divider:
- Place two resistors (i.e. drag-and drop) onto the schematic:	Components → lumped components → resistor
  - N.B. You can rotate the components via 'Ctrl+R'
- Place a dc voltage onto the schematic:	Components → sources → dc Voltage Source

---
Quick getting started with Qucs
- Wire the parts either using the 'wire' button, or 'Ctrl+E')
- Place a simulation block – in our case 'DC':	Components → simulations → dc simulation
- Label wires to calculate voltages of give nodes:	Insert → Wire Label (or 'Ctrl+L') – <type/confirm name>
- N.B. if you haven't already → save the schematic:	File → Save (as) (or 'Ctrl+S')→ <type descriptive name>

---
Quick getting started with Qucs
- Issue a Simulation: Simulation → Simulate (or 'F2')
  - This opens a new panel (<name>.dpl) which can house the results and opens the 'Components→diagrams' sub-panel on the left	(you can switch back and forth with 'F4')(you may change this via 'File → Document Settings → 'open data display …' check-box)
- You can add e.g. a table and select (double-click) the nodes for which the currents and voltages have been calculated (here: 'V1.I' & 'midpoint.V')

---
Quick getting started with Qucs
Available dataset items
- Depending on the type of simulation performed you ﬁnd the following types of items in the dataset:
  - node.V	– DC voltage at node node
  - name.I	– DC current through component name
  - node.v	– AC voltage at node node
  - name.i	– AC current through component name
  - node.vn	– AC noise voltage at node node
  - name.in	– AC noise current through component name
  - node.Vt	– transient voltage at node node
  - name.It	– transient current through component name
  - S[1,1]	– S-parameter value
- N.B. Please note that all voltages and currents are peak values and all noise voltages are RMS values at 1Hz bandwidth

---
Quick getting started with Qucs
- Additional functions:
  - read & write data to file
  - execute octave (matlab) scripts
  - (simple) equations
  - … extend missing functionality	(i.e. it's open-source)
- Equations:
  - … = PlotVs(<variable a>, <variable b>, …)
  - … = dB(<variable a>) or … = a*b
  - … = Time2Freq(<variable y>, <time vector>)
  - variables/component value definition → useful if you e.g. want to test two scenarios – just disable ('Ctrl+D') the equation set that isn't in use
- More detailed info:
  - Help → Tutorials → Equations.pdf
  - Help → Tutorials → Functions.pdf
Ctrl+D

---
Qucs – Resonant Circuit

---
Qucs – AC Simulation
- … going to be used more frequently during RF tutorial
  - N.B. Noise simulation needs to be manually enabled:	ac simulations → 'Properties' tab → Noise = <yes/no> (optional: 'display in schematic')

---
Quick getting started with Qucs
Parameter sweeps – can be also cascaded

---
S-Parameter Simulation – Bode Plot (guided)
This will be more discussed during the RF tutorial

---
Exercises – your turn

---
Exercise I
Get acquainted with Qucs – Repeat the examples for the RC and RL high- and low-pass filters
  1. Simulate and plot the transient response.
  2. Simulate and plot (Bode) the frequency response
  3. Can you make a band-pass out of R, C, and Ls?
  4. Discuss the results

---
Exercise II
- A frequency generator (Zi = 50 Ω) is connected to a lossy LC resonator.
  - N.B. This type of structure is important for discussing cavities, impedances and beam instabilities.
  1. You have seen the magnitude response for the circuit. Derive the corresponding phase response as a function of ω, ω0, and ζ.
  - “Construct“ a parallel RLC resonance circuit schematic with L=2.2 uH, C=5 nF, and R being variable (N.B. use 'Parameter Sweep')..
  1. Calculate the resonance frequency for R = 0Ω.
  2. Plot and calculate the quality factor Q for R = 0.1, 1, 2, 10, 20, ...Ω (N.B. use 'Parameter Sweep').
  3. Discuss the results.
IR
IL
IC
IRLC
IRLC
V

---
Exercise III
- We want to study minute 'betatron motion'* at the Australian Synchrotron (circumference≈216 m).
  - Construct a notch filter that suppresses the first revolution lines and main RF frequency (assume: fRF=500 MHz) using only passive components. N.B. There is more than one option!
  - Find the optimal values that would do the job.
    - Somebody mentioned to you that most components are only available for a limited number of values. Find the canonical component values that would match your ideal filter response best.
    - Compare your solution with the real-world R, L, C components including the discussed parasitics.
  - Discuss the pro's, con's and limitations of your solution.
*These are small transverse oscillations of the electron bunches as they circulate around the machine.

---
Exercise IV – Optional
Re-use your RLC resonant circuit from exercise II.
  1. Simulate the transient response to an AC source operating at the LC resonance frequency, and while being
    - switched-on (let the transient stabilise), and
    - subsequently switched-off.
  1. What are your observations when you increase or decrease the quality factor of the resonance?
  - What impact might this have on e.g. bunch-by-bunch diagnostics?