Electronics for Pedestrians
Ralph J. Steinhagen, CERN
– Tutorial II/II –
“In theory, 'theory' and 'praxis' are the same, in praxis they aren't”

---
Exercises – your turn

---
Exercise I
Diodes are probably the single most important non-linear devices in RF application.
  1. Simulate and plot the V-I response curve for the following diodes (N.B. 'DC simulation', use 'DC voltage source' and 'Current Probes'):
    - 1N4002, 1N4148, 1N746, BAS40, BAS70, LED (IR, red, …)
      - Specific diodes are found at: 'Tools → Component Library'
    - Compare and discuss the differences
  1. Simulate and plot the AC voltage-response of the above diodes connected to a 50 Ohm load (exciting frequency: 10 kHz, 1 MHz & 1GHz)
    - Which one would you use for RF applications and why?

---
Exercise II
- For the given schematic (N.B. this doesn't need to be simulated):
  - Explain its function.
  - Suggest a modification that loads the	battery with a constant current of 10 mA.
load
12V
battery

---
Exercise III
Design a circuit schematics for a voltage doubler. Assume a series resistance of Rs=10 Ohm prior to the diode, a load resistance RL=1 kOhm and parallel capacity C=1 uF. Simulate and plot
  1. Transient response for a 1kHz AC voltage source (i.e. first 15 ms)
  2. Re-simulate at 2 MHz.
- Optional: design a full-size high-voltage source (i.e. Cockcroft-Walton, Greiner)
  - What do you reckon are the limitations of such circuits?

---
Exercise IV – Optional
In the given amplifier circuit, the gate bias-voltage is UGS=- 2 V and the drain-source voltage UDS=15 V. The operating voltage +U is 25 V.
  1. Compute R1 and R2 so that the drain current is 5 mA.
  2. “Build” the given schematic and verify the amplification gain for an input voltage of Vpp= 10, 100 and 1000 mV.
  3. What would be the impact of a capacitor in parallel to R2?

---
Exercise V
Using the 741 opamp, design an inverted amplifier with a symmetric ±10 V supply voltage, R1=100 Ohm input resistor and for an AC input voltage Vpp < 500 mV@1 kHz.
  1. Simulate and plot the AC- and transient response for input frequencies ranging from 1 Hz to 10 MHz
  2. Check the amplifier gain for the feedback resistor values	R2=0.1, 1, 10, 1k, and 100 kΩ.
  3. Confirm the relationship between gain and bandwidth
  4. Are there significant offset-voltage effects?

---
Exercise VI
- Somebody drew up the schematic below:
  - What does the circuit do?
  - Assume an input signal Ue(ω,t)=U0⋅sin(ω⋅t). Compute (analytically) the output signal Ua(ω,t). Then...
  - Simulate and confirm your hypothesis using Qucs.
  - How does the circuit behave for square or single/periodic pulses

---
Exercise VII – Optional
- Build a voltage stabiliser using an opamp and JFET
- Simulate and plot the performance.

---
Exercise IV – Optional
Simulate and plot the characteristics of the 2N2222 BJT
  1. Plot the DC-response for UBE =0.5 … 0.8 V and for UCE=10 & 20 V.
  2. Plot the DC-response for UCE=0.1 mV … 10 V and UBE= 0.65...0.8V.
  3. Plot the current amplification for UCE =10 V & 20V.
Design a schematic to measure the FET characteristics (2N3458 or better alternative?). Perform the following simulations:
  1. Plot the drain current as a function of drain-source voltage (0...10 V) for the following gate-source voltages: 0 V, -1 V, -2 V, -3 V.
  2. Plot the drain current as a function of the gate-source voltage for a drain-source voltage of 7V.
  3. Discuss the slope and pinch-off voltage
Discuss the differences between FETs and BJTs

---
- Übernehmen Sie die nebenstehend skizzierte Schaltung in Schematics.
- Untersuchen Sie den Transienten Uaus (t) in einem geeigneten Zeitfenster und erklären Sie die Wirkungsweise dieser Schaltung.

---
- Dimensionieren Sie den gegebenen Schaltplan eines bipolaren Transistors 2N2222 in Emitterschaltung mit Stromgegenkopplung. Vorgegeben sind der Kollektorstrom Ic = 2.7 mA, die Betriebsspannung U+ = 12 V, die Stromverstärkung B = β = 255, die Spannung am Emitter UE = 1.8 V und die Spannung am Kollektor U CA = 6 V. Bei der Dimensionierung ist zu berücksichtigen:
- • Arbeitspunktberechnung über einen Basisspannungsteiler: Dieser ist so zu berechnen, dass der Querstrom (Strom durch R2) I q = 10 IB ist, damit das Basispotential wenig durch IB beeinflusst wird.
- • Dimensionieren Sie die Eingangskapazität Ce so, dass die untere Grenzfrequenz ca. 100 Hz beträgt.
- Führen Sie die folgenden Simulationen durch:
- • Wie groß ist die Kollektorstromänderung in Abhängigkeit von der Temperatur?
- • Wie groß ist die Spannungsverstärkung der Schaltung?
- • AC-Analyse: 0.1 Hz bis 200 MHz
- • Einschwinganalyse: 0 bis 0.5 ms.