Accelerator Lattice Design – Part II Insertions
– Laboratory Exercise –
Ralph J. Steinhagen, CERN
- Acknowledgements and credits to: W. Herr, B. Holzer, A. Streun, A. Wolski

---
Exercise I – 1/2
Design a Chasman-Green Double-Bend-Achromat
  - Start with the doublet Q1+Q2, use the same constraints as during the day before.
    - Assume a fixed cell length of ~10-30m	→ get a reasonable optics with 100 m > βx> βy a the beginning and end of the cell
    - Once you are happy insert the Q3 and D2 at the centre of the doublets
  - The dipole D1 generates dispersion wave which is closed by dipole D2, which is 180° apart → phase advance condition is steered with Q3 and distance between D1 & D2 (hint: M180°-cell = MDrift·MQ3·MDrift).
    - Q1,Q2 are used to make βx in D1 & D2 small
  - Leave some space (~5 m) left and right of the Q1s to allow some space for undulators, RF cavities, or instrumentation.
D2
D1
Q1
Q2
Q3
Q2
Q1

---
Exercise I – 2/2
- Design tips:
  - there is only a narrow range of kQ1, kQ2, and Q3 for which the DBA converges ↔ many local optima → need to guide MAD-X before you can do the regular cell matching (i.e. start with the linear approximations)
  - The first step is thus very much iterative and it's (strongly) recommended that you first match the cell as a transmission line with fixed initial conditions
    - i.e. βx, βy being constant & αx/y,μx/y, Dx/y, and D'x/y being zero. Use the following line to compute the 'Twiss' call : twiss, file=test_output.twiss, betx=<your value>, alfx=0, mux=0, bety=<your value>, alfy=0, muy=0, DX=0, DY=0, DPX=0, DPY=0, deltap=0.0, X=0, Y=0, PX=0, PY=0;
    - Vary Q3, check that you reached the dispersion cancelling condition via:
      - value, table(twiss,MB2,mux)-table(twiss,MB1,mux);
      - Should be equal/very close to '0.5' (ie. phase advances given in units of 2π)
  - Once you are happy with the symmetry of the initial conditions try to match the dispersion suppression and exact beta-function with the cell-matching, I.e use
    - match,sequence=DBACell, betx=<your value>, alfx=0, mux=0, bety=<your value>, alfy=0, muy=0; // [..]
    - and then simply: Twiss; → match, sequence=DBACell;
  - Check how your Q3 value compare with the theoretic linear approximation
  - Enjoy!

---
Exercise II – Dispersion Suppressor (DS)
- Aim: we need (at least) two regions with low dispersion in our existing FoDo lattice to accommodate our RF system and an experiment	(e.g. undulator or high-energy physics interation point).
- Insert two straight sections each consisting of at least cells (e.g. FoDo cells without bending magnets). Keep the same quadrupole focusing:
  - Insert the two straight sections opposite in azimuth in the ring. Plot the results.
- The dispersion shall be well below (< 1 m) along this straight section. Chose and implement one of the following options:
  1. missing-dipole scheme (tip: for the simplest case you need to change Δμcell := 60°), or
  2. changing the bending radius of some or all the bending magnets, or
  3. Full Monty – independent quadrupole-based DS
  - At this stage do not change the focusing properties of the arc cells.

---
Exercise III
- Start from the previous lattice and design a symmetric insertion with a low-β section in a dispersion free region. The β should be small at least in one plane and should have a waist at an ”interaction point”.
- Two options:
  - Try to design the insertion yourself
  - Use an already prepared example sequence and try to match