Machine Protection
Ralph J. Steinhagen, CERN
- Material and acknowledgements to: R. Schmidt and J. Wenninger

---
Safety at accelerators - definitions
Safety at Accelerators – Definitions
Accelerators, as all other technical systems, must respect some general principles with respect to safety:
Protect the people (legal requirements).
Protect the environment (legal requirements).
Protect the equipment (asset management).
– Without beam : superconducting magnets, high power equipment, power cables, normal conducting magnets, RF systems, etc.
– With beam: damage caused by beams.

---
Trends in modern accelerators
Trends in modern Accelerators
All major accelerator projects are pushed to new records.
Higher beam energy and intensity:
Hadron colliders – LHC.
Linear e+e- colliders.
CERN Future Circular Colliders study.
Higher power and brightness:
Neutron spallation sources.
Neutrino physics.
Synchrotron light sources (synchrotron light power).
Frequent mixing of super-conducting magnets/RF and high power beams
In many modern projects machine protection aspects have a large impact on (or may even dominate) design and operation

---
Modern accelerators
Modern Accelerators
High power accelerators – from some 10 kW to above 1 MW.
Neutron spallation sources (SNS, ISIS).
High power/high duty cycle machines (PSI cyclotron, JPARC).
High energy hadron colliders and synchrotrons.
LHC and its upgrades.
Synchrotrons for fixed target experiments (SPS).
e+e- colliders.
B-factories (KEKB, super-KEKB).
Synchrotron light sources.
High power photon beams.
Linear colliders/ Free Electron Lasers (FEL).
SLAC linac, ILC, CLIC, FLASH, XFEL.
Energy recovery linacs.
Medical accelerators.
The patients !

---
Hazard and Risk for accelerators
Hazard and Risk for accelerators
Hazard: a situation that poses a level of threat to the accelerator. Hazards are dormant or potential, with only a theoretical risk of damage. Once a hazard becomes "active“: incident / accident. Consequences and possibility of an incident interact together to create RISK, can be quantified:
RISK = Consequences ∙ Probability
Related to accelerators
- Consequences of an uncontrolled beam loss
- Probability of an uncontrolled beam loss
- The higher the RISK, the more Protection is required

---
The Large Hadron Collider LHC
The Large Hadron Collider LHC
Installed in the LEP tunnel, 27 km, Depth of 70-140 m
the Alps
Lake of Geneva
Sector 34
Jura mountains
LHC ring

---
27 km Circumference – 1232 LHC dipole magnet
B field 8.3 T (11.8 kA) @ 1.9 K (super-fluid Helium)
two-in-one magnet design:	two beam tubes with an opening of 56 mm (210 mm separation)
Operating challenges:
Very low quench levels (~ mJ/cm3) in an environment that stores MJ → GJ
Control of particle beam stability and losses is paramount!

---
Relevant parameters for MPS
Relevant parameters for MPS
One LHC beam = 360 MJ = ?
Momentum of the particle
Particle type
Activation is mainly an issue for hadron accelerators.
Energy stored in the beam
1 MJ can heat and melt 1.5 kg of copper.
Beam power
Beam size
Power or energy density
Time structure of beam
The kinetic energy of a 200 m long train at 155 km/hour
90 kg of TNT
Key factor : how easily and how fast
the energy is released !!
15 kg of chocolate

---
Stored Beam Energies
Stored Beam Energies
x 200
XFEL (1s)
x 10 000
Quench Levels	Units	Tevatron	RHIC	HERA	LHC
Instant loss (0.01 - 10 ms)	[mJ/cm3]	4.5	18	2.1 - 6.6	87
Steady loss (> 100 s)	[mW/cm3]	75	75		5.3
[Speaker Notes: LHC extrapolation Energy in beam 7 times Tevatron Intensity of beam 30 times Tevatron Number of LHC of moving elements in the LHC about 200 Energy stored in both beams:	0.7 GJoule heat up from cryogenic temperature and melt 0.1 m3 of Copper]

---
From uncontrolled damage tests…
From uncontrolled damage tests…
A real case from the 2008 SPS run !
Impact on the vacuum chamber of a	400 GeV beam of 3x1013 protons (2 MJ).
Event is due to an insufficient coverage of the SPS MPS (known !).
Vacuum chamber to atmospheric pressure, downtime ~ 3 days.
Risk = (3 days downtime + dose to workers)	x (1 event / 5-10 years)

---
…to controlled damage tests
…to controlled damage tests
In the past decade a lot of effort was invested to better understand the interaction of high energy / high density beams with matter.
Experiments:
Ad-hoc experiments for the LHC,
Construction of a dedicated test facility at CERN (HiRadMat @ SPS).
Modeling and comparison with tests.
Many matter phases (solid, liquid, plasma), ‘hydro-codes’.
Some outcomes:
Validation of LHC carbon collimator robustness,
Validation of damage thresholds for LHC injection energy,
Validation of simulation codes,
Search for more robust material.

---
SPS experiment : damage at 450 GeV
SPS Experiment : Damage at 450 GeV
Controlled SPS experiment / protons.
- Energy 450 GeV,
- Beam area σx x σy = 1.1 x 0.6 mm2,
- Damage limit for copper at 2×1012 p.
- No damage to stainless steel.
Shot	Intensity / p+
A	1.2×1012
B	2.4×1012
C	4.8×1012
D	7.2×1012
Special target (sandwich of Tin, Steel, Copper plates)
Damage limit is ~200 kJ, < 0.1 % of a nominal LHC beam.
Impact D:  1/3 of nominal LHC injection.
25 cm
V.Kain et al
6 cm
A B D C

---
HiRadMat tests – new materials
HiRadMat Tests – New Materials
Courtesy A. Bertarelli (EN)
CERN CAS - Machine Protection - J. Wenninger
Inermet 180, 72 bunches
Molybdenum, 72 & 144 bunches
Glidcop, 72 bunches (2 x)
Copper-Diamond
144 bunches
Molybdenum-Copper-Diamond 144 bunches
Molybdenum-Graphite (3 grades)
144 bunches

---
Release of 600 MJ at LHC
Release of 600 MJ at LHC
The 2008 LHC accident happened during test runs without beam.
A magnet interconnect was defect and the circuit opened. An electrical arc provoked a He pressure wave damaging ~600 m of LHC, polluting the beam vacuum over more than 2 km.
53 magnets had to be repaired
Arcing in the interconnection
Over-pressure
Magnet displacement

---
Machine Protection
Machine Protection

---
Example for Active Protection - Traffic
Example for Active Protection - Traffic
A monitor detects a dangerous situation
An action is triggered
The energy stored in the system is safely dissipated

---
Example for Passive Protection
Example for Passive Protection
Active protection not possible – passive protection by bumper, air bag, safety belts
The monitor fails to detect a dangerous situation
The reaction time is too short

---
Modern Machine Protection System : P3
Modern Machine Protection System : P3
Protect the machine
Highest priority is to avoid damage of the accelerator.
Protect the beam
Complex protection systems reduce the availability of the accelerator, the number of “false” interlocks stopping operation must be minimized.
Trade-off between protection and operation.
Provide the evidence
Clear (post-mortem) diagnostics must be provided when:
the protection systems stop operation,
something goes wrong (failure, damage, but also ‘near miss’).

---
MPS design strategy
MPS Design Strategy
Avoid a failure by design – if you can.
Detect a failure at the hardware (equipment) level and stop operation – first protection layer.
Detect the consequences of the failure on beam parameters	(orbit, tune, losses etc) and stop operation – second protection layer.
Stop beam operation.
Inhibit injection, send beam to a dump,
Stop the beam by collimators / absorbers.
Demonstrate safety / availability / reliability
use established methods to analyse critical systems and to predict failure rate
Managing interlocks
disabling of interlocks is common practice (keep track !)
LHC: masking of some interlocks possible for low intensity/low energy beams
Elements of protection – third protection layer
Equipment and beam monitoring,
Collimators and absorbers, beam dumps,
Interlock system linking different systems.

---
Timescales @ LHC
Time
10000 turns
= 0.89 s
1000 turns
100 turns
Quench
protection
Power converter
interlocks
UFO
10 turns
FMCM
1 turn
= 89 ms
Kicker
magnets
BPMs
BLMs
Absorbers
NC magnet
powering failures
Quenches
Operational
‘mistakes’

---
The beam’s gone immediately isn’t it?
The beam’s gone immediately isn’t it?
Unfortunately even the best failure detection takes some time, the signal must be propagated to the dumping system, the dumping system must synchronize to the beam.
Unavoidable delay to fire the dump !
At the LHC the delay can be up to ~3 turns – ~300 s.

---
Learning curve
LHC Machine Protection Learning Curve
It took more than a year of commissioning and tuning (e.g. BLM thresholds) to reach the maximum intensity at 3.5/4 TeV

---
Beam instrumentation for machine protection
Beam Instrumentation for Machine Protection
Beam Loss Monitors
  - stop beam operation in case of too high beam losses
  - monitor beam losses around the accelerator (full coverage?)
  - could be fast and/or slow (LHC down to 40 s)
- Beam Position Monitors
  - ensuring that the beam has the correct position
  - in general, the beam should be centred in the aperture
- Beam Current Transformers
  - if the transmission between two locations of the accelerator is too low (=beam lost somewhere): stop beam operation
  - if the beam lifetime is too short: dump beam
- Beam Size Monitors
  - if beam size is too small could be dangerous for windows, targets, …

---
Beam Loss Monitors
Beam Loss Monitors
Ionization chambers to detect beam losses:
Reaction time ~ ½ turn (40 s)
Very large dynamic range (> 106)
There are ~3600 chambers distributed over the ring to detect abnormal beam losses and if necessary trigger a beam abort !

---
LHC
LHC
IR5:CMS
3600 x
IR4: RF + Beam instrumentation
IR8: LHC-B
IR2: ALICE
IR1: ATLAS
Injection
Injection

---
Beam collimation (cleaning)
Beam Collimation (cleaning)
The LHC requires a complex multi-stage collimation system to operate at high intensity.
Previous hadron machines used collimators only for experimental background conditions.
Almost 100 collimators, mostly made of Carbon and Tungsten, protect the superconducting magnets against energy deposition from the beam
140 MJ in each beam
versus
few mJ to quench a magnet
beam
1.2 m

---
Collimation system
Collimation System
To be able to absorb the energy of the protons, the collimators are staged – primary, secondary, tertiary – multi-stage system.
The system worked perfectly – also thanks to excellent beam stabilization and machine reproducibility – only one setup / year.
~99.99% of the protons that were lost from the beam were intercepted.
No magnet was quenched in operation at 3.5/4 TeV.
Experiment
Protection
devices
Primary
collimator
Secondary
collimators
Tertiary
collimators
Triplet
magnets
Absorbers
Tertiary halo
particle showers
Primary
halo particle
Secondary halo
+ particle showers
Beam

---
LHC
IR5:CMS
3600 x
IR4: RF + Beam instrumentation
100 x
Opening
IR3: Momentum Collimation
IR7: Betatron Collimation
IR8: LHC-B
IR2: ALICE
IR1: ATLAS
Injection
Injection

---
Continuous beam losses at LHC
Continuous beam losses at LHC
The BLM signals near the experiments are almost as high at the collimators (steady losses) due to the luminosity.
At the experiments the BLM record collision debris – in fact the physics at small angles not covered by the experiments !!
Collisions points
Collimators
Loss rate
S

---
LHC beam dumping system
LHC beam dumping system
When it is time to get rid of the beams (also in case of emergency!) , the beams are ‘kicked’ out of the ring by a system of kicker magnets and send into a dump block !
Ultra-high reliability system
15 septum magnets deflect the beam vertically
Beam 1
Q5L
10 kicker magnets dilute the beam
Beam dump block
Q4L
 900 m
15 fast ‘kicker’ magnets deflect the beam to the outside
Q4R
 500 m
Q5R
quadrupoles
Beam 2

---
LHC dump line
LHC Dump Line

---
The LHC dump block
The LHC dump block
The dump block is the only LHC element capable of absorbing the nominal beam
CERN visit McEwen

---
Beam dump
Beam Dump
- Screen in front of the beam dump block
- Each light dot shows the passage of one proton bunch traversing the screen
- Each proton bunch has a different trajectory, to better distribute the energy across a large volume
50 cm

---
The Unexpected

---
Incidents happen
Incidents happen
JPARC home page – October 2013

---
JPARC incident – May 2013
JPARC incident – May 2013
Due to a power converter failure, a slow extraction was transformed into a fast extraction.
Extraction in milliseconds instead of seconds.
As a consequence of the high peak power a target was damaged and radio-isotopes were released into experimental halls.
>> machine protection coupled to personnel protection !
Investigations and protection improvements are ongoing to allow JPAC to restart.
One insufficiently covered failure case had major consequences !

---
Summary
Machine protection:
manages risk = 'failure probability' * 'failure consequences'
requires a comprehensive overview of all aspects of the accelerator (accelerator physics, operation, equipment, instrumentation),
requires understanding the different failure types that could lead to uncontrolled beam loss,
must be an integral part of the machine design,
is becoming increasingly important for future projects, with increased beam power / energy density and increasingly complex machines.

---
Acknowledgements to many colleagues from CERN
and to the authors of the listed papers
- R.F.Koontz, Multiple Beam Pulse of the SLAC Injector, PAC 1967
- R.Bacher et al., The HERA Quench Protection System, a Status Report, EPAC 1996
- C.Adolphsen et al., The Next Linear Collider Machine Protection System, PAC 1999
- M.C.Ross et al., Single Pulse Damage in Copper, LINAC 2000
- C.Sibley, Machine Protection Strategies for High Power Accelerators, PAC 2003
- C.Sibley, The SNS Machine Protection System: Early Commissioning Results and Future Plans, PAC 2005
- S.R.Buckley and R.J.Smith, Monitoring and Machine Protection Designs for the Daresbury Laboratory Energy Recovery Linac Prototype, EPAC 2006
- L.Fröhlich et al., First Operation of the FLASH Machine Protection System with long Bunch Trains, LINAC 2006
- L.Fröhlich et al., First Experience with the Machine Protection System of FLASH, FEL 2006
- N.V.Mokhov et al., Beam Induced Damage to the TEVATRON Components and what has been done about it, HB2006
- M.Werner and K.Wittenburg, Very fast Beam Losses at HERA, and what has been done about it, HB2006
- S.Henderson, Status of the Spallation Neutron Source: Machine and Experiments, PAC 2007
- H.Yoshikawa et al., Current Status of the Control System for J-PARC Accelerator Complex, ICALEPCS 2007
- L.Froehlich, Machine Protection for FLASH and the European XFEL, DESY PhD Thesis 2009
- A.C.Mezger, Control and protection aspects of the megawatt proton accelerator at PSI, HB2010
- Y.Zhang, D.Stout, J.Wei, ANALYSIS OF BEAM DAMAGE TO FRIB DRIVER LINAC, SRF 2012

---
References
Acknowledgements to many colleagues from CERN
and to the authors of the listed papers
CERN and LHC
- R.B.Appleby et. al., Beam-related machine protection for the CERN Large Hadron Collider experiments, Phys. Rev. ST Accel. Beams 13, 061002 (2010)
- R.Schmidt et al., Protection of the CERN Large Hadron Collider, New Journal of Physics 8 (2006) 290
- R.Schmidt, Machine Protection, CERN CAS 2008 Dourdan on Beam Diagnostics
- N.Tahir et al., Simulations of the Full Impact of the LHC Beam on Solid Copper and Graphite Targets, IPAC 2010, Kyoto, Japan, 23 - 28 May 2010
Theses
- Verena Kain, Machine Protection and Beam Quality during the LHC Injection Process, CERN-THESIS-2005-047
- G.Guaglio, Reliability of the Beam Loss Monitors System for the Large Hadron Collider at CERN /, CERN-THESIS-2006-012 PCCF-T-0509
- Benjamin Todd, A Beam Interlock System for CERN High Energy Accelerators, CERN-THESIS-2007-019
- A. Gomez Alonso, Redundancy of the LHC machine protection systems in case of magnet failures / CERN-THESIS-2009-023
- Sigrid Wagner, LHC Machine Protection System: Method for Balancing Machine Safety and Beam Availability /, CERN-THESIS-2010-215
- Roderik Bruce, Beam loss mechanisms in relativistic heavy-ion colliders, CERN-THESIS-2010-030

---
References
Acknowledgements to many colleagues from CERN
and to the authors of the listed papers
- L.Tchelidze, In how long the ESS beam pulse would start melting steel/copper accelerating components? ESS AD Technical Note, ESS/AD/0031, 2012
- Conference reports in JACOW, keywords: machine protection, beam loss