Title
LHC Commissioning Working Group:
Overview of foreseen Feedbacks
and implications for commissioning
Ralph J. Steinhagen
Accelerators & Beams Department, CERN
and 3rd Physics Institute, RWTH Aachen
with input from:
J. Wenninger, R. Jones and others

---
Will cover ...
Summary of requirements and expected dynamic perturbations
Feedback architecture and 'test-bed'
Some comments on getting them going
Disclaimer:
Already covered in earlier meetings:
  - Beam Instrumentation and their commissioning → R. Jones, recent LHCCWG talk
  - Corrector circuits and optics: polarities, mapping, rough calibration, ...
Will evolve most issues around orbit feedback system
  - largest multi-input-multi-output system, largest complexity
  - issues are similar for other FBs

---
Preliminary Remark:
Traditional requirements on beam stability (in particular orbit)...
... to keep the beam in the pipe!
LHC: Requirements/time-line of key beam parameters control depend on:
  1. Capability to control level/ tolerances of particle losses in the machine
    - Machine protection & Collimation
    - Quench prevention
  1. Commissioning and operational efficiency

---
Requirements on Orbit I/II
Example: Collimation System, Phase I: 43x43 → Nmax≈ 5∙1012 protons/beam
  - required collimation inefficiency1,2:
  - Min. accept. lifetime:	Τmin ≈ 10 min.
  - Dilution length:	Ldil ≈ 50 m
  - Quench level (@7 TeV) Rq:	Rq ≈ 7.6∙106 prot./m/s
  - → η < 0.05 (≈ single stage system)
Orbit stability of < 1 σ seem to be sufficient for ≤ 43 bunches
Nominal: ≈ 0.3 σ locally (collimation) and ~ 0.3 σ globally
%eta = {%tau_{min} cdot R_q cdot L_{dil.}} over N_{max}
Stage I
nominal
1 R. Assmann, “Collimation and Cleaning: Could this limit the LHC Performance?”, Chamonix XII, 2003
2 S. Redaelli, “LHC aperture and commissioning of the Collimation System”, Chamonix XIV, 2005
Coll. system
version ~ 2002
Collimation inefficiency vs. orbit error1
courtesy R. Assmann
peak-to-peak orbit error [σ]

---
Requirements on Orbit I/II: machine protection
Combined failure1: Local orbit bump and collimation efficiency (/kicker failure):
To guarantee (two stage) cleaning efficiency/machine protection:
  - TCP (TCS) defines the global primary (secondary) aperture
The orbit is not a “play-parameter” for operation, except at low intensity. (‘Playing’ with the orbit will result in quasi-immediate quench at high intensity.)
  - → Bumps may potentially compromise collimation function
  - machine protection proposal1: regularly check aperture → see link
e.g 'bump in arc'
IR2
IR3
Potentially:
< 6.7s
Na [σ]
~7.5σ
secondary halo
6.7s
5.7s
closed orbit
TCP & TCS
MKI
TDI
1 R. Steinhagen, “Closed Orbit and Protection”, MPWG #53, 2005-12-16

---
Nominal Requirements on Orbit
LHC cleaning System:	< 0.3 σ	IR3,IR7
Machine protection & Absorbers:
  - TCDQ (prot. asynchronous beam dumps)	< 0.5 σ	IR6
  - Injection collimators & absorbers	~ 0.3 σ	IR2,IR8
  - Tertiary collimators for collisions	~ 0.2 σ	IR1,IR5
    - absolute numbers are in the range: ~100-200 μm
Inj. arc aperture w.r.t. prot. devices and coll.:	< 0.3-0.5 σ (??)	global (estimated arc aperture 7.5 σ vs. Sec. Coll. @ 6.7 σ)
Active systems :
  - Transverse damper, Q-meter, PLL BPM	~ 200 μm	IR4
  - Interlock BPM	~ 200 μm	IR6
Performance :
  - Collision points stability	minimize drifts	IR1,2,5,8
  - TOTEM/ATLAS Roman Pots	< 10 μm	IR1,IR5
  - Reduce perturbations from feed-downs	~ 0.5 σ	global
  - Maintain beam on clean surface (e-cloud)	~ 1 σ ??	global
... requirements are similar → distinction between local/global less obvious!

---
Requirements on Energy
Energy matching between of SPS → LHC
  - use horizontal orbit corrector magnets adjust LHC energy (easiest and cleanest!)
A priori not urgently required for low intensity beams, but
  - may keep capture losses below an acceptable limit
  - minimises abort gap population & feed-down of higher multipoles
  - → favourable once running with high intensity
Required1 initial momentum stability: Δp/p < 10-4 = nominal
  - Simplifies setup of nominal beam after commissioning pilot
alignl%DELTA Q = Q_{nat}^{,} cdot {{%DELTA p} over {p}} ~~~~~~ %mu(b_1) = 1 unit toward color blue {%DELTA Q approx -0.014}
1 E. Chapochnikova, private communications
2 E. Shaposhnikova, “Abort Gap Cleaning and the RF System”, Chamonix XII, 2003
3 T. Linnecar, “RF Capture and Synchronisation”, Chamonix XII, 2003

---
Requirements on Tune and Chromaticity
Tune spread ΔQ|av≈1.15∙10-2
  - fixed by available space in Q-diagram
  - Working assumption: (first order:	no non-linear effects, avoid 3rd and 4th order resonances)
      - δQ ≤ 0.015 → 0.003
      - (early commissioning → 43x43)
  - Nominal1,2: ΔQ ≤ 0.003 (inj.) δQ ≤ 0.001 (coll)
Chromaticity
  - SPS: Δp/p: 2.8∙10-4	(actual Δp/p given by SPS → LHC inj.)
  - → allowed max lin. chromaticity (5-6 σ, first order):
                - → Q'max ≈ 10 & Q' > 0 !
  - Nominal1,2: Q'max ≈ 2 ± 1
coll.
3rd
inj.
δQ
2∙ΔQ(6σ)
10th
7th
← 4th
11th
Q'_max prop {{%DELTA Q_{av}} over {%DELTA p/p}}
“Numbers are estimates, other more/less strict choices are of course possible – commissioning will clarify real requirements!”
1 S. Fartoukh, O. Brüning, “Field Quality Specification for the LHC Main Dipole Magnets”, LHC Project Report 501
2 S. Fartoukh, J.P. Koutchouk, “On the Measurement of the Tunes, [..] in LHC”, LHC-B-ES-0009, EDMS# 463763

---
Requirements on Coupling
Minimum distance Δ- between tunes given by coupling c_
  - LHC injection: Δ-=|qx-qy|=0.03, collision: Δ-=0.01
  - Closest tune approach → c-«0.03 and c-«0.01 respectively
Requirement for other feedbacks that rely on decoupled planes
Proposal for alternate higher tune split1: Δ-=0.1 (qx=0.285 ,qy=0.385)
1S. Fartoukh, “Commissioning tunes to bootstrap the LHC”, LCC #31, 2002-10-23
qx
qx
q2
q1
~|C-|

---
Requirements vs. Perturbations
Expected Dynamic Perturbations vs. Requirements
Expected dynamic perturbations*
  - For details, please see additional slides
Feedback priority list: Coupling/Tune → Chromaticity → Orbit → Energy
Feedback list of “what's easiest to commission”:
  - 1rd: Orbit	→ functional BPM system	→ OK
  - 1½: Energy	→ consequence of 100k turn acquisition	→ OK
  - 2nd: Coupling/Tune	→ functional Q-meter (-PLL)	→ Day I-N
  - 3rd: Chromaticity	→ functional Q-meter and Δf/f modulation	→ ??
Foresee time to commission feedbacks at an early stage
  - Most instruments are commissioned parasitically with first circulating beam
* numbers in brackets are 'worst case'

---
Parameter control, either through...
Feed-Forward: (FF)
  - Steer parameter using precise process model and disturbance prediction
Feedback: (FB)
  - Steering using rough process model and measurement of parameter
  - Two types: within-cycle (repetition Δt<<10 hours) or cycle-to-cycle (Δt>10 hours)
preferred choice!
From the steering point of view: → All control schemes possible
For the full block diagram → click here
Choice of Feedback vs. Feed-forward
depends on available robust beam parameter measurements
Feedback:
Δx → E
Process:
E → P
Energy, Orbit,
Q, Q', c- etc.
Σ
Reference
Monitor:
P → P'
P
P'
Δx
Σ
actual disturbance
+
-
+
+
Σ
+
Feed-Forward:
M → E
Model
+
Σ
predicted disturbance
+
+

---
No “black feedback magic”
Effects on orbit, Energy, Tune, Q' and C- can essentially cast into matrices:
  - similar for other parameters
  - their control consists essentially in inverting these matrices
Some potential complications:
  - Singularities = over/under-constraint matrices, noise, element failures, spurious BPM offsets, calibrations, ...
  - Time dependence of total control loop
  - Controls: How to receive, process, send data ...
%DELTA vec{x}(t) = underline R cdot vec%delta_{ss} ~with~ R_{ij} = {alignc sqrt{%beta_i %beta_j}} over {2 sin(%pi Q)} cdot cos(%DELTA %mu_{ij}-%pi Q)
matrix multiplication

---
O-Strategy
“One-Slide” Orbit Correction Strategy
Orbit Correction will consist of two steps (which may alternate repetitively):
  - Initial setup: “Find a good orbit” (mostly feedback “off”)
    - establish circulating beam
    - compensate for each fill recurring large perturbations:
      - static quadrupole misalignments, dipole field imperfections
      - ...
    - tune for optimal orbit
      - keep aperture limitation
      - rough jaw-orbit alignment in cleaning insertions
      - ...
    - → reference orbit
  - During fill: “Stabilise around the reference orbit” (feedback “on”):
    - correct for small and random perturbations Dx
      - environmental effects (ground-motion, girder expansion, ...)
      - compensate for residual decay & snapback, ramp, squeeze
    - optimise orbit stability at collimator jaws/roman pots.
back

---
Orbit Feedback I/III
LHC orbit feedback system
Small perturbations around the reference orbit will be continuously	compensated using beam-based alignment through a	central global orbit feedback with local constraints:
  - 1056 beam position monitors
    - BPM spacing: DmBPM≈45° (oversampling → robustness!)
    - Measure in both planes: > 2112 readings!
  - One Central Orbit Feedback Controller (OFC)
    - Gathers all BPM measurements, computes and sends currents through Ethernet to the PC-Gateways to move beam to its reference position:
      - high numerical and network load on controller front-end computer
      - a rough machine model is sufficient for steering (insensitive to noise and errors)
      - most flexible (especially when the correction scheme has to be changed quickly)
      - easier to commission and debug
  - 530 correction dipole magnets/plane (71% are of type MCBH/V)
    - Bandwidth (for small signals): fbw≈ 1-2 Hz (defines total feedback limit)
    - more than 3000 actively involved elements!
BPM/COD
crates
Ethernet
LHC
OFC

---
Orbit Feedback II/III
Common Feedback/Feed-forward Control Layout
LHC feedback control scheme implementation split into two sub-systems:
  - Service Unit: Interface to users/software control system
  - Orbit Feedback Controller: actual orbit/feedback logic
    - Simple streaming task for all feed-forwards/feedbacks:	(Monitor → Network )FB→ Data-processing → Network → PC-Gateways
    - Can run auto-triggered (no timing necessarily required)
    - Hardware and functional specifications already available
CMW
Database settings,
operation,other user
Service Unit
Ethernet UDP/IP
Ethernet UDP/IP
m x
n x
Monitor-Frontend
PC-Gateways
Monitor-Frontend
PC-Gateways
Monitor-Frontend
FB/FF Controller
PC-Gateways
...
...
beam instrument
multipole magnets
beam response
Surface
Tunnel

---
Orbit Feedback III/III
LHC orbit feedback system III/III
SVD* based global correction scheme in space-domain and	Proportional-Integral-Derivative (PID) controll (+ Smith Pred.) in time-domain
  - Uses pseudo-inverse orbit response matrix:
    - Orbit correction = simple matrix multiplication
  - Can easily eliminate near-singular solutions	(= solutions that may potentially drive the loop instable)
    - Uses all (selected) CODs with rather small correction strengths
    - Less sensitive to single BPM errors, BPM noise and COD failures1,2
  - intrinsically minimise uncertainties and unknown effects,	due to “integral” part of PID controller
    - Classic, well studied and understood controller
    - Does not require an accurate process model
    - Linearises non-linear systems
  - does not correct for dispersion orbit → minimises cross-talk with E-FB
→ see additional slides on SVD correction
→ All light sources go in this direction!
* SVD: G. Golub and C. Reinsch, “Handbook for automatic computation II, Linear Algebra”, Springer, NY, 1971
1 R. Steinhagen, “Can the LHC Orbit Feedback save the beam in case of a closed orbit dipole failure?”, MPWG #46, 2005-06-01
2 R. Steinhagen, “Closed Orbit and Protection”, MPWG #53, 2005-12-16

---
Feedback Robustness
Feedback Design Targets:
Feedback loops are designed to be robust against:
  - optics and calibration uncertainties (through using SVD)
    - “number of used eigenvalues” #λsvd controls robustness vs. precision
  - measurement noise and failing monitors:	→ see additional slides
    - very likely failure during operation
    - expect up 20% (worst case) and more dis-functional BPMs during operation with beam
  - Failure of orbit corrector circuits:	→ see additional slides
    - Present estimate: about one failure every 5 days during operation with beam
  - Failures and unavailability of controls infrastructure:
    - network, front-ends, timing etc.

---
Example: Sensitivity to beta-beat
Low sensitivity to optics uncertainties = high disturbance rejection:
  - LHC simulation: Inj. Optics B1&B2 corrected
Robust Control: OFB can cope with up to about 100% β-beat!
  - Available aperture and collimation inefficiency w.r.t. β-beat is clearly more an issue
#λsvd controls correction precision
{ 20 cdot log left lline {{orbit r.m.s. after} over {orbit r.m.s. before}} right rline_{ref} }
attenuation =

---
Virtue of PID Controller: Integral Action example
Machine imperfections (beta-beat, hysteresis....), calibration errors and offsets can be translated into a steady-state εss and scale error εscale:
%DELTA x(s) = R_i(s) cdot %delta_i ~ toward ~ %DELTA x(s) = R_i(s) cdot (color red %epsilon_{ss} + (1 + color red %epsilon_{scale}) cdot %delta_i)
error signal Δ =
integral feedback signal
1rst
2nd
nth
...
Uncertainties and scale error of beam response function affects rather the convergence speed (= feedback bandwidth) than achievable stability
A 4% error of the orbit transfer function has in first order a similar effect as 4% beta-beat on the quadrupole magnets.
Stability limit: BPM noise and external perturbations w.r.t. FB bandwidth
time
norm. parameter
Reference = 1
1-ε
actual parameter
Feed-Forward:
time
norm. parameter
Reference = 1
1-ε
actual parameter
Integral feedback:

---
TestBed
Orbit Feedback Controller – Test Bed
Test bed complementary to Feedback Controllers:
  - Simulates the open loop and orbit response of COD→BEAM→BPM
    - Decay/Snap-back, ramp, squeeze, ground motion simulations, ...
    - Keeps/can test real-time constraints up to 1 kHz
  - Same data delivery mechanism and timing as the front-ends
    - transparent for the FB controller
    - same code for real and simulated machine:
      - possible and meaningful “offline” debugging for the FB controller
Central Timing
generator
... t=20/40 ms Dt<1 ms
OFC Test Bed
covers whole ring (27 km)
  BI-Frontend
  PC-Gateways
Feedback Controller
CTR
CTR
CTR
CTR
buffer etc.
buffer etc.
PPC
c-alg.
PC-CO
DAB
DAB
18 BPM/crate
16 COD/gateway
70x
network
   50 x
   network
beam response

---
Commissioning of Feedbacks without Beam
Most feedbacks checks can be and are done during hardware commissioning:
  - Interfaces and communication from BI and to PO front-ends
  - Synchronisation of BPM acquisition	(using the BPM's 'calibration' mode)
  - Synchronisation of PO-Gateways	(using the provided 50 Hz status feedback channel)
  - Interfaces to databases
Using the 'test-bed' we can do the further tests without beam:
  - PID/Smith-Predictor functionality at nominal/ultimate feedback frequency
  - Test automated countermeasures against failing BPMs or CODs
  - other parts of the feedback architecture:	controls, non-beam-physics issues

---
Commissioning of Feedbacks with Beam
Things that have to and can only be checked with beam:
  - Beam instrumentation: polarities, planes, mapping
  - Corrector circuits: polarities, planes, mapping	(longitudinal and beam1/beam2)
  - Transfer function and rough test of calibrations
  - Circulating beam
  - Static coupling is under control
It is possible to run feedbacks already after above procedures:
  - e.g. auto-triggered at 0.1 – 1 Hz
  - low integral gain (Kp=Kd=0)
partially done
while threading
the first beam!

---
Requirements for nominal Feedback Performance
If we want to run at nominal feedback performance: Favourable to have
  - Beta-beat of about 20% or less
    - e.g. measurement of orbit response matrix:
      - excitation of all CODs and measuring the BPM response
        - not all CODs were necessarily used for threading (polarity checks)
      - requires about ~10 s per COD → 4h: one shift
      - intrinsically gives a coherent COD/BPM calibration
  - BPM vs. COD calibration within 20%
  - Total feedback loop delay and optimisation of PID gains
  - Test of automated feedback procedure for BPM intensity settings change
    - can be omitted, since it seems to be intended to always use low intensity bunches for operation up to 43x43 bunches
    - BBQ is insensitive to bunch/beam intensitiy

---
From threading the first pilot to 43x43 bunches
43x43 operation: max. intensity 4∙1010 protons/bunch
→ No gain-switching: BPMs will always operate at 'high' sensitivity
noise/error: ~ (nb)-1.5, half-aperture ≈ 22 mm
switch at: ~5.3·10-10 protons/bunch

---
Commissioning of Feedbacks: nominal performance
The possible parameter stability is essentially determined by:
  - feedback bandwidth
  - noise and stability of beam measurements
Example:
  - BPM orbit resolution: pilot Δxturn ≈ 200 μm → orbit: Δx ≈ 13-20 μm
  - BBQ (Q,Q' & C-): ΔQ ≈ ~10-4, avg. over 10 s
Actual stability depends on whether we (want to) steer to these limits
  - Filtering is of course possible (e.g. low integral gain Ki)
  - Robustness and availability of instruments is an issue
    - more pronounced for the BPMs
    - Q,Q',Coupling: essentially only one instrument per beam

---
Conclusions
Feedback architecture, strategies and algorithms are well established
  - Orbit FB: stability better than about 200 μm should not pose a problem
  - Tune FB: ΔQ<0.003 seems possible, if BBQ works
Biggest problem so far for LHC feedbacks:
  - Human resources to implement the FB controller, service unit, GUIs, ...
Commissioning of feedbacks:
  - Most of the requirements for a minimum workable feedback systems are already fulfilled after threading and establishing circulating beam.
  - Redo the optics measurements and calibration with higher accuracies for nominal performance.
Feedbacks are most useful when used at an early stage
  - RHIC: it is possible to commissioning a new ramp in one go
  - Possibility to use feedback signals as feed-forward for next cycles

---
Reserve Slides

---
Aperture Title
Aperture and Reference Orbit
How to determine the actual aperture?
or:
How do we now that we established a good/safe orbit?

---
Aperture e-blow-up
Aperture measurement proposals:
Two methods to test whether the closed orbit is within 6.7σ of the available mechanical or dynamic aperture:
Scan using emittance blow-up:
  - Increase beam size in a controlled	way while measuring the beam size.	(e.g. using transverse damper and wire scanner)
  - Once particle loss above given threshold:
    - → store last beam size measurement
  - “Is beam size ≥ 6.7 s0 ?” (s0: beam size at injection)
    - Yes:	→ mechanical aperture ≥ 6.7 s → orbit is safe
    - No:	→ mechanical aperture ≤ 6.7 s → orbit is un-safe
      - rework orbit reference (compare with old reference....)
%sigma(s)=sqrt{%varepsilon %beta(s)}
ε0→
72∙ε
aperture
particle loss
→stop ε blow-up
beam@inj
blown-up beam
Orbit
offset

---
Aperture COD
Scan of mechanical/dynamic aperture
Scan using two COD magnets (currents: I1 & I2) with p phase advance:
  - Scan Imax/φ:
    - φ = 0→2π (takes ~25 second @ 7σ, due to COD power converter speed)
  - Increase amplitude (COD currents) till orbit shift corresponds to 6.7σ
  - Loss does not exceed predefined BLM threshold if COD settings@ 6.7σ:
    - Yes:	→ mechanical aperture ≥ 6.7 s → orbit is safe
    - No:	→ mechanical aperture ≤ 6.7 s → orbit is un-safe
  - additional feature: compare measured with reference BPM step response (xco= 0-3σ)
    - → rough optics check (phase advance and beta-functions)
aperture
φ = 0 → 2π
I1=Imax∙sin(φ)
Imax
φ
ideal orbit
I2=Imax∙cos(φ)
x/√β [σ]
Amp.: 3σ→7σ

---
Aperture Procedure I
Mechanical Aperture Scan through...
Controlled emittance blow-up:
may check both planes at the same time
relatively fast measurement
reliability/robustness of beam size measurement/blow-up is an issue
no information on injection optics
tests only one phase
Tests rather dynamic than mechanical aperture if adyn < amech
Destructive measurement
  - beam has to be dumped after scan
  - cannot be used for collimator setup
  - increased beam loss during extraction
Betatron oscillation scan:
non-destructive measurement	(could be done to check during each injection)
rough information on injection optic
Independent information on planes
checks only one plane at a time
What to do if on COD is down?
  - spares: longer measurement
requires ~30 s for a scan at 7s
Required:
  - inhibit injection during scan
  - COD setting reset after scan
Both methods:
  - Determine the available aperture
  - should be performed with low-intensity beams
  - need time and exclusive control of the machine
in order to minimise the need for too frequent aperture scans:
  - → perform above checks only when exceed given window

---
Aperture Procedure II
Indicators whether Aperture Scan is required:
Beam Position Monitors:
Procedure:
  - A: Initial check whether Orbit is safe:
    - aperture scan (ε blow-up, betatron-oscillation)
      - Potential bump scans to determine location of aperture
    - save “safe BPM reference” current settings → xref = “SAFE SETTING”
  - B: Check:	if ( |xmeas.- xref| < Δxtol) {...}
    - FALSE: potential orbit bump detected
    - TRUE: Orbit is safe
  - Pro's:
    - Easy to check with circulating beam
    - Less dependent on machine optics
    - Sensitive to most orbit manipulations
  - Con's:
    - erroneous BPMs
    - No information before injection
    - Bunch intensity systematics (gain settings) and change of BPM calibration
    - Potential cross-talk with orbit feedback
no
yes

---
Aperture Procedure III
Magnet Current Surveillance I/II
Iref(..)=Imeas.(..)
yes: Orbit Safe
no: perform aperture scan
Aperture scan:
→ Orbit safe!
Save COD reference
settings Iref(..)
[...]
Proposed Procedure:
  - A: Initial check whether Orbit is safe:
    - aperture scan (ε blow-up, betatron-oscillation)
      - Potential bump scans to determine location of aperture
    - Save “safe COD reference” current settings → Iref(...) = “SAFE SETTING”
  - B: Each cycle:
    - Compare with actual current reference Imeas(..):
if (|Imeas(..) - Iref(...)| < ΔItolerances) {...}
      - FALSE:	Orbit may contain potential bumps	→ State A
      - TRUE:	Orbit can be considered to be safe → State B
no
yes
time

---
Aperture Procedure IV
Magnet Current Surveillance II/II
Current Surveillance:
  - Pro's
    - Can be used to check even before first injection
    - Can run continuously with orbit feedback in operation
  - Con's
    - Less sensitive to complicated orbit bumps
    - No precise&simple 'ΔI → Δx' transfer function available
      - depends on machine optic, energy
      - CODs create not only bumps but compensate
        - ground motion,
        - decay & snap-back,
        - multipole field errors,
        - squeeze induced effects, ...
→ Current tolerance level ΔItolerances (“SAFE SETTINGS”) should include margin for
  - orbit feedback operation
  - expected compensation of closed orbit uncertainties = “natural effects”

---
Beam Perturbations Overview
Expected Perturbations of
Orbit, Energy, Tune, Chromaticity, Coupling

---
Perturbation Overview
Perturbation Prediction of Orbit, E, Q, Q', C-, ....
...can be grouped into:
  - Environmental sources:	(mostly propagated through quadrupoles and their girders)
    - correlated and random ground motion, tides,
    - temperature and pressure changes,
    - cultural noise (human activity), and other effects.
  - Machine inherent sources:
    - decay and snap-back of the main dipoles' multipoles,
    - eddy currents in the magnet and on the vacuum chamber,
    - flow of cooling liquids, vibrations of the ventilation system,
    - changes of the final focus optics
  - Machine element failures:
    - particularly orbit correction dipole magnets	(most other magnets are interlocked and inevitably lead to beam dump)
    - → summary

---
Environmental sources
Environmental Sources
Perturbations due to
correlated and random ground motion, tides
and thermal expansion of girders

---
Ground 1
Correlated vs. Random Ground Motion I/II
Two classes of ground motion (see CERN-AB-2005-087):
Correlated ground motion waves: 'Cultural Noise', ocean swelling, tidal waves, ...
  - Assuming visibility threshold of 1 μm and κ≈1000	→ coherent ground motion negligible above 1 Hz (beware of cryogenics!)
%sigma_{beam} left[ %mu m right]= %kappa(f) cdot %sigma_{ground} left[ %mu m right]

---
Ground 2
Correlated vs. Random Ground Motion II/II
Random ground motion (Brownian motion):
  - amplitudes increases with ~√t
    - LEP and SPS based measurements:
  - Propagation of random ground motion onto orbit r.m.s. σbeam:
    - LHC injection optics:
κH=30.5±11.5 and κV=29.6±9.0
    - LHC collision optics:
κH=63.3±32.5 and κV=62.1±25.5
color blue { %sigma_{ground}[%mu m] approx 5-6 cdot 10^{-2} left[{%mu m} over {sqrt{s}} right] cdot sqrt{t} }
%sigma_{beam} left[ %mu m right]= %kappa cdot %sigma_{ground} left[ %mu m right]

---
Ground 3
“Analysis of Ground Motion at SPS and LEP,
Implications for the LHC”, AB Report CERN-AB-2005-087
prediction based on LEP and SPS orbit data
R. Pitthan, “LEP Vertical Tunnel Movements -
Lessons for Future Colliders”, CLIC-Note 422
→ closed Orbit drifts after 10 hours ≈ 0.3 -0.5 σ

---
Ground 4
Lunar and Solar Tides
Moon/sun tides change the geometric circumference of the machine:
  - well tested at LEP	→ J. Wenninger: CERN-SL-99-025-OP
  - LHC: ΔC ≈ ± 0.5 mm, momentum compaction factor αp= 3.2∙10-4
    - Δp/p ≈ 5.8∙10-5 → 2Δx = 2∙Dmax∙Δp/p∙ = 326 μm ≈ 0.29 σ
{%DELTA p} over {p} = - {1 over %alpha_p} cdot {{%DELTA C} over C}

---
Solar/Lunar Tides prediction for 2007
Algorithm courtesy J. Wenninger
Dx:= 2 m

---
Tides
Solar/Lunar Tides prediction for June 2007
Dx:= 2 m

---
Thermal Expansion of Girders
23 ± 6 °C
18 ± 1 °C
18 ± 1 °C
23 ± 6 °C
23 ± 6 °C
18 ± 1 °C
18 ± 1 °C
23 ± 6 °C

---
Thermal Expansion of Girders
Mechanism: Orbit feedback intrinsically aligns with respect to the BPMs that are either attached to the quadrupoles or have similar girders
Thermal expansion, steel αsteel≈ 10-17∙10-6 K-1 (BS:970, DIN18800):
Systematic shift of beam reference system with respect to non-moving external reference (e.g. potentially collimators):
  - Cryo-Magnets:	x0 ≥ (340 ± 20) mm	→ Δx ≈ 3.4 - 5.8 μm/°C
  - Warm equipment:	x0 ≈ 950 mm	→ Δx ≈ 9.5 – 16 μm/°C
The inlet temperature is stabilised to about ±1°C
  - temperature changes shouldn't pose a problem for even IRs
%DELTA x = x_0 cdot %alpha cdot %DELTA T

---
Thermal Expansion of Girders
However, temperature variations in odd IRs might be larger due to different thermal loads in neighbouring arcs.
Special case: Collimation in IR7
Closed air circulation in IR7: T estimate as high as 35°C
Already ΔT = ± 2°C → Δx ≈ ± 20 μm, Collimation: ± 50 μm might be tolerable	(TOTEM 10 μm requirements – a midnight summer dream?)
CNGS/Ti8: Estimates where ≈ 10°C off (measured 25°C vs. estimated 35°C)
Wait for LHC commissioning with beam and real temperature experience
beta-collimation IR7
ventilation
door
regular air circulation
ventilation
door
regular air circulation
BPM
BPM
BPM
BPM
TCP.X6L7.B1
BPM
BPM

---
Machine inherent sources
Machine Inherent Sources
Perturbations due to Multipole Field Errors of
main dipoles and quadrupoles

---
Expected Dynamic Perturbations
Current decay in main bends1,2 (b1 & b3) and lattice quadrupoles (b2):
  - ...LHC injection optics (v6.5, MAD-X)
    - Orbit (H/V):	Δx ≈ (0.68±0.23) mm/unit ∙Δb1(R) →	Δx(y) ~ 0.44 ± 0.17 σ
    - Energy:	Δp/p ≈ 10-4 ∙Δb1(S)	→	Δp/p ~ 0.78∙10-4
    - Tune:	ΔQx(y) ≈ Q'nat∙10-4 ∙Δb1(S)	→	ΔQ ~ -0.011
    - Tune(MQ):	ΔQx(y) ≈ 80∙10-4 ∙Δb2(S)	→	ΔQ ~ 0.014
    - Chromaticity:	ΔQ'x(y) ≈ 44(-39) ∙Δb3(S)	→	ΔQ' ~ 62 – 70
    - Coupling	Δc_ ≈ 0.46 ∙Δa2(S)	→	Δc_ ~ 0.005
    - Coupling	Δc_ ≈ 0.014 ∙Δa2(R)	→	Δc_ ~ 0.003
  - + feed-downs due to orbit ... depends on operational conditions
    - Coupling4	Δc_ ≈ 0.1 (worst case)
Machine intrinsic effects: Squeeze (raw uncorrected orbit drift ~ 30 mm)
Environmental sources & machine element failures (ground motion, girder, cryogenics, ...)
snapback:
1L. Bottura, “Cold Test Results: Field Aspects”, Proceedings of Chamonix XII, 2003
2L. Bottura, “Superconducting Magnets on Day I”, Proceedings of Chamonix XI, 2001
4S. Fartoukh, “Commissioning tunes to bootstrap the LHC”, LCC #31, 2002-10-23

---
Expected Time-Scales of Perturbations
Orbit & Energy:
  - Injection (ground-motion, Δb1):	~ 0.4 σ/10 h	→ Control @1 Hz sufficient
  - Snap-back:	0.3 σ/100 s	→ Control @1-10 Hz ??
  - β*-Squeeze:	0.1 σ/s	→ Control @10++ Hz OK
Tune & Chromaticity (Snapback: MQ's b2 and MB's b3 resp.; a2 similar):
  - (ΔQ'/Δt)max < 1.3 units/s & (ΔQ')max < ~ 10 units
    - → (measure &) control chromaticity every ≈ 10 seconds (or faster)
Decay: b2|max = 1.68 units
Decay: b3|max = 1.64 units

---
Orbit Transient due to Squeeze
Mechanism: Off-centre beam in quadrupoles with varing focusing strength (e.g. due to crossing angle, quadrupole misalignments, ...)
Assume Δx=0.5 mm r.m.s. random quadrupole and BPM misalignment	(= hopefully, this is the worst case scenario for LHC!)
  - Survey group targets:
    - 0.2 mm r.m.s. globally
    - 0.1 mm r.m.s. as an average over 10 neighbouring magnets.
  - Feed-down are linear: Results can easily be scaled down to your favourable alignment assumption
Without k-modulation: BPM offsets w.r.t. quadrupole are unknown
Transient is an issue w.r.t. beam stability and available current rate limit (0.5 A/s)
→ Likely/hopefully 'preaching to the choir': We should spend some time and tune the orbit inside IR1 and IR2 before squeezing the first time.
alignl %delta_{kick} = (k+ %DELTA k_{squeeze})l_{mag}cdot %DELTA x_{quad.-misalign.}

---
Transient due to low beta Squeeze: Overview LHC

---
Transient in Collimation insertion vs. squeeze step
β* = 17	→ 9 m	and
β* = 1.5	→ 1.1 m
will be toughest for keeping orbit collimation requirements
(will be further mitigated by PID)

---
Dynamic Perturbations vs. Requirements Summary
1: J. Wenninger: “Observation of Radial Ring Deformation using Closed Orbits at LEP”
2: RST, “Analysis of Ground Motion at SPS and LEP, implications for the LHC”, CERN-AB-2005-087
3: M. Haverkamp, “Decay and Snapback in Superconducting Accelerator Magnets”, CERN-THESIS-2003-030
    L. Bottura, “Cold Test Results: Field Aspects”, Proceedings of Chamonix XII
    L. Bottura, “Superconducting Magnets on Day 1”, Proceedings of Chamonix XI
   FQWG-Homepage: http://fqwg.web.cern.ch/fqwg/

---
COD failure
Machine Element Failures
Perturbations due to
failing orbit corrector magnets
(other failures are issue to MP and in most cases result in an immediate beam dump)

---
General Parameters
Main MCB Circuit Parameter
Total 1060 orbit corrector dipole (COD) magnets in the LHC.
Focus on 752 MCBH(V) magnets since they have the same design, parameter and powering: (other: insertion CODs (triplets..), warm, different powering ...)
  - Part of arc SSS: half-cells 11R'x' ≤ locationMCB ≤ half-cell 11L'x+1'
  - Individually powered by a ±8V, ±60A converter, rate limit: 0.5 A/s
  - inductance L: 5.92 H @ 1kHz resp. 5.48 H @ 120 Hz	(measured: LHC-MSCB-FR-0001, courtesy Mikko Karpinnen)
  - resistance R: 64.5 ... 91.3 mW	(including intrinsic magnet, cable and current lead resistance)
Maximum kick dmax (↔55 A) on beam:	1260 mrad @ 450 GeV	81 mrad @ 7 TeV
Maximum kick amplitude : 144 mm @ 450 GeV and 9 mm @ 7 TeV)

---
Optics Parameter
MCB Optics Parameter
Arc lattice is similar for injection and collision optics. Maximum orbit response in arc (b = 170 m)
  - DxBPM ≈ 100-110 mm/mrad · dCOD
  - resulting orbit change:	~ 1.2 mm/0.5 A @ 450 GeV	~ 75 mm /0.5 A @ 7 TeV
expected average/max kick:	8/30 mrad	(compensation of random 0.4 mm r.m.s. quadrupole misalignment)
  - Corresponding current in COD circuit:
    - ~ 0.4 / 1.3 A @ 450 Gev
    - ~ 5.5 / 20 A @ 7 TeV
one COD failure corresponds to an average/max orbit change of (b = 170 m)
~ 0.9 / 2.9 mm per COD failure
  - breaks collimation tolerances by order of magnitude!
  - Online compensation is favourable in order to increase the beam availability but not required for protection!

---
MCBH/V quench
Case I: quenching MCBH/V, current decay
100%
1/e
data courtesy to Felix Rodriguez Mateos
very fast current decay:
decay time: t ~ 0.35 s	↔	DI/Dt ~ 16 (58) A/s @ 7 TeV
after 1 s the current is practically 0 A
MCB quenches are expected to be rare
~ 350 ms

---
MTBF estimate
Case II: 60A/8V Power Converter MTBF
There are 19 documented and in db logged causes for PC failure
Mean-Time-Between-Failures (MTBF) expected to be ≈ 105 hours
  - Probability that one of the 752 MCB PC fails during a 10 hour run:
  - Expect one PC/COD failure in 14 cycles ≈ once per week	(including all CODs: one failure every ~ 10 cycles)
  - Circuit discharges with a decay time: t ~ 60-80 s
  - This likely leads to an beam dump request due to:
    - increased particle losses e.g. at the collimator.
    - beam position interlock.
Beware: actual operational experience may show higher/lower MTBF
{ P_{failure}/h = 10^{-5} {failures}over {hour} ~ dlrarrow ~ {overline P}_{failure}/h = 1-10^{-5} {overline failures} over {hour} }
{P_{failure/10 h} = 1- left( left( {overline P}_{failure} right)^{752} right)^{10} approx 7 percent}

---
BPM failures
Identification and Compensation of
bogus and failing Beam Position Monitors

---
Anticipated BPM Failures/Noise/Systematics
LHC BPM Prototype in the SPS:
Most common: acquisition failure = no orbit info available and spikes
  - Short term (few ms-s): Zero Order Holder (ZOH)
  - Long term: Disable BPM in feedback and recalculate SVD pseudo-inverse matrix
Only a few drifts observed: systematic on bunch length & bunch intensity
    - within 1% of BPM half aperture ↔ 250 μm (complies with specification)
LHC BPM test in 2004
with coasting beam in the SPS:
spikes:
few μm to many mm
acquisition failures → orbit = “0”

---
Orbit Feedback Robustness against
BPM Failures/Errors
BPM phase advance of ~π/4:
  - Twice the sampling than minimum required to detect β-oscillation
  - Distribution of consecutive BPMs on different front-ends (minimise impact of front-end drop outs)
Detection of erroneous BPM failures (SPS: mostly spikes)	(xi(n)=position at ith monitor, n: sampling index; σorbit= residual orbit r.m.s.)
  - Reject BPM if the following applies:
    - Cuts in Space Domain:
      - (BPMs marked by the front-end itself)
      - xi(n) > machine aperture
      - xi(n) – xi,ref > 3∙σorbit
      - Option: interpolate position from neighbouring BPMs (implemented in APS)	→ sensitive to quadrupoles/dipoles between BPMs,
    - Cuts in Time Domain (Spike detection!):
      - Δxi(n)=xi(n)-xi(n-1) > 3∙Δxrms(n→n-m) (dynamic r.m.s. of last 'm' samples)
      - filters to reduce noise (e.g. low integrator gain)
      - re-enable BPMs with new reference if dynamic r.m.s. is stable for n seconds
      - ...
  - Difficult to detect coherent, very slow or systematic drifts	(e.g drift of BPM electronics vs. systematic ground motion, temperature drifts ... etc.)
Use SVD based correction → less sensitive to BPM errors

---
SVD Robustness: Properties
Global orbit feedback with local constraints
  - Based on SVD algorithm → see attachment for details
  - Expands orbit using orthogonal “eigen-orbits”
Important mathematical properties:
    - SVD minimises orbit & deflection strengths
    - Uses rather many CODs with small than few with large kicks
    - Solutions are sorted by their 'effectiveness': large eigenvalues λi (solutions) first
    - Local 'bump-like' solutions corresponds to small eigenvalues
  - “number of used eigenvalues” #λsvd controls OFB robustness vs. precision
    - more #eigenvalues → more precise correction (collimation requirement)
    - less #eigenvalues → more robustness against BPM & optic failures
  - discard deliberately solutions with small eigenvalues (=local bumps)	→ SVD cannot generate (= correct) those bumps
  - However: Will use all (local SVD) eigenvalues regions like collimation.	(due to precision requirement)

---
Robustness Examples
kick1
kick3
E.g. simplest Three-Corrector-Bump is sampled with at least three BPMs
  - erroneous or noisy BPM has less effect on total correction
trajectory
kick2
Example: Single BPM spike
perfect orbit (=0)
BPM.33L4.B2 with spurious offset
SVD corrects the spurious offset (ridge in surface plot), if a large number of eigenvalues #λsvd is used for the orbit correction
e.g. #λsvd = 100 → spurious offset propagates to 16 % to the orbit

---
Feedback Sensitivity to BPM Failure
Propagation of single (arc) BPM failure with xi(n) < 3∙σorbit < σbeam
  - #λ≈250: < 40% (β ≈ 175m) resp. < 10% (β ≈ 39 m)
Propagation of random (white) noise on all BPMs
  - 30% (worst case #λ=529) resp. 10% (OFB operation with #λ≈250)
BPM induced noise on orbit (single bunch):
  - Single BPM failure:	< 0.01 - 0.4 σ
  - White BPM noise:	< 0.001 σ (inj) resp. 0.02 σ (coll)
ridge due to spurious single BPM offset
see previous slide
simulation, N=105 orbits
← Trade-off required! →
more precise corrections
more prone to BPM errors

---
COD Failure Backup Scenario
Compensation of
failing Closed Orbit Dipole Magnets

---
COD Failure Backup II-1
COD/PC failure: Backup Scenario I/IV
What will the feedback do in case of a fast COD drop-out?
The effect of the failing COD can for sufficiently long (spacial) distances be compensated and replaced through a pattern of correctors:
  - Though a minimum two correctors are required, it is favourable to spread replacement pattern over more CODs (e.g. use intrinsic SVD property):
    - smaller maximum currents in the pattern
      - avoid hitting individual COD's maximum current
      - single COD failure becomes less critical
      - faster reaction time since max DI/Dt = n · 0.5 A/s	(total speed determined by time required to reach pattern's largest current)
failing COD betatron oscillation
replacement betatron oscillation
failing COD
replacements
affected
region

---
COD Failure Backup II-2
COD/PC failure: Backup Scenario II/IV
What can the feedback do in case of a fast COD drop-out?
Controller procedure:
  - If detected: Send the pre-calculated replacement pattern instead of the failing COD's DI(t) through the feed-forward path :
    - Procedure for the first few (milli-) seconds:
      - Mark COD
      - Temporarily disable BPMs (ZOH) in the adjoining region	(in order to be insensitive to the spacial transient)
      - Continue normal correction
      - Replace bogus DI(t) with R-pattern	only intermediate region affected
    - In parallel:
      - compute new inverse SVD matrix without bogus COD (~ 15s/COD)
      - Swap active matrix once finished recalculation
      - recalculate new anticipatory R-patterns (~ 2 hours/all CODs)
The feed-forward action is transparent for large spacial distances
The effectiveness depends on the notify- and feedback-delay.

---
COD Failure Backup II-3
COD/PC failure: Backup Scenario III/IV
Example: COD MCBV.30R5 failure and compensation (LHC collision optics)	plotted: number of used eigenvalues vs. monitor index and residual orbit shift (colour coded: Blue=OK, Red=large transient):
since number of used eigenvalues and loop stability does not affect the feed-forward one may choose a large number of eigenvalues
  - Apart from transient, cleaning insertion is not affected by failing COD.
IR1
IR2
IR3
IR4
IR5
IR6
IR7
IR8
IR1
cleaning
unaffected
cleaning
unaffected
affected
region

---
Backup II-4
Backup Scenario II – low number of eigenvalues help
For small #λSVD the correction is less sensitive to failing or not-reacting CODs
Plotted: damping with (bold red) and without (bold green) detected COD failure vs. number of used eigenvalues. (damping: ratio between un- to corrected orbit)
moderate damping without detected failure slows the orbit transient due to the missing deflection.

---
COD Failure Backup II-4
COD/PC failure: Backup Scenario IV/IV
It is important that the delay tnotify till the OFC is notified is short and constant.
ripple < 10-3 if tnotify~0.1
The length of tnotify determines the ripple : ~ '1-exp(-tnotify/t)'
1 Hz would be OK but will reuse already present 50Hz status feedback channel provided by the power converter gateways (S. Page, AB/PO)

---
Orbit Correction SVD
Automated Orbit Correction
using Singular Value Decomposition

---
Orbit Response Matrix
Space Domain: Orbit Response Matrix
The orbit is sampled at m discrete not necessarily
equidistant locations in the machine:
orbit response matrix example of a regular
FODO lattice:
Dxi+1
Dxi
Dxi+2
dj
dj+1
dj+2
The superimposed beam position shift at the ith monitor due to single dipole kicks is described through the orbit response matrix R. It can be written as
color black{ alignl ~~~~%DELTA x_{i} = sum csup{n} R_{ij} cdot %delta_j ~with~ R_{ij} = {alignc sqrt{%beta_i %beta_j}} over {2 sin(%pi Q)} cdot cos(%DELTA %mu_{ij}-%pi Q) } newline color black { alignl dlrarrow{}~ %DELTA vec x = sum from {j=0} to {n} %delta_j {vec u}_j ~with~ {vec u}_j = (R_{1j}, dotslow , R_{mj})^{T} dlrarrow{}~ %DELTA vec{x}(t) = underline R cdot vec%delta_{ss} }
where (b,m,Q) depends on the machine optic (example: Q=4.31).

---
O-Key-Eq
Space Domain:
Task in space domain:
Solve linear equation system and/or find (pseudo-) inverse matrix R-1
Singular Value Decomposition (SVD) is the preferred orbit feedback workhorse:
standard and proven eigenvalue approach
insensitive to COD/BPM faults and their configuration (e.g. spacing)
minimises orbit deviations and COD strengths
numerical robust:
  - guaranteed solution even if orbit response matrix is (nearly) singular	(e.g. two CODs have similar orbit response ↔ two rows are (nearly) the same)
  - easy to identify and eliminate singular solutions
high complexity:
  - Gauss(MICADO):	O= ½ mn2 + 1/6 n3
  - SVD:	O= 2mn2+4n3
  - m=n: SVD is 9 times more expensive, even on high-end CPUs full initial decomposition may take several seconds (LHC: ~15 s/plane), but once decomposed and inverted: simple matrix multiplication (O(n2) complexity, LHC: ~15ms!)
color black { {left ldline {vec x}_{ref} - {vec x}_{actual} right rdline}_2 = {left ldline underline R cdot {vec %delta_{ss}} right rdline}_2 < %epsilon ~ rightarrow~ vec %delta_{ss} = {tilde R}^{-1} %DELTA vec{x} }

---
SVD on a slide
Singular Value Decomposition (SVD) on a slide
Theorem from linear algebra*: “It is always possible to decompose a orbit response (real) matrix into a set of orthonormal BPM and COD eigenvectors”
eigen-vector relation:
color black {alignl %lambda_i {vec u}_i = {underline R} cdot {vec v}_i} newline color black {alignl %lambda_i {vec v}_i = {underline R}^T cdot {vec u}_i}
color white { dlrarrow }
final correction is a simple matrix multiplication
large eigenvalues ↔ bumps with small COD strengths but large effect on orbit
Easy removal of singular (=undesired, large corrector strengths) eigen-values/solutions:
  - near singular eigen-solutions have li~0 or li=0
  - to remove those solution: lim li→∞ 1/li =0
discarded eigenvalues corresponds to bumps that won't be corrected by the fb
color black{ vec %delta_{ss} = {tilde R} ^{-1} cdot %DELTA {vec x} ~ with ~ {tilde R} ^{-1} = underline V cdot {underline %lambda}^{-1} cdot {underline U}^T ~~ dlrarrow ~~ vec %delta_{ss} = sum from{i=0} to{n} {{a_i} over {%lambda_i} {vec v}_i} ~ with ~ a_i= {vec u}_i^T %DELTA {vec x} }
*G. Golub and C. Reinsch, “Handbook for automatic computation II, Linear Algebra”, Springer, NY, 1971
color white {{underline U}^T underline U = underline 1} color white {underline %lambda = diag(%lambda_1 , .. , %lambda_n) } newline color white {%lambda_1 > %lambda_2 > dotslow > %lambda_n} color white {underline R in setR ^{m times n}} color white {{underline V}^T underline V = underline V {underline V}^T = underline 1 }
U
V
=
T
x
R
x
l
response matrix
BPM eigenvectors
eigenvalues
COD eigenvectors
n x COD
m x BPM

---
SVD example: LHC eigenvalue spectrum
Eigenvalue spectra for vertical LHC response matrix using all BPM and COD:
near
singular
solutions
dominant eigenvalues
condition number ~ 106
-> indicator of numerical good matrix condition
(numerical precision (noise) of CPU is less an issue)

---
LHC example: BPM eigenvector #50 l50= 6.69•102

---
LHC example: BPM eigenvector #100 l100= 3.38•102

---
LHC example: BPM eigenvector #291 l291= 2.13•102

---
LHC example: BPM eigenvector #449 l449= 8.17•101

---
LHC example: BPM eigenvector #521 l521= 1.18•100

---
#Eigenvalues
Space Domain: Number of used eigenvalues?
Gretchen Frage: “How many eigenvalues should one use?”
high number of eigenvalues:	(still without using singular solutions)
more local type of correction
  - more precise
  - less leakage of local sources onto the ring
  - perturbations may be compensated at their location
good correction convergence
...
more prone to imperfections
  - calibration errors more dominant
  - instable for beta-beat > 70%
more prone to false BPM reading
  - Errors & faults
...
low number of eigenvalues:	(e.g. ~20% of total # e-values)
more global type of correction:
  - use arc BPM/COD to steer in crossing IRs
  - less sensitive to BPM noise
  - less sensitive to single BPM faults/errors
  - less sensitive to single COD/BPM faults/errors
robust wrt. machine imperfections:
  - beta-beat
  - calibration errors
easy to set up
...
poor correction convergence
leakage of local perturbations/errors
  - not fully closed bump affects all IRs
  - squeeze in IR1&IR5 affects cleaning IRs
...
orbit stability requirement
feedback stability requirement

---
Space Domain: local within global correction
The orbit and feedback stability requirements vary with respect to the location in the two LHC rings. In order to meet both requirements:
  - Implement robust global correction (low number of eigenvalues)
  - fine local correction where required (high number of eigenvalues or simple bumps):
    - Cleaning System in IR3 & IR7
    - Protection devices in IR6
    - TOTEM
Scheme I
Scheme II
Scheme for
machine development
no leakage
no leakage
no leakage
uncorrected
free orbit manipulation (within limits) while still globally correcting the orbit
coarse global SVD with
fine local “SVD patches”
(no leakage due to closed boundaries)
minor disadvantage: longer initial computation	(global + local SVD + merge vs one local SVD)
coarse global SVD with weighted monitors where required (w = 1 ... 10)
disadvantage:
total number of to be used eigenvalues less obvious
Matrix inversion may become instable
correct “MD” leakage
#l small
#l large
#l large
+
+
BPM·w
BPM·w

---
Miscellaneous Slides
ahead

---
Small remark on cross-talk between beams
Energy, Q, Q' and Coupling feedbacks are less affected by cross-talk:
  - Instrumentation and correctors act exclusively on either B1 or B2
Orbit steering using common elements in beam crossing insertions:
  - Optimisations for 'Beam 1' may have the opposite effect for 'Beam 2'
  - Only use common elements when acting on both circulating beams! (exception: one-beam operation)
Control procedure:
  1. Inject 'Beam 1', correct orbit without insertion CODs
  1. Inject 'Beam 2', correct orbit without insertion CODs
  1. Once having both beams circulating → enable CODs in common regions

---
Timing
Real-Time control requires upper limit on total loop delay
Two main strategies:
measurement of actual delay and its dynamic compensation in SP-branch:
  - high numerical complexity, branch transfer function has continuously to be modified
  - only feasible for small systems
Jitter compensation using a periodic external signal:
  - CERN wide synchronisation of events on sub ms scale that triggers:
    - BPM Acquisition, Reading of receive buffers, Processing and sending of data
    - time to apply in the power converter front-ends
  - The total jitter, the sum of all worst case delays, must stay within “budget”.
  - feedback loop frequency of 50 Hz feasible for LHC, if required...
Central Timing
generator
... t=20/40 ms Dt<1 ms
covers whole ring (27 km)
  BPM-Frontend
  PC-Gateways
Orbit Feedback Controller
CTR
CTR
CTR
CTR
buffer etc.
buffer etc.
PPC
c-alg.
PC-CO
DAB
DAB
18 BPM/crate
16 COD/gateway
70x
network
   50 x
   network

---
FB vs. FF: When is which applicable?
Border is rather fuzzy.... injection likely won't require RT-feedbacks
S. Sanfilippo (SM18 Review): “Decay of these magnets not scalable yet.”
  - b3 & b1 decay prediction:
random b3 → negligible effect
systematic b3 → seem to be reproducible
→ constant feed-forward function may be established at some point of time
random b1 → perturbs orbit
systematic b1 → Δp/p shift
→ both require feedback control for each fill

---
Feedback Loop
Example: LHC Orbit Feedback Loop
Full block diagram:
D(s): Standard Proportional Integral Derivative (PID) controller
  - Option: Non-linear PID gains based on actual orbit stability/noise
  - 'rescaling part': Counteracts clipping/saturation of CODs
Internal Smith-Predictor feedback loop:
  - favourable once running at 25/50 Hz
  - provides “cleaner” PID gains which are independent from sampling and other transport lags (simplifies further optimisations)

---
Smith-Predictor
What a Smith-Predictor compensates:
Classic Smith Predictor compensates only constant delays
induces an inhibitor signal to to delay the actuator signal by l
designed response
un-compensated response
compensated response