Bad Honnef talk Steinhagen
BBQ based tune PLL
Collimator impedance measurements in the SPS
Ralph J. Steinhagen
Acknowledgements:
A. Boccardi, T. Bohl, M. Gasior, R. Jones, K. Kasinski,
E. Métral, S. Redaelli, F. Roncarolo, B. Salvant,
F. Zimmermann and others

---
Overview
Brief description of measurement principle
  - Tune PLL studies at the SPS
Preliminary results of collimator impedance measurements:
  - Horizontal tune shift versus collimator jaw opening → Im(Zeff)
  - Vertical tune shift due to SPS machine impedance → Im(ZSPS)@270GeV
  - Instability rise-time due to collimator → Re(Zeff)
  - Instability rise-time due to SPS machine impedance → Re(ZSPS)
For more details on PLL design and architecture (USLARP TF review):
http://www.agsrhichome.bnl.gov/LARP/061024_TF_FDR/index.html

---
Basic Phase Locked Loop in two Slides I/II
A∙sin(2πfe)
reference signal
Phase
Detector
Low-pass
Filter
φ
Control Law
e.g. PID
NCO
Δf
beam response signal
A∙sin(2πfe)
R(fe)∙sin(2πfe+φ)
beam
pickup
kicker
(transverse damper)
(BPM+BBQ electronic)
NCO: Numerically Controlled Oscillator = digital sine wave generator
Aim of the PLL control law:
  - regulate the frequency in order to minimise Δφ (match to 90°)
  - first iteration choice: e.g. classic proportional-integral (PI) controller
beam response

---
Basic Phase Locked Loop in two Slides II/II
Phase Locked Loop Principle: shift of excitation frequency till Δφ = 0
N.B In addition to the tune, the beam response also depends on the chromaticity → affects the tune PLL tracking speed but not the resolution
amplitude response:
phase response:

---
21 September 2006: First successful BBQ based PLL
SPS 25ns fixed target beam: 26GeV → 450GeV, ~ 3e12 protons/beam
  - Horizontal tune: Qh≈ 26.76 → 26.66 (slow resonant extraction)
  - Fastest tracked tune change: ΔQ≈0.1 within about 200-300 ms
    - much faster than the maximum expected tune drift in the LHC!

---
Horizontal tune during ramp
phase error and non-vanishing amplitude indicate lock during ramp
tune trace
phase response
amplitude response

---
BBQ based Tune Tracking
Temporal evolution of the individual FFT acquisition:
Tune resolution:
  - FFT based (1024 turns):	ΔQres ≈ 10-3 - depends on Q'!
  - PLL based:	ΔQres «10-4-10-6 - independent on Q'!
    - limited by underlying tune stability → SPS is a tough testbed
    - excitation well below the 1 μm level (factor 10-600 below MultiQ Settings) → negligible emittance blow-up
  - Seem(ed) to be a very robust measurement!

---
Imaginary Part of Collimator Impedance:
Horizontal Tune versus Full Gap Opening I/II
Correlation between tune shift and collimator opening

---
Imaginary Part of Collimator Impedance:
Horizontal Tune versus Full Gap Opening II/II
nb =1.25·1011 protons
σt = 0.5 ns
jaw opening calibration pending
“Official” jaw opening calibration still pending!
Further optimisation: systematic tune shift and PLL intrinsics (delays)
N.B. classic tune shift measurement (FFT using BBQ) was limited by large Q'

---
“Free” measurement:
Vertical Tune Shifts due to SPS Impedance
Vertical tune shift are a result of:
  - SPS transverse impedance and changing bunch length/intensity

---
“Free” measurement:
SPS Impedance at 270 GeV
tune resolution:
ΔQres≈ 10-6...10-7 !!
Using Sacherer's impedance approximation: Zeff ≈ 21.54 MΩ/m

---
Real Part of Collimator Impedance:
Vertical Tune versus Full Gap Opening I/II
instability rise-time due to chromaticity change: Q' ≈ 22 → 1.1
Effect of the collimator on the beam instability rise-time is visible/evident
Detailed analysis of rise times including intensity normalisation pending	(B. Savant et al.)
with retracted collimator jaws
(SPS impedance)
jaw opening ≈ “4 mm”
horizontal plane
vertical plane
Plot courtesy K. Kasinski
Δt ≈ 1s
~ 4·104 turns
Δt ≈ 2s
~ 8·104 turns

---
Real Part of Collimator Impedance:
Vertical Tune versus Full Gap Opening II/II
Disclaimer:
Model calculations were performed assuming heaviside step functions of parameter change
However: the real machine does not reveal such sharp responses
  - change of Q' limited by sextupole circuit time constant
    - time-constants are amplitude dependent
    - particularly slow at 270 GeV
  - change of collimator gap is limited by maximum slew rate of ≈ 2 mm/s
→ The observed rise-times are a convolution of impedance, slew rate collimator jaw opening change - a detailed analysis should reflect this property.

---
MD Summary
Prototype tests of the BBQ based tune PLL were very successful!
Mutually exclusive modes of PLL operation:
  - either: track tune changes during the SPS ramp with ΔQ/Δt ≈ 0.1/s
  - or: achievable tune resolution ΔQres≈ 10-4 ... 10-6
Required PLL excitation was very low
  - factor 10 up to 600 times smaller than standard SPS MultiQ
  - measurements were done with a S/N ratio of less than 3..10dB
First “real world” test:
  - Measured real and imaginary part of collimator impedance
  - First results look promising but certainly require more detailed studies of systematics in particular “official” agreement on jaw opening calibration

---
reserve slides

---
Quick PI(D) Controller Gain HOWTO II/II
PLL low-pass:
Youla's affine parameterisation1 for stable plants:
Using the following ansatz
(1)+(2)+(3) yields:
α > τ...∞ moderates closed loop response between (trade-off):
  - fast and less accurate tracking vs. slow and more accurate tracking
G(s) = {K_0} over {%tau s + 1} ~~~ with ~~~ %tau approx 25 ms ( dlrarrow f=40Hz)
(1)
D(s)={Q(s)} over {1- Q(s)G(s)}
(2)
Q(s) = {color red {F_Q(s)}} G^i(s) = {color red {{1} over {%alpha s + 1}}} cdot {{%tau s + 1} over {K_0}}
(3)
D(s) = K_P + K_i 1 over s ~~~ with ~~~ K_p=K_0{%tau over {color red %alpha}} ~&~ K_i =K_0{ 1 over {color red %alpha}}
1D. C. Youla et al., “Modern Wiener-Hopf Design of Optimal Controllers”,	IEEE Trans. on Automatic Control,1976, vol. 21-1,pp. 3-13 & 319-338

---
Robust vs. Fast Tracking PLL
Similar to the other feedback designs: 1/α ~ effective PLL bandwidth
α facilitates the closed-loop trade-off:
  - fast and noise sensitive vs. slow and robust PLL loop

---
A more complete PLL schematic
phase detector +
low-pass filter
beam response
N.B. the phase reference includes correction for constant delays and BBQ filter systematics

---
Chromaticity and PLL Non-linearities
The first order PLL controller assumed a constant open-loop gain K0
Real open-loop response depends also on the actual phase and
Two observations:
K0 ~ const for |Δφ|≤ 60° (linear regime)
K0 depends on Q' (non-linear regime)

---
Q' measurement trough slow Δp/p modulation
Used PLL to track Q' (measurement during ramp)
Δp/p = 6·10-4
Q'~ 2-4
slow resonant
extraction
ramp start
SPS operation:	Δp/p > 10-3 & ΔQres≈10-3 → ΔQ'res ~ 1
LHC:	Δp/p < 10-4 & ΔQ'res ~ 1 → ΔQres < 10-4
  - tough, still not established!
Further tests with averaging over several tune measurement and slow underlying systematic Q,Q' changes