Bad Honnef talk Steinhagen
8th Workshop on Beam Diagnostics and Instrumentation for Particle Accelerators, DIPAC 2007, Venice, Italy
Feedbacks on Tune and Chromaticity
the essentials....
Ralph J. Steinhagen
Accelerator & Beams Department, CERN

---
Overview
Optimal Beam-Based Feedback Design
Tune & Chromaticity Measurements
  - Phase-Locked-Loop Systems
  - Cross-Dependability and Cross-Constraints between Feedback loops
  - What can break the PLL
Goal: provide roadmap to avoid less obvious pot holes

---
Beam Parameter Stability
Requirements on orbit stability:
  - Effective emittance preservation
  - Minimisation of coupling (orbit in sextupoles)
  - Minimisation of spurious dispersion (orbit in quadrupoles)
  - Collider Luminosity and collision point stability
→ Nearly all 3rd generation light-sources deploy	at least orbit/energy feedbacks
Hadron Colliders:
  - Traditionally: ... keep the beam in the pipe!
  - Present: Increased stored intensity and energy	→ quenches and/or serious damage
    1. Capability to control particle losses in the machine
      1. LHC: Δx|max ≤ 25 μm, Δp/p ≤ 5·10-5
    1. Commissioning and operational efficiency
LHC:
 50.0 mm
L.Farvacque, ESRF
36 mm
Beam 3 envel.
 ~ 1.8 mm @ 7 TeV

---
Requirements on Tune and Chromaticity
Lepton machines: δQ ~ 10-2 ... 10-3
  - some have tough working points, e.g.:
    - PEP-II: qx= 0.505 (LER), 0.503 (HER)
    - KEK-b: qx= 0.504 (LER), 0.510 (HER)
Hadron machines:
  - negligible synch. radiation damping
  - large tune footprints
  - avoid up to 12th order resonances
  - Example LHC: δQ ≤ 0.003...0.001
    - Space in Q-diagram: ΔQ|av≈1.15∙10-2
    - Allowed max lin. chromaticity14,15 (5-6 σ):	→ Q'max ≈ 2 ± 1 & Q' > 0
    - N.B.: Δp/p ≈10-5 → ΔQres≈10-5
Sources: supply drifts and ripples, hysteresis, ramp tracking errors, beam-beam, e-cloud, ...s.-con. accelerators: decay & snap-back, persistent currents
  - LHC: Chromaticity change ≈ 300 units, maximum rate ≈ 1.2 units/s
top energy
3rd
inj.
δQ
2∙ΔQ(6σ)
10th
7th
← 4th
11th
LHC

---
OFC Scheme
Orbit Feedback/Feed-Forward Control Scheme
Feedback controller usually decomposed into three stages:
  - Compute steady-state corrector settings based on	measured parameter shift that moves the beam	parameter to its reference in a steady state case
  - Compute a that will enhance the transition
  - Feed-forward: anticipate and add deflections to compensate	changes of well known or non-measurable effects:
space
domain
color black {{vec %delta}(t)}
color black {{vec %delta}(t = 0) rightarrow {vec %delta}_{ss}}
time
domain
color black {{vec %delta}_{ff}}
external noise
Controller
Process
reference
actual state
Monitor Transfer
Function
measurement noise
T0(s): Closed loop transfer function
S0(s): Complementary sensitivity

---
Lattice and Calibration Imperfections
Machine imperfections (beta-beat, hysteresis....), calibration errors and offsets can be translated into a steady-state εss and scale error εscale:
%DELTA x(s) = R_i(s) cdot %delta_i ~ toward ~ %DELTA x(s) = R_i(s) cdot (color red %epsilon_{ss} + (1 + color red %epsilon_{scale}) cdot %delta_i)
error signal Δ =
integral feedback signal
1rst
2nd
nth
...
Uncertainties and scale error of beam response function affects convergence speed (= feedback bandwidth) rather than achievable stability
Can be improved through measured or adjusting the actual response matrices
time
norm. parameter
Reference = 1
1-ε
actual parameter
Feed-Forward:
time
norm. parameter
Reference = 1
1-ε
actual parameter
Integral feedback:

---
Optimal Controller Design
Youla's affine parameterisation
Controller design often regarded as specialists' topic only - wrong!
Youla17,18 showed that all stable closed loop controllers D(s) can be written as:
Example: first order system
Using for example the following ansatz:
  - FQ(s) models the desired closed-loop response
  - Gi(s) being the pseudo-inverse of the nominal plant G(s)
(1)+(2)+(3) yields PI controller:
D(s)={Q(s)} over {1- Q(s)G(s)}
(1)
G(s) = {K_0} over {%tau s + 1} ~~~~~~~ %tau
(2)
with being the circuit time constant
Q(s) = {color red {F_Q(s)}} G^i(s) = {color red {{1} over {%alpha s + 1}}} cdot {{%tau s + 1} over {K_0}}
(3)
rightarrow T_0(s) = {color red {{1}over{%alpha s +1}}}
D(s) = K_P + K_i 1 over s ~~~ with ~~~ K_p=K_0{%tau over {color red %alpha}} ~&~ K_i =K_0{ 1 over {color red %alpha}}

---
Optimal Controller Design
Robust vs. Fast Closed Loop Response
α > τ...∞ facilitates the trade-off between speed and robustness
  - operator has to deal with one parameter → enables simple adaptive gain-scheduling based on the operational scenario!
faster
more robust/precise
disturbance rejection S0(s)
T0(s)

---
Motivation for Delay and Rate-Limiter Compensation
Example: LHC orbit feedback control
rate-limted process
without anti-windup
reference
current response
ramping rate
integral signal
without delay compensation
with full delay and windup
compensator scheme:

---
Time Domain: Optimal Controller Design
Including Non-Linearities
If G(s) contains non-stable zeros e.g. delay λ & non-linearities GNL(s)
with the power converter time constant, then:
Using (1) and (3) yields
Inserting in (1) yields Smith-Predictor and Anti-Windup schemes:
G(s) = {color blue e^{-%lambda s}} over {%tau s + 1} cdot {color blue {G_{NL}(s)}}
G^i(s) = {%tau s + 1} over {1}
%tau
T_0(s) = color red {F_Q(s)} cdot {color blue {e^{-%lambda s} G_{NL}(s)}}
DPID(s) gains are independent on non-linearities and delays!!

---
Part II: Tune and Chromaticity Measurements

---
Performing Tune/Q' FB: Measurement Options
Classic kicked or chirp excitation:
  - limited by aperture constraints
    - Performance reduction (lepton machines)
      - typically:
    - Loss of particles & protection (hadron machine)
      - LHC: Δz ≤ 25 μm & Δp/p ≤ 5·10-5
  - limited by emittance blow-up (hadron machines)
Passive monitoring of residual oscillations:
  - Schottky monitors
  - Diode-based Base-Band-Q (BBQ) meter
  - → also measures incoherent external noise	propagating onto the beam
Active Phase-Locked-Loop (PLL) systems
  - In combination with RF modulation → chromaticity tracking
color blue { {%DELTA z} ~leslant~ {0.1 %sigma} }
typical: ΔQres ≈ 10-3
typical: ΔQres ≈ 10-3 ...10-4
typical: ΔQres ≈ 10-3 ...10-5

---
Classic Phase-Locked-Loop Scheme
A∙sin(2πfe)
reference signal
Phase
Detector
Low-pass
Filter
Δφ
Control Law
D(s)
NCO
Δf
R(fe)∙cos(2πfe-Δφ)
A∙sin(2πfe)
beam
pickup
kicker
90°
beam response signal
G_{Beam}(%omega) = color blue {R(%omega)} cdot e^{i color red {%varphi(%omega)}}
beam response

---
Classic PLL Detector
Pro: robust analogue circuit implementation possible
Con:
  - non-linear control signal for large phase difference Δφ
  - Control signal depends on beam response's amplitude R(fe)
X
zexciter(t)
zdet(t)
zinput(t)
alignl z_{det}(t) = LP left(z_{%input}(t) cdot z_{exciter}(t) right)newline alignl ~~~~~~ = LP left(R(f_e) cdot cos(2%pi f_e - %DELTA%varphi(t)) cdot A sin(2%pi f_e) right)newline newline alignl ~~~~~~ = {{A R} over {alignc 2}} {sin(%DELTA%varphi(t))} ~+~ {{A R} over {alignc 2}} sin(4%pi f_e - %DELTA%varphi(t))
for small phases
removed by low-pass filter
color blue {% approx %DELTA%varphi(t)}
fLP

---
Improved PLL detector: Phase – Amplitude Decoupling
sin(2πfe)
Usually further compensation for other non-beam related phase responses:
  - constant lag (data processing, cables),
  - analogue pre-filters, beam exciter response...
Rectangular-to-Polar conversion
  - e.g. CORDIC algorithm (implements “atan2(y,x)”)
    - twice the dynamic range
rect2polar
Rect.
2
Pol.
NCO
ILP
X
ampl. loop
a
a
zinput(t)
φ
ILP
QLP
X
phase loop
φ
zexciter(t)
QLP
cos(2πfe)
fLP
fLP

---
PLL Closed Loop Controller
The PLL control loop dynamics and its design split into two parts:
  - PLL low-pass filter:	→
  - Beam response:	→ open loop gain K0
    - first order: K0 = const.
  - Youla's affine parameterisation: → yields optimal PI controller
%tau = 1 over {f_{BW}}
G_{PLL}(s) = {color magenta K_0} over {%tau s + 1} ~with~ %tau = 1 over f_{bw}
D(s) = K_P + K_i 1 over s ~~~ with ~~~ K_p = color magenta K_0 {%tau over {color red %alpha}} ~&~ K_i = color magenta K_0 { 1 over {color red %alpha}}
K0

---
Working Example: SPS PLL Tune Tracking
Phase error and non-vanishing amplitude indicate lock during ramp
ΔQ/Δt|max ≈ 0.3 about two orders of magnitude faster than required for LHC
tune trace
phase response
amplitude response
frev ≈ 43 kHz

---
Cross-Dependability and Constrains of FB Loops II/III - Coupling I/II
Strictly speaking: PLL measures eigenmodes (Q1, Q2) which in the presence of coupling may be rotated w.r.t. unperturbed tunes (qx, qy, Δ = |qy – qy|):
Possible improvement:
  - optimise tune working point (larger tune-split),
  - vertical orbit stabilisation in lattice sextupoles,
  - active compensation and correction of coupling
Q_{1,2} = {1 over 2} left( q_x + q_y +- sqrt{%DELTA^2 + {abs{C^{-%}}}^2} right)
Δ
|C-|
Tune FB on Q1,Q2 only
would break here
qy
qx
Q2
Q1
courtesy P. Cameron, BNL
RHIC, 2005

---
Cross-Dependability and Constrains of FB Loops II/III - Coupling II/II
Measure ratio between regular and cross-term:
  - A1,x: “horizontal” eigenmode in vertical plane
  - A1,y: “horizontal” eigenmode in horizontal plane
Decoupled feedback control
  - qx, qy	→	quadrupole circuits strength
  - |C-|, χ	→	skew-quadrupole circuits strength
color red {r_1 = A_{1,y} over A_{1,x}} ~~and~~ color red {r_2 = A_{2,x} over A_{2,y}} newline newline alignl % drarrow ~~~ abs{C^{-%}} = abs{Q_1 - Q_2} cdot {{2 sqrt{r_1 r_2}} over {(1 + r_1 r_2)}} ~~and~~ %DELTA = abs{Q_1 - Q_2} cdot {{(1 - r_1 r_2)} over {(1 + r_1 r_2)}}
χ
implemented and tested at RHIC
R. Jones e.al., “Towards a Robust Phase Locked Loop Tune Feedback System”, DIPAC'05, Lyon, France, 2005
P. Cameron, this workshop's Poster Session

---
Cross-Dependability and Constrains of FB Loops III/III
- Nested Feedback Loops
Traditionally loop designs are often addressed one-by-one
  - neglects cross-dependence and cross-constraints w.r.t. other nested FB loops
(skew) Quadrupole settings
ΔQ,ΔC-
Σ
Tune/Coupling
Controller
Qref,C-ref
Qavg
ΔQ'ref
ΔQmod
Sextupole Settings
ΔQ'
Amplitude
Detector
Chromaticity
Reconstr.
Σ
Chromaticity
Controller
Δp/p RF
modulation
A∙sin(2πfe)
reference signal
φ
Δf
Phase
Detector
Low-pass
Filter
PLL-Control Law
e.g. PID
NCO
A∙sin(2πfe)
beam response signal
R(fe)∙sin(2πfe+φ)
pickup
AC dipole
Tune/Coupling PLL
Chromaticity Tracker/Feedback
further: fBW(PLL) » fBW(Q') » fBW(Q, C-)
Tune/Coupling Feedback
cascading & separation of operational range (e.g. bandwidth or amplitude)
cross-dependence with orbit and energy feedback (dispersion orbit)
beam response

---
What Makes the PLL Break
- Tune Width Dependence
Optimal PLL parameters (tracking speed, etc.) depend - beside measurement noise – on the effective tune width.
Intrinsic trade-off:
  - Optimal PI for large ΔQ ↔ sensitivity to noise (unstable loop) for small ΔQ
  - Optimal PI for small ΔQ ↔ slow tracking speed for large ΔQ
Can be improved by putting knowledge into the system: “gain scheduling”
Tune width change →
change of phase slope (K0)

---
What Makes the PLL Break
- Erroneous Locking on Synchrotron Sidebands
Qualitatively: PLL locks on the largest peak within the bandwidth
Option I: gain scheduling
  - initial lock: open loop band-	width to cover more than one	side band (PLL noise ~ chirp)
    - side-bands “cancel out”
    - strongest resonance prevails
  - once locked:	reduce bandwidth for better	stability/resolution
Option II: larger excitation bandwidth
  - multiple exciter or broadband excitation19
phase response
courtesy C.-Y. Tan, FNAL
initial lock
fBW
once locked
fbw

---
What Makes the PLL Break
- Coupled-Bunch Instabilities
High-sensitivity PLL that operates within the transverse feedback “noise” (alternative: pilot/sacrificial bunch)
  - Pro: range separation minimises inter-loop coupling effects
  - Con: PLL does not benefit from suppression of coupled bunch modes
    - e-cloud, impedance, beam-beam, ....
κ2(s)
κ1(s)
κn-1(s)
E
//
G1(s)
G3(s)
...
G2(s)
Gn(s)
phase response
amplitude response
E
E

---
Summary
Beam-based FBs are remedies for perturbations on slow/medium time scales
  - Feedbacks on orbit/energy are standard, tune feedbacks quite common
    - Hadron machines starting to recognise their necessity
  - Chromaticity feedbacks still require pioneering work (LHC first?)
Feedbacks are only as good as the measurements they are based upon!
  - Systematic and thorough analysis of involved beam instrumentation and corrector circuits is essential!
Youla's affine parameterisation facilitates optimal adaptive non-linear control
  - enables gain-scheduling based on operational scenario
  - (Ziegler-Nichols/Coohen-Coon PID tuning are outdated!)
Beware of cross-constraints/coupling of simultaneous nested loops
  - May break a loop near you
  - Feedbacks should be designed as an ensemble
The author gratefully acknowledges contributions from many colleagues!

---
Reserve Slides

---
References I/II
(1) Proceeding of “3rd International Workshop on Beam Orbit stabilization”, 2004, http://iwbs2004.web.psi.ch/
(2) M. Böge, “Achieving Sub-micron Stability in Light Sources”, EPAC'04, Lucerme, 2004
(3) G Decker, “Beam Stability in Synchrotron Light Sources”, DIPAC'05, Lyon, France, 2005
(3.5) A. Camiel et. al., “Tune Feedback System at ELETTRA”, EPAC'94, London, England, 1994
(4) O. Berrig et al., “The Q-Loop: A Function Driven Feedback System for the Betatron Tunes During the LEP Energy Ramp”, CERN SL-98-039, 1998
(5) A.Fisher et al., “Tune Feedback in PEP-II”,SLAC-PUB-10230, 2003
(6) P. Cameron et al., “Tune Feedback at RHIC”, PAC'01, Chicago, IL, 2001
(7) P. Cameron et al., “Measuring Chromaticity Along the Ramp Using the PLL Tune-Meter in RHIC”, EPAC'02, Paris, 2002
(8) R. Hettel, “Beam Stability Issues at Light Sources”, 25th ICFA Advanced Beam Dynamics Workshop, Shanghai, 2002
(9) Chamonix XIV, “Damage levels - Comparison of Experiment and simulation” and PAC'05
(10) R. Assmann, “Collimation and Cleaning: Could this limit the LHC Performance?”, Chamonix XII, 2003
(11) S. Redaelli, “LHC aperture and commissioning of the Collimation System”, Chamonix XIV, 2005
(13) R. Steinhagen, “Closed Orbit and Protection”, CERM, MPWG #53, 2005-12-16
(14) S. Fartoukh, O. Brüning, “Field Quality Specification for the LHC Main Dipole Magnets”, LHC Project Report 501
(15) S. Fartoukh, J.P. Koutchouk, “On the Measurement of the Tunes, [..] in LHC”, LHC-B-ES-0009, EDMS# 463763
(16) G. Golub and C. Reinsch, “Handbook for automatic computation II, Linear Algebra”, Springer, NY, 1971
(17) D. C. Youla et al., “Modern Wiener-Hopf Design of Optimal Controllers”, IEEE Trans. on Automatic Control,1976, Vol. 21-1,pp. 3-13 & 319-338
(18) B. Anderson, “From Youla-Kucera to Identification, Adaptive and Non-linear Control”, Automatica, 1998, Vol. 34, No. 12, pp. 1485-1506
(19) C.Y. Tan, “The Tevatron Tune Tracker PLL”, FERMILAB-TM-2275-AD

---
References II/II
(20) R.J. Steinhagen et al., “Influence of Varying Chromaticity on Robustness of the LHC Tune PLL and its Application for Continuous Chromaticity Measurement.”, PAC'07, 2007
(21) R.J. Steinhagen, “First Results of the PLL Tune Tracking in the SPS”, Tune Feedback Final Design Review, BNL,http://www.agsrhichome.bnl.gov/LARP/061024_TF_FDR/index.html
(22) R.J. Steinhagen et al., “The LHC Phase-Locked-Loop for Continuous Tune Measurement - Prototype tests at the CERN-SPS”, PAC, 2007
(23) M. Gasior, R. Jones, “The principle and first results of betatron tune measurement by direct diode detection”, CERN-LHC-Project-Report-853
(24) R. Jones et al., “Towards a Robust Phase Locked Loop Tune Feedback System”, DIPAC'05, Lyon, France, 2005
(25) T. Schilcher, “Commissioning and Operation of the SLS Fast Orbit Feedback”, EPAC'04, Lucerne/Switzerland, 2004
(26) K. Park, “Development of High Precision Magnet Power Supply using the DSP”, this proceedings
(27) Q. King, “The All-Digital Approach to LHC Power Converter Current Control”, ICALEPS'01, 2001
(23) R.J. Rushton, “Diamond Storage Ring Power Converters”, EPAC'06, Edinburgh, Scotland, 2006
(29) P. Gros, “The 3Hz Power Supplies of the SOLEIL Booster”, EPAC'06, Edinburgh, Scotland, 2006

---
Expected LHC Tune Footprint
regular
PACMAN
courtesy H. Grote, CERN

---
Non-linear Slew-rate Limited Exciter Response
LHC orbit dipole corrector: ΔI=0.01 ↔ Δx ≈ 15 μm @7TeV

---
Tune and Chromaticity Perturbations Sources
Lepton and warm hadron accelerator
  - systematic quadrupole and dipole power supply drifts and ripples
  - hysteresis and temperature effects of magnet yokes
  - dipole to quadrupole tracking errors during ramp
  - beam-beam
  - e-cloud
Superconducting Accelerators
  - Decay & snap-back
  - Reduction of persistent	currents while ramping
esp.
KEK-b, PEP-II
& LHC
LHC nominal ramp (without FF):
        Maximum Rate ≈ 1.2 units/s
Chromaticity Change ≈ 300 units