Header
Accelerator Performance Committee Meeting, 2007-06-08
PLL Tune and Chromaticity Measurements
Ralph J. Steinhagen, AB-BI-QP
Acknowledgements: A. Boccardi, M. Gasior, K. Kasinski & R. Jones
References:	APC 2006-11-10(slides), Tune Feedback FDR (BNL, slides), DIPAC'07 (paper)

---
LHC Tune and Chromaticity Requirements
The measurement and control of
  - -- orbit, tune, chromaticity, energy and coupling --
  - will be an integral part of the LHC operation
Requirements summary (Chamonix'06):

---
Expected Tune and Chromaticity Drifts during LHC ramp
Exp. perturbations are about 200 times than required stability!
however: maximum drift rates are expected to be slow in the LHC
    - Tune:	ΔQ/Δt|max < 10-3 s-1
    - Chromaticity:	ΔQ'/Δt|max < 2 s-1
Requires active control relying on beam-based measurements
Feedbacks are only as good as the measurements they are based upon!
← the critical/difficult parameter

---
Performing Tune/Q' FB: Measurement Options
Classic kicked or chirp excitation:
  - limited by aperture constraints
    - Performance reduction
      - typically:
    - Loss of particles & protection
      - LHC: Δz ≤ 25 μm & Δp/p ≤ 5·10-5
  - limited by emittance blow-up (LHC: ~10 kicks)
Passive monitoring of residual oscillations:
  - Schottky monitors
  - Diode-based Base-Band-Q (BBQ) meter
  - → also measures incoherent external noise	propagating onto the beam
Active Phase-Locked-Loop (PLL) systems
  - In combination with RF modulation → chromaticity tracking
color blue { {%DELTA z} ~leslant~ {0.1 %sigma} }
typical: ΔQres ≈ 10-3
typical: ΔQres ≈ 10-3 ...10-4
typical: ΔQres ≈ 10-3 ...10-5

---
Classic Phase-Locked-Loop Scheme
A∙sin(2πfe)
reference signal
Phase
Detector
Low-pass
Filter
Δφ
Control Law
D(s)
NCO
Δf
R(fe)∙cos(2πfe-Δφ)
A∙sin(2πfe)
beam pickup
(BBQ)
90°
Kicker
(Trans. Damper/
Tune Tickler)
beam response signal
G_{Beam}(%omega) = color blue {R(%omega)} cdot e^{i color red {%varphi(%omega)}}
beam response

---
LHC PLL schematic: Phase – Amplitude Decoupling
sin(2πfe)
FPGA based decoupled loop implementation:
  - phase-locked-loop (→ tune)
  - excitation amplitude loop
Further compensation for other non-beam related phase responses:
  - constant lag (data processing, cables),
  - analogue pre-filters, beam exciter response...
rect2polar
Rect.
2
Pol.
NCO
ILP
X
ampl. loop
a
a
zinput(t)
φ
ILP
QLP
X
phase loop
φ
zexciter(t)
QLP
cos(2πfe)
fLP
fLP

---
PLL Closed Loop Controller
The PLL control loop dynamics and its design split into two parts:
  - PLL low-pass filter:	→
  - Beam response:	→ open loop gain K0
    - first order: K0 = const.
  - Youla's affine parameterisation: → yields optimal PI controller
%tau = 1 over {f_{BW}}
G_{PLL}(s) = {color magenta K_0} over {%tau s + 1} ~with~ %tau = 1 over f_{bw}
D(s) = K_P + K_i 1 over s ~~~ with ~~~ K_p = color magenta K_0 {%tau over {color red %alpha}} ~&~ K_i = color magenta K_0 { 1 over {color red %alpha}}
K0

---
21 September 2006: First successful BBQ based PLL
SPS 25ns fixed target beam: 26GeV → 450GeV, ~ 3e12 protons/beam
  - Horizontal tune: Qh≈ 26.76 → 26.66 (slow resonant extraction)
  - Fastest tracked tune change: ΔQ≈0.1 within about 200-300 ms
    - much faster than the maximum expected tune drift in the LHC!

---
Horizontal tune during ramp I/II
phase error and non-vanishing amplitude indicates lock during ramp
tune trace
phase response
amplitude response

---
Horizontal tune during ramp II/II
PLL – FFT Comparison:
excitation well below the 1 μm level (factor 10-600 below MultiQ)	→ negligible emittance blow-up
without Tune-PLL
with Tune-PLL

---
Imaginary Part of Collimator Impedance:
Horizontal Tune versus Full Gap Opening I/II
See APC 2006-11-10 for details
Correlation between tune shift and collimator opening

---
Imaginary Part of Collimator Impedance:
Horizontal Tune versus Full Gap Opening II/II
N.B. classic tune shift measurement (FFT using BBQ) was limited by large Q'

---
“Free” measurement:
Vertical Tune Shifts due to SPS Impedance
See APC 2006-11-10 for details
Vertical tune shift are a result of:
  - SPS transverse impedance and changing bunch length/intensity

---
“Free” measurement:
SPS Impedance at 270 GeV
See APC 2006-11-10 for details
tune resolution:
ΔQres≈ 10-6...10-7 !!
Using Sacherer's impedance approximation: Zeff ≈ 21.54 MΩ/m

---
Q' measurement trough slow Δp/p modulation
Tune PLL to track Q' (measurement during ramp)
Δp/p = 6·10-4
Q'~ 2 - 4
slow resonant
extraction
ramp start
SPS operation:	Δp/p > 10-3 & ΔQres≈10-3 → ΔQ'res ~ 1
LHC:	Δp/p < 10-4 & ΔQ'res ~ 1 → ΔQres < 10-4
  - limited by LHC Collimation orbit 'budget': Δx < 35 μm (nominal)
  - tough, still not established! → 2007 MD Target #1/3

---
If the accelerator world would be perfect.....
next slides: Things that can compromise PLL operation...

---
Cross-Dependability and Constrains of FB Loops II/III - Coupling I/II
Strictly speaking: PLL measures eigenmodes (Q1, Q2) which in the presence of coupling may be rotated w.r.t. unperturbed tunes (qx, qy, Δ = |qy – qy|):
Possible improvement:
  - optimise tune working point (larger tune-split),
  - vertical orbit stabilisation in lattice sextupoles,
  - active compensation and correction of coupling
Q_{1,2} = {1 over 2} left( q_x + q_y +- sqrt{%DELTA^2 + {abs{C^{-%}}}^2} right)
Δ
|C-|
Tune FB on Q1,Q2 only
would break here
qy
qx
Q2
Q1
courtesy P. Cameron, BNL
RHIC, 2005

---
Cross-Dependability and Constrains of FB Loops II/III - Coupling II/II
Measure ratio between regular and cross-term:
  - A1,x: “horizontal” eigenmode in vertical plane
  - A1,y: “horizontal” eigenmode in horizontal plane
Decoupled feedback control
  - qx, qy	→	quadrupole circuits strength
  - |C-|, χ	→	skew-quadrupole circuits strength
    - Requires local control of strong coupling sources
color red {r_1 = A_{1,y} over A_{1,x}} ~~and~~ color red {r_2 = A_{2,x} over A_{2,y}} newline newline alignl % drarrow ~~~ abs{C^{-%}} = abs{Q_1 - Q_2} cdot {{2 sqrt{r_1 r_2}} over {(1 + r_1 r_2)}} ~~and~~ %DELTA = abs{Q_1 - Q_2} cdot {{(1 - r_1 r_2)} over {(1 + r_1 r_2)}}
χ

---
What Makes the PLL Break
- Coupled-Bunch Instabilities
High-sensitivity PLL that operates within the transverse feedback “noise” (alternative: pilot/sacrificial bunch)
  - Pro: range separation minimises inter-loop coupling effects
  - Con: PLL does not benefit from suppression of coupled bunch modes
    - e-cloud, impedance, beam-beam, ....
κ2(s)
κ1(s)
κn-1(s)
E
//
G1(s)
G3(s)
...
G2(s)
Gn(s)
phase response
amplitude response
E
E

---
What Makes the PLL Break
- Synchrotron Sidebands: PLL locks on the largest peak
Option I: gain scheduling
  - initial lock: open bandwidth to cover more than one side band (PLL noise ~ chirp)
    - side-bands “cancel out”, strongest resonance prevails
  - once locked: reduce bandwidth for better stability/resolution
Option II: larger excitation bandwidth, multiple exciter or broadband excitation(FNAL)
initial lock
fBW
once locked
fbw

---
What Makes the PLL Break
- Tune Width Dependence
Reminder: optimal PLL Settings:
D(s) = K_P + K_i 1 over s ~~~ with ~~~ K_p = color magenta K_0 {%tau over {color red %alpha}} ~&~ K_i = color magenta K_0 { 1 over {color red %alpha}}
K0

---
What Makes the PLL Break
- Tune Width Dependence
Optimal PLL parameters (tracking speed, etc.) depend - beside measurement noise – on the effective tune width.
Intrinsic trade-off:
  - Optimal PI for large ΔQ ↔ sensitivity to noise (unstable loop) for small ΔQ
  - Optimal PI for small ΔQ ↔ slow tracking speed for large ΔQ
Can be improved by putting knowledge into the system: “gain scheduling”
Tune width change →
change of phase slope (K0)

---
Tune Width Measurement using PLL Side Exciter
Resonant phase change ↔ tune width change
  - → “free” real-time tune footprint measurement
  - → measurable dependence of ΔQ ~ Q'
driven resonance:
tan(%varphi) approx {%DELTA Q cdot %omega_Q%omega_D} over {%omega_Q^2 - %omega_D^2}
Q
Q-ΔQ
Q+ΔQ
2ΔQ ≈ 0.002 « 2Qs

---
16th November 2006:
Apparent Tune Width ΔQ dependence on Q'
tan[φ(Q-ΔQ)]
tan[φ(Q+ΔQ)
(ΔQ = 0.001)
ΔQ' ~ 2.6
Inverse amplitude response R-1(Q)
Side-exciter phase appears to change linearly with Q'
  - No additional momentum modulation
  - Absolute scale requires calibration w.r.t. to classic Q' measurement
  - Non-linear effects require further assessment → 2007 MD Target #2/3
preliminary!

---
Machine Development Summary of 2006 activities
The prototype test of the BBQ based tune PLL were very successful!
  - Mutually exclusive modes of PLL operation:
    - either: track tune changes with ΔQ/Δt ≈ 0.1/s
    - or: achievable tune resolution ΔQres≈ 10-4 ... 10-5
Required PLL excitation was...
  - at least a factor 10 smaller than standard SPS MultiQ
  - done with a S/N ratio of less than 3..10 dB
BBQ based PLL showed to be very robust as long as bunch-to-bunch coupling was small
  - will be addressed through selecting only single bunch
Question is not: “Can we measure chromaticity?”,	but “Can we measure Q' with a given precision and minimal excitation?”
  - Requires studies of systematics with “slow” coasting beam to prove feasibility of LHC Q' baseline (ΔQ'=1 & Δp/p«10-4)

---
Outlook Machine Development Studies in 2007
Measurement programme:
  - a) LHC Q' baseline via slow Δp/p modulation, 3x8h
  - b) Indirect Q' through ΔQ measurement, 3x8h
  1. c) Q' through continuous head-tail phase shift, 3x8h
  1. d) HW tests, mostly in parallel to regular physics programme
Total dedicated MDs:
  - coasting beam @ 270GeV: W28, W32, W35, W37, W42
  - coasting beam @ 26GeV: W30, W34
  - Reminder: assumed accelerator efficiency of about 60%

---
Reserve Slides

---
Coupled Bunch Instabilities
Coupled bunch effect became more pronounced during later MDs
  - possible causes: impedance driven wake fields, e-cloud, ...
Phase response can be explained by simple first order model:
  - e.g. classic Landau resonator Gn(s) and first order coupling Kn(s)
  - example: two coupled bunches
Possible remedy: BBQ selects and measures only one (first) bunch
κ2(s)
κ1(s)
κn-1(s)
E
//
G1(s)
G3(s)
...
G2(s)
Gn(s)
excitation
G1(s)
Σ
output
κ'2(s)
κ1(s)
Σ
G2(s)
E
E

---
PLL Measurement Resolution I/II
beam
amplitude
response
change of beam response amplitude indicates changing chromaticity
  - showed later to be cause for instabilities during the ramp

---
PLL Measurement Resolution I/II
Phase can be used as an estimate for tracking error (for a given chromaticity)
After some spike filter routine: ΔQres ≈ 10-4 - 10-5 @ 10 Hz	( compare traditional kick + FFT yields usually ΔQres ≈ 10-3)

---
Measurement Methodology I/III
Tune reference measurements (MultiQ) – (zoom in ramp):
Slow variation of Q
ΔQres≈10-3 visible
QV = 0.18
QH = 0.13

---
Measurement Methodology II/III
Chromaticity Reference Measurement during ramp (slow Δp/p + MultiQ):
Injecition: Q'≈2
ΔQres (~ΔQres) visible
Δp/p ≈ 1.6·10-3
ξV = 0.15
ξH = 0.3

---
Expected LHC Tune Footprint
regular
PACMAN
courtesy H. Grote, CERN

---
Non-linear Slew-rate Limited Exciter Response
LHC orbit dipole corrector: ΔI=0.01 ↔ Δx ≈ 15 μm @7TeV