Feasibility of (semi-) automated Tune Control in the PS
Internal BI Meeting, 2007-09-13
On the
Feasibility of (semi-) automated Tune Control in the PS
Ralph J. Steinhagen
Special thanks to
A. Boccardi, M. Gasior, S. Gilardoni,
Y. Papaphilippou, R. Steerenberg

---
Motivation
AB Management Board Meeting discussion (2007-08-13):
  - “Further tests were carried out on the pole face windings during the week and some higher frequency perturbations (100, 150 and 200Hz*) were observed in the beam. “
  - “S. Myers asked R. Garoby (for the BI group) to investigate the feasibility and the potential bandwidth of a closed loop control of the tune in the PS.”
  - (*minimised through power-converter controller optimisation)
Some basic considerations:
  - Stability:	“What are the required stabilities on Q/ξ?”
  - Controllability:	“Can Q/ξ be controlled without 'hidden parameters'?”
  - Observability:	“Can we measure Q/ξ (and also C-) robustly?”
  - will comment on staged implementation, steps and possible performance
Sensors
Controller
Actuators
controllability
observability
stability
beam response

---
Stability: “What are the required stabilities on Q/ξ?”
Discussion with OP/ABP (Rende, Yannis):
  - main outcome: inconclusive, since most beam parameter (orbit, tune, chromaticity) have/could not be measured systematically
  - most tight requirements assumed during slow extraction 10-3...10-4
  - otherwise: “keep the beam in the pipe”
    - minimisation of resonances, transition crossing, ...
    - to be kept in mind: the PS was/is running without beam-based feedbacks on orbit, tune, coupling and chromaticity for ~ 50 years
      - ... still the slow extraction worked.
  - preliminary: ΔQ ~ 10-2 ... 10-3, Δξ ~ 0.1...0.2 units?? (~SPS/LHC!?!)
    - time-scales are unclear – working assumption similar to SPS
(Ongoing) observation with beam required to quantify PS reproducibility and to cross-check real requirements with physics model prediction
N.B. “Requirements” are tighter than what is actually achieved in the PS. Many PS cycle show tune stabilities in the order of a few percent	(see measurements)

---
Controllability: PS' Combined Function Magnets
- Pole-Face-Winding (PFW, since 1978) I/IV
“Recent” 5-current mode implementation eliminates hidden parameters and enables independent control of QH, QH, ξH and ξV
8-loop

---
Controllability: PS' Combined Function Magnets
- Pole-Face-Winding (PFW, since 1978) II/IV
Main-magnet cross-section:
Main-magnet top-view:
2x Defocus. (DW, DN), 2x Focus. (FW, FN), 8-loop (~octupole) → 5 circuits
  - orthogonal control of: Qx, Qy, ξx, ξy
yoke
Currents direction:
    positive
    negative
main coils
main coils
8-loop
8-loop
Narrow defocusing PFW (DN)
Wide focusing PFW (FW)
IFW
IDN
IFN
Wide defocusing PFW (DW)
Narrow focusing PFW (FN)
IDW
8-loop
main coil
De-focusing
Focusing
(schematics courtesy Mariusz Juchno)
Pole-Face-Windings (PFW)

---
Controllability: PS' Combined Function Magnets
- Pole-Face-Winding (PFW, since 1978) III/IV
Response can be cast into beam matrix form, e.g.:
  - source: R. Gouiran, CERN/PS/SM 76-1, ΔIxx [A], p [GeV/c], p <15 GeV/c
  - Iron yoke saturation makes matrices slightly momentum dependent
    - differences per matrix element are small: < 10...20%
      - does not pose a big problem for feed-back systems
Main issues/concern:
  - Large differences (>100%) between model and measured response matrix
  - Assumes small betatron-coupled machine
    - Most PS cycle at least partially coupled	(quality of 5-current MD reponse matrix data?)
→ Any orbit, Q or Q' control requires also control/minimisation of coupling!
p cdot left( matrix{%DELTA Q_H ## %DELTA Q_V ## %DELTA %xi_H ## %DELTA %xi_V} right) ~=~ left( matrix{ +0.0647 # +0.0662 # -0.0352 # -0.0437 ## -0.0345 # -0.0444 # +0.0641 # +0.0668 ## +1.7909 # -0.3109 # +1.0416 # -0.2016 ## -1.2220 # +0.1820 # -1.4866 # +0.3066 } right) cdot left( matrix{ %DELTA color blue I_{FN} ## %DELTA color red I_{FW} ## %DELTA color blue I_{DN} ## %DELTA color red I_{DW} } right)

---
Controllability: PS' Combined Function Magnets
- Circuit and PFW Time-Constants
natural time constants ~ 2 ms (wide) and ~ 9 ms (narrow) resp.	(wide: R= 1 mΩ, L = 2 mH; narrow: R= 2.1 mΩ, L = 17 mH)
  - natural circuit bandwidth ~ 125 Hz
PFW are by ±1200V/±250A power converters (ΔI/Δt|max = 5 kA/s)
  - Driven “large signal” bandwidth:	~ 125 Hz	(ΔI~ 50A ↔ ΔQ ~ 0.1 @26 GeV/c)
  - Driven “small signal” bandwidth:	> 1 kHz (theoretical)	(ΔI~ 5A ↔ ΔQ ~ 0.01 @26 GeV/c, noise: ~ 50 mA ↔ ΔQ ~10-4)
Main limitations:
  - non-linearities due to current rate-limit (similar to LHC PC → easy for FB control)
  - PC sampling frequency (fs = 1kHz) limits effective Q-loop bandwidth, typically: fs ≈ 25...40 ∙ fbw
  - thus, from controllability point of view only Q-loop BW': fbw < 40 Hz
  - or: if fbw:= 100 Hz → fs > ~ 4 kHz

---
Observability -
PS version of the Diode-based Base-Band-Q-meter (BBQ)
Same proven analogue principle/acquisition electronics/software as in the SPS, except:
  - higher sampling rate (PS frev > 436 kHz vs. SPS frev ≈ 43 kHz)
    - specialised 40 MHz ADC mezzanine card
  - low-level analogue hardware:
    - Pre-low-pass and frev notch filter are adjusted to PS beam parameters
    - pickup geometry, ...
Some measurements with PS beam available, preliminary observations:
  - in contrast to SPS: no “tune-spectra guarantee” without excitation	→ kicks -- though they can be small -- seem to be mandatory
  - seems to work with un-bunched beam (see attachment)
  - seems to be compatible with most “RF-gymnastics” at least with those seen on the LHC25ns, MD2 and SFTPRO cycle (see following plots).
  - transparent to slow bunch length variations
  - of course: further tests are required and will be done!

---
DAB based BBQ acquisition: PS examples
PS-MD2, H/V kicks, “free-running mode”

---
PS-SFTPRO cycle, back-to-back acquisition, H/V kicks every 5 ms, horizontal plane
time in cycle
tune

---
PS-SFTPRO cycle, back-to-back acquisition, H/V kicks every 5 ms, vertical plane
time in cycle
tune

---
PS-SFTPRO cycle
Betatron-Coupling after Injection

---
What if.... (the nearish future) I/II
Provided that betatron-coupling is not required and minimised to zero....
...a semi-automated slow cycle-to-cycle feedback control could
  - correct for fast intra-cycle perturbations due to
    - current overshoots, b1/b2 mismatches, ramp systematics, ...
  - correct for slow environmental induced cycle-to-cycle perturbations:
    - girder movements, temperature drifts of magnetic fields (iron), slow intensity variations, ...
  - be useful for the fast setup of new user/cycles
  - reach an “intra-cycle” correction bandwidth” of ~ 100-200 Hz
  - possible implementation:
    - could be based on the already available BBQ instrumentation (the necessary tools are there!)
    - top-level GUI that performs an automated measure-and-correct principle using chirped FFT data
      - e.g. 1024 turn-FFT every 5 ms
      - similar to what is known in the SPS as 'Auto-Pilot' in case of trajectory/orbit steering

---
What if.... (the far (far?) away future) II/II
Provided that betatron-coupling is not required and minimised to zero....
...a fully-automated intra-cycle feedback control could in addition
  - correct for fast intra-cycle perturbations due to:
    - power converter (mains) harmonics,
    - fast intensity driven tune changes (beam loss + impedance)
    - other 'truly random'/incoherent noise sources
  - reach a feed-back bandwidth of ~ 100-200 Hz	(provided PC sampling frequency is increased to 4 kHz)
  - possible implementation:
    - PLL is not the ideal candidate for a robust Q-loop in the PS since RF bunch splitting, gymnastics, coupling and other effects 'skews up' the beam-transfer function which is required to be reasonably stable
    - (narrow bandwidth) chirp-based excitation with continuous FFT detection is preferable (e.g. 1024-turn FFT every 100 turns)
      - robust peak-detection needs further assessment
      - control logic could be fairly easily implemented within a FPGA once the digital converter input interface is established

---
Preliminary Conclusions
The actual implementation of the five current scheme enables (new) possibilities for the control of tune and chromaticity in the PS
  - requires control/minimisation of coupling!
However the need and/or requirements for a fast Q-loop control are unclear
Proposed feedback implementation/deployment steps:
  - 1. Quantification of parameter requirements based on robust measurements (ongoing)
  - 2. Semi-automated cycle-to-cycle feedback control
    - could reach a bandwidth of about 100-200 Hz
    - be implemented based on already available hardware
  - 3. Fully automated in-cycle feedback within in the Q-meter FPGA
    - could reach a true closed-loop bandwidth of about 100-200 Hz

---
additional supporting slides

---
Tune Measurement with slowly-extracted un-bunched Beam in the SPS
chirp off
RF + damper
noise
chirp on
RF off
vertical tune
horizontal tune
second injection
damper noise
first injection

---
Q/ξ Beam Response Matrix Uncertainties
Uncertainties in the beam response matrix reduced the effective control/feedback bandwidth but does not affect the steady-state precision
E.g. LHC orbit feedback:
perfect optic	→ 1 iteration
20% beta-beat	→ ~2 iterations
20% calibration error	→ ~7 iterations

---
Non-linear Slew-rate Limited Exciter Response
LHC orbit dipole corrector: ΔI=0.01 ↔ Δx ≈ 15 μm @7TeV

---
Cross-Dependability and Constrains of FB Loops II/III - Coupling I/II
Strictly speaking: PLL measures eigenmodes (Q1, Q2) which in the presence of coupling may be rotated w.r.t. unperturbed tunes (qx, qy, Δ = |qy – qy|):
Possible improvement:
  - optimise tune working point (larger tune-split),
  - vertical orbit stabilisation in lattice sextupoles,
  - active compensation and correction of coupling
Q_{1,2} = {1 over 2} left( q_x + q_y +- sqrt{%DELTA^2 + {abs{C^{-%}}}^2} right)
Δ
|C-|
Tune control on Q1,Q2 only
would break here
qy
qx
Q2
Q1
courtesy P. Cameron, BNL
RHIC, 2005

---
Cross-Dependability and Constrains of FB Loops II/III - Coupling II/II
Measure ratio between regular and cross-term:
  - A1,x: “horizontal” eigenmode in vertical plane
  - A1,y: “horizontal” eigenmode in horizontal plane
Decoupled feedback control
  - qx, qy	→	quadrupole circuits strength
  - |C-|, χ	→	skew-quadrupole circuits strength
color red {r_1 = A_{1,y} over A_{1,x}} ~~and~~ color red {r_2 = A_{2,x} over A_{2,y}} newline newline alignl % drarrow ~~~ abs{C^{-%}} = abs{Q_1 - Q_2} cdot {{2 sqrt{r_1 r_2}} over {(1 + r_1 r_2)}} ~~and~~ %DELTA = abs{Q_1 - Q_2} cdot {{(1 - r_1 r_2)} over {(1 + r_1 r_2)}}
χ
implemented and tested at RHIC
R. Jones e.al., “Towards a Robust Phase Locked Loop Tune Feedback System”, DIPAC'05, Lyon, France, 2005
P. Cameron, this workshop's Poster Session

---
PS magnet - old layout
Controllability -
PS' Combined Function Magnets
Main Dipole's Pole-Face-Winding (PFW) Schematic (before 1978)
1x Focus. (FW, FN), 1x Defocus. (DW, DN), 8-loop (~octupole) → 3 circuits
narrow
wide
2x Focusing (
2x Defocusing

---
HOT: SPS Q' tracking study
Radial RF modulation dp/p=1.6∙10-5, set ξ := 0.05
ΔQmod≈ 10-5