MAC 2007-12-06
Machine Advisory Committee 2007-12-06
some slides on:
SPS prototype tests for the
baseline LHC Q' measurement
Ralph J. Steinhagen for the BI-QP team
Accelerator & Beams Department, CERN

---
LHC Tune and Chromaticity Requirements
The measurement and control of
  - -- orbit, tune, chromaticity, energy and coupling --
  - will be an integral part of the LHC operation
Stability requirements summary (Chamonix'06):

---
Expected Tune and Chromaticity Drifts during LHC ramp
Exp. perturbations are about 200 times than required stability!
however: maximum drift rates are expected to be slow in the LHC
    - Tune:	ΔQ/Δt|max < 10-3 s-1
    - Chromaticity:	ΔQ'/Δt|max < 2 s-1
Requires active control relying on beam-based measurements
Feedbacks are only as good as the measurements they are based upon!
← the critical/difficult parameter

---
LHC Q' Tracking and Parameters
Baseline: RF/energy induced tune change Q' = ΔQmod/(Δp/p)
SPS standard operation:	Δp/p > 10-3 & ΔQres≈10-3 → ΔQ'res ~ 1
LHC operation (requirement):	Δp/p < 10-4 & ΔQ'res ~ 1 → ΔQres < 10-4
  - limited by LHC Collimation orbit 'budget': Δx < 35 μm (nominal)
  - Important milestone:
    - feasibility established during 2007 SPS MD tests (see examples):
      - modulation frequency: 0.5 Hz
      - Δp/p < 2·10-5 & ΔQres ~ 10-6 !! (limited by RF ADC quantisation)
  - Foreseen LHC parameter: Δp/p ~ 10-5 @ fmod = 1-2 Hz
    - essentially limited by whether:
      - possible remedies:
        - either: increasing Q'ref to e.g. 10 units
        - or: increasing Δp/p amplitude (if low-intensity beam)
        - or: increasing fmod (PLL limit: << 60 Hz)
{{Q' cdot {%DELTA p/p}} over {%DELTA t}} ~>~ left lline {{%DELTA Q} over {%DELTA t}} right rline_{max}

---
Cross-Dependability and Constrains of FB Loops
- Nested Feedback Loops
In order to address cross-dependence and constraints → nested FB loops
(skew) Quadrupole settings
ΔQ,ΔC-
Σ
Tune/Coupling
Controller
Qref,C-ref
Qavg
Q'ref
ΔQmod
Sextupole Settings
Q'
Amplitude
Detector
Chromaticity
Reconstr.
Σ
Chromaticity
Controller
Δp/p RF
modulation
A∙sin(2πfe)
reference signal
φ
Δf
Phase
Detector
Low-pass
Filter
PLL-Control Law
e.g. PID
NCO
A∙sin(2πfe)
beam response signal
R(fe)∙sin(2πfe+φ)
pickup
AC dipole
Tune/Coupling PLL
Chromaticity Tracker/Feedback
further: fBW(PLL) » fBW(Q') ≥ fBW(Q, C-)
Tune/Coupling Feedback
cascading & separation of operational range (e.g. bandwidth or amplitude)
orbit and energy feedback subtract ( = no correction of) dispersion orbit
beam response

---
Example: Prototype in the SPS (measurement)
modulation amplitude: Δp/p ≈ 1.85∙10-5
tune
PLL phase
PLL amplitude [a.u.]

---
Chromaticity Reconstruction (measurement)
modulation amplitude: Δp/p ≈ 1.85∙10-5
tune
Q'/Q
real-time Q' detection algorithm (agrees with SPS cross-calibration):
  - Q' resolution better than 1 unit (nominal performance)
  - N.B. tracking transients: ΔQ' feed-down on ΔQ (non-centred orbit)
    - ΔQ/Δt >> ΔQ'/Δt → SPS specific, LHC: ΔQ/Δt|max < 10-4/s