Feasibility of (semi-) automated Tune Control in the PS
APC Meeting, 2008-01-17
Results of the
Tune and Chromaticity MDs in the SPS
Ralph J. Steinhagen
for the BI-QP team

---
Outline
Motivation for extensive Q' MDs in the SPS
Base-line LHC Q' measurement techniques
  - slow Δp/p modulation based
  - Beam-Transfer-Function based Side-Exciter method
  - Results with Beam at the SPS
Outlook and 2008 MD programme

---
Reminder: LHC Tune and Chromaticity Requirements
The measurement and control of
  - -- orbit, tune, chromaticity, energy and coupling --
  - will be an integral part of the LHC operation
Stability requirements summary (Chamonix'06):

---
Reminder Exp. Tune and Chromaticity Drifts during LHC ramp
Exp. perturbations are about 200 times than required stability!
however: maximum drift rates are expected to be slow in the LHC
    - Tune:	ΔQ/Δt|max < 10-3 s-1
    - Chromaticity:	ΔQ'/Δt|max < 2 s-1
Requires active control relying on beam-based measurements
← the critical/difficult parameter

---
Flash Back: APC 2007-06-08
Tune PLL to track Q' (measurement during ramp)
Δp/p = 6·10-4
Q'~ 2 - 4
slow resonant
extraction
ramp start
SPS operation:	Δp/p > 10-3 & ΔQres≈10-3 → ΔQ'res ~ 1
LHC:	Δp/p < 10-4 & ΔQ'res ~ 1 → ΔQres < 10-4
  - limited by LHC Collimation orbit 'budget': Δx < 35 μm (nominal)
  - tough, still not established! → 2007 MD Target #1/3
Today ~ one year later: → this presentation's focus

---
Flash Back: APC 2007-06-08
Outlook Machine Development Studies in 2007
Measurement programme:
  - a) LHC Q' baseline via slow Δp/p modulation, 3x8h
  - b) Indirect Q' through ΔQ measurement, 3x8h
  1. c) Q' through continuous head-tail phase shift, 3x8h
  1. d) HW tests, mostly in parallel to regular physics programme
Total dedicated MDs:
  - coasting beam @ 270GeV: W28, W32, W35, W37, W42
  - coasting beam @ 26GeV: W30, W34
  - Reminder: assumed accelerator efficiency of about 60%
End of 2007: half of our MD time was lost to due to
  - machine setup (timing table setup errors, going-into-coast errors, ...)
  - tardy users prior to our MDs (clean-up of previous settings, ...)
However, we express our gratitude to OP, Elias and many others for the good cooperative environment that nevertheless made these measurements under these circumstances possible.

---
LHC Base-Line Q/Q' Diagnostics Overview – Q'
Slow RF momentum modulation – LHC Commissioning Phase A.3
  - class: Q' is proportional to momentum induced tune changes
Kicked Head-Tail Phase-Shift – LHC Phase A.3 (~ copy++ of SPS installation)
  - Status Quo (with a few detection improvements/GUI though)
  - multiple dependences on beam parameter other than Q'
    - impedance, non-linear damping (Q'/Q'', RF damper), non-lin. Qs, Qs
  - limited by emittance growth/orbit budget	→ however: still a good cross-reference and diagnostics tool for MDs
Side-exciter based method – end 2008/beginning of 2009
  - needs broader acceptance (human component) and assessment with LHC beam (parameters)
Continuous Head-Tail Phase-Shift – 2009++
  - Tested various schemes in2007 at the SPS but need further assessment.
Q' = {color red {%DELTA Q}} over {color blue {%DELTA p/p}}
the measured tune change
the RF induced momentum change (known)

---
Q' trough RF momentum modulation based method
Q' = {color red {%DELTA Q}} over {color blue {%DELTA p/p}}
the measured tune change
the RF induced momentum change (known)
There are multiple but similar detection techniques (classic, Brüning, McGinnis, ...)
  - LHC RF cooling power permits only slow modulation (J. Tückmantel et al.)
Controllability of Q' depends on ability to track the tune both accurately & fast, two options:
  - Fourier based:
  - Phase-Locked-Loop based:
Also intrinsic to this problem:
  - LHC expectations:
    - Tune:	ΔQ/Δt|max < 10-3 s-1
    - Chromaticity:	ΔQ'/Δt|max < 2 s-1
  - → Choose to tackle the Q/Q' measurement in the high accuracy limit.
  - → very small but slow (few Hz) Δp/p modulation while tracking Q with a PLL
%DELTA Q_{res} prop 1 over {sqrt{t_{meas}}}
tmeas: duration of measurement
{%DELTA Q_{res} prop 1 over {t_{meas}}}
%DELTA Q_{res}^{(,)} cdot %DELTA t_{res} = const.
“slow” compared to Q/Q' drifts
e.g. in the SPS/CPS/PSB

---
Quick-Reminder:
Classic Phase-Locked-Loop Scheme
A∙sin(2πfe)
reference signal
Phase
Detector
Low-pass
Filter
Δφ
Control Law
D(s)
NCO
Δf
R(fe)∙cos(2πfe-Δφ)
A∙sin(2πfe)
beam
pickup
kicker
90°
beam response signal
G_{Beam}(%omega) = color blue {R(%omega)} cdot e^{i color red {%varphi(%omega)}}
beam response

---
Quick Reminder:
Classic PLL Detector
Pro: robust analogue circuit implementation possible
Con:
  - non-linear control signal for large phase difference Δφ
  - Control signal depends on beam response's amplitude R(fe)
X
zexciter(t)
zdet(t)
zinput(t)
alignl z_{det}(t) = LP left(z_{%input}(t) cdot z_{exciter}(t) right)newline alignl ~~~~~~ = LP left(R(f_e) cdot cos(2%pi f_e - %DELTA%varphi(t)) cdot A sin(2%pi f_e) right)newline newline alignl ~~~~~~ = {{A R} over {alignc 2}} {sin(%DELTA%varphi(t))} ~+~ {{A R} over {alignc 2}} sin(4%pi f_e - %DELTA%varphi(t))
for small phases
removed by low-pass filter
color blue {% approx %DELTA%varphi(t)}
fLP

---
Quick Reminder:
LHC Phase-Locked-Loop Scheme
G_{Beam}(%omega) = color blue {R(%omega)} cdot e^{i color red {%varphi(%omega)}}
beam response
reference signal
BBQ
Trans. Damper/
Tune Tickler
R(fe)∙cos(2πfe-φ)
A∙sin(2πfe)
X
fLP
X
fLP
Rect.
2
Pol.
NCO
phase loop
ampl. loop
R(ω)
φ
φ
ILP
QLP
QLP
ILP
rect2polar
sin(2πfe)
cos(2πfe)
R(ω)
Gpre(s)
zinput(t)
Gex(s)
zexciter(t)
Δf
Δa
beam response signal
90°

---
Flash Back: APC 2007-06-08
SPS PLL Tune Tracking – fast tracking
Phase error and non-vanishing amplitude indicate lock during ramp
ΔQ/Δt|max ≈ 0.3 within 300 ms, two orders of magnitude faster than LHC req.
tune trace
phase response
amplitude response
frev ≈ 43 kHz

---
Flash Back: APC 2007-06-08
SPS Impedance at 270 GeV – precise tracking
See APC 2006-11-10 for details
tune resolution:
ΔQres≈ 10-6...10-7 !!
Using Sacherer's impedance approximation: Zeff ≈ 21.54 MΩ/m

---
2007 Q' Milestone:
High-Res. Q Measuremnt of RF Induced Δp/p Modulation
SPS Q' MD parameters:
  - RF modulation frequency: 0.5 Hz (fixed frequency external generator)
    - Δp/p < 2·10-5 & ΔQres ~ 10-6 !!
    - limited by RF DAC generator quantisation (fmax-fmin ↔ ~ 6 bins)
  - Foreseen LHC parameter: Δp/p ~ 10-5 @ fmod = 1-2 Hz
    - essentially limited by whether:
    - possible optimisations:
      - either: increasing Q'ref to e.g. 10 units (LHC Stage-1)
      - or: increasing Δp/p amplitude
        - only possible with low-intensity beam (depreciated)
      - or: increasing fmod (PLL limit: << 60 Hz)
        - estimated maximum analogue PLL bandwidth ~ 6- 10 Hz
    - Multiple detection techniques available:
      - linear regression, full Χ2-fit, amplitude demodulation (LHC),
{{Q' cdot {%DELTA p/p}} over {%DELTA t}} ~>~ left lline {{%DELTA Q} over {%DELTA t}} right rline_{max}

---
PLL based Q/Q' tracking study at the SPS
Radial RF modulation dp/p=1.6∙10-5, set ξ := 0.05
N.B. done in parallel with a collimation MD

---
PLL based Q/Q' tracking study at the SPS
Radial RF Modulation dp/p=1.6∙10-5, set ξ := 0.05
ΔQmod≈ 10-5
N.B. done in parallel with a collimation MD

---
Dedicated PLL based Q/Q' tracking study at the SPS
Modulation Amplitude: Δp/p ≈ 1.85∙10-5
tune
PLL phase
PLL amplitude [a.u.]

---
Dedicated PLL based Q/Q' tracking study at the SPS
Modulation Amplitude: Δp/p ≈ 1.85∙10-5
→ EPAC'08
tune
Q'/Q
real-time Q' detection algorithm (agrees with SPS cross-calibration):
  - Q' resolution better than 1 unit (nominal performance)
  - N.B. tracking transients: ΔQ' feed-down on ΔQ (non-centred orbit)
    - ΔQ/Δt >> ΔQ'/Δt → SPS specific, LHC: ΔQ/Δt|max < 10-4/s

---
Dedicated PLL based Q/Q' tracking study at the SPS
Modulation Amplitude: Δp/p ≈ 1.85∙10-5
Q'/Q
tune
Scans to assess the maximum useful range yield showed that this method can cope with values of Q' up to at least 34 units.
  - larger than (any other) Fourier based method ... (usually damping limited)

---
PLL based Q/Q' tracking study at the SPS
Beam-Transfer-Function
Require for:
  - LHC: PLL setup and re-calibration: phase/amplitude adjustments, ...
“Free” fast tune footprint measurement that can be used to measure:
  - Impedance, Q', Q'', Q''', other advanced beam measurements, ...
Thus, we plan to deploy this facility in 2008 as an MD tool also for the SPS.

---
PLL based Q/Q' tracking study at the SPS
PLL Side Exciter (SEX) based Tune Width/Q' Measurement
Resonant phase change ↔ tune width change
  - → “free” real-time tune footprint measurement
  - → measurable dependence of ΔQ ~ Q'
driven 2nd order resonance:
tan(%varphi) approx {%DELTA Q cdot %omega_Q%omega_D} over {%omega_Q^2 - %omega_D^2}
Q
Q-ΔQ
Q+ΔQ
2ΔQ ≈ 0.002 « 2Qs

---
PLL based Q/Q' tracking study at the SPS
PLL Side Exciter (SEX) based Tune Width/Q' Measurement
tan[φ(Q-ΔQ)]
tan[φ(Q+ΔQ)
(ΔQ = 0.001)
ΔQ' ~ 2.6
Inverse amplitude response R-1(Q)
Side-exciter phase appears to changes linearly with Q' (2007 MDs)
  - No additional momentum modulation
  - Absolute scale requires calibration w.r.t. to classic Q' measurement
  - Non-linear effects require further assessment → 2007 MD Target #2/3

---
PLL based Q/Q' tracking study at the SPS
Tune Width Dependence on Chromaticity
... common believe/dogma: ΔQ = Δp/p
Since then: 2007 SPS MDs
  - many additional BTF/side-exciter data taken which seem to confirm previous observation → need cross-verification on other machines (LHC)
  - Sketch of possible mechanism (/best candidate?) to explain the effect:
    - Sextupole intrinsically include/create Landau damping
      - lowest-order non-lin. accelerator element (Hamil. ~ J, J1/2, J3/2)
      - strong pre-set fields to compensate usually the large	'natural chromaticity' → intrinsic non-linearities are strong
    - However: classic/operational control relies on small variation around the pre-set Q' value only (Q' > 0 & σQ' < 10) which make the non-linearities “appear” linear in this regime.
    - depends on the lattice and likely scales with accelerator size
Further assessment of higher order feed-down effects required (octupoles...)
Q'', octupole strengths are measurable as an asymmetry in the ΔQ distrib.	→ net effect on the SEX-based Q' method seems to be small.
  - Further simulations in progress → paper/report in preparation

---
Machine Development Summary of 2007 activities
The prototype test of the PLL based Q' measurement were very successful!
  - 1 unit of Q' resolution with Δp/p < ~ 10-5 @ 0.5 Hz (target ~ 2-5 Hz)
  - compatible with large values of chromaticity and LHC operation
  - → baseline Q' control in good shape for nominal LHC
Tune-Width dependence on Q' was verified to be a reproducible effect
  - Exploited through using Side-Exciter
  - Better understanding on dependence on other non-linear elements/effects
    - Intrinsic sextupole non-linearities are important aspect in this
Many thanks to all who helped in participated in these MDs
  - special thanks to T. Bohl and J. Wenninger who helped with SPS setup

---
Outlook Machine Development Studies in 2008
Measurement programme:
  - Dedicated MDs:
    - Continuous beta-beat measurement
    - Q' through continuous head-tail phase shift
    - Side-Exciter based Q'
  - MDs in parallel with other users/physics operation:
    - Fast/continuous measurements of Q'', Q''', ...
      - using the PLL Beam-Transfer-Function scan facility
      - using the side-exciter type method
    - Further LHC related BBQ improvements
      - bunch selector, diode-detector
“... to boldly do what no one thought or dared before.”

---
additional supporting slides

---
FFT Based Q Acquisition – 'On Demand'
Example: Tests at the SPS - Real-Beam Data

---
FFT Based Q Acquisition
Δp/p ~ 2·10-5 driven Q modulation (Q'v ~ 36 units)

---
Future Integration of Q/Q' Measurements for Q/Q' Control
Full LHC Beam-Based Control Scheme
(Skew-) Quadrupole settings
ΔQ,ΔC-
Σ
Tune/Coupling
Controller
Qref,C-ref
Qavg
Q'ref
ΔQmod
Sextupole Settings
Q'
Chromaticity
Reconstr.
Σ
Chromaticity
Controller
f0+Δf, Δp/p
A∙sin(2πfe)
reference signal
φ
Δf
Phase
Detector
Low-pass
Filter
PLL-Control Law
e.g. PID
NCO
orbit ref.
δ, Δp/p, Δf
Δp/p RF
modulation
Orbit Feedback
Controller
Σ
(12x/10x)
16x2
32x
1075x2
530x2
x2
2x2
BBQ
BPMs
CODs
RF
mini-
AC
dipole/
damper
2 (+2) x 2
Orbit/Energy Feedback
Tune/Coupling PLL
Chromaticity Tracker/Feedback
further: fBW(PLL) » fBW(Q') ≥ fBW(Q, C-)
Tune/Coupling Feedback
LHC FBs: 2158 input devices, 1136 output devices → total: ~3300 devices!
R(fe)∙sin(2πfe+φ)
beam response
A∙sin(2πfe)
LHC
beam response
Δf