Title
Some aspects on:
LHC Global Aperture Measurements
Ralph J. Steinhagen
with input from:
R. Jones, S. Redaelli, J. Wenninger and others
see also:
link → LHCCWG, Classification and Detection of LHC BPM Errors and Faults, 2007-10-23
link → MPWG #53, Closed Orbit and Protection, 2005-12-16

---
Motivation
Motivation for aperture scans:
  - Machine Protection : combined failure mode: bump + other fast failure
  - LHC Cleaning System: settings dependence on aperture model assump.
  - BPMs alignment and calibration: detection of spurious offsets
  - Optics verification for regular LHC operation
Two applicable methods:
  - Aperture scans: free Betatron-oscillations, controlled emittance blow-up
  - Magnet surveillance: main dipoles (done), CODs, quadrupoles,

---
Machine Protection: Closed Orbit drifts...
alone are unlikely to cause damage to the machine
  - Expected drift velocities are slow: < 2 σ/s
  - Easily detectable and captured through beam loss monitors
    - independent on whether they are local or global drifts
However, combined failures are an issue:
  - “local orbit bump” + fast other failure, e.g.:
    - Single turn failure involving injection, extraction or aperture kicker
    - fast magnet field decays
  - reduction of alignment margin at local protection devices
    - TDIs, TCDQs, Collimators etc.
Local orbit bumps may compromise passive protection properties of absorbers and collimators for machine protection!

---
Example: Protection against Single Turn Failures
Combined failure: (Pilot) Injection with perfect closed orbit
TI8/TI2 collimators limits |xb(s)|max < 5 s, TDI (locally) limits |xb(s)|max < 7 s
Perfect matching: beam circulates on closed orbit & εTI8/TI2 = εring
Δx,Δx'/optics mismatch: → oscillation around xco & filamentation εring > εTI8/TI2
  - But: sring < 7 s globally (if proper TDI setup)
  - TDI shadows critical machine aperture
“Ring aperture is safe”, assuming only single turn (injection) failures.
IR2
'e.g. arc'
res. betatron oscillation
Na [σ]
~7.5σ
>7.7s
5s
closed orbit
MKI
TDI

---
Example: Compromised Protection through Orbit Bumps
Combined failure: Local orbit bump and injection of nominal beam:
TI8/TI2 collimators limits |xb(s)|max < 5 s, TDI (locally) limits |xb(s)|max < 7 σ
  - TDI does potentially not shadow sensitive equipment
  - → Orbit bumps may compromise function of absorbers for protection if beam is closer to the aperture than to TDI
IR2
e.g 'bump in arc'
Potentially:
< 7s
Na [σ]
~7.5σ
Space covered by potential
injection oscillations
5 σ
closed orbit
MKI
TDI

---
Example: Compromised Protection through Orbit Bumps
Combined failure: Local orbit bump and collimation efficiency (/kicker failure):
Primary collimator (TCP) limits |xb(s)|max locally to <5.7s, secondary collimator (TCS) at~ 6.7s
To guarantee two stage cleaning efficiency/machine protection:
  - Local: TCP must be >0.7s closer than TCS w.r.t. the beam → Orbit FB
  - Global: no other object (except TCP) closer to beam than TCS
  - → Orbit bumps may compromise function of collimation if beam is closer to the aperture than to jaws!
IR2
IR3
e.g 'bump in arc'
Potentially:
< 6.7s
Na [σ]
~7.5σ
primary halo
6.7s
5.7s
closed orbit
TCP & TCS
MKI
TDI

---
BPM Functionality Test Procedure
Three main lines of defence against BPM errors and faults:
  - Pre-checks without beam using the in-build calibration unit
    - eliminates open/closed circuits, dead circuits/element candidates
  - Pre-checks with Pilot and Intermediate beams
    - verifies calibration offset (guarantee) and slope (golden orbit)
    - verifies/guarantees proper function of machine protection
  - Continuous data quality monitoring through Orbit Feedback
    - detects spikes, steps and BPMs that are under verge of failing
(k-modulation can for a few (insertion) BPMs provide some additional limited cross-checks for BPM misalignments w.r.t. magnetic quadrupole limits. However: no hard limits!)

---
2.Pre-checks with Pilot and Intermediate beams I/III
Two simple functional tests to check whether BPMs are working.	Idea: “Every non-moving position reading indicates a dead BPM”.
  - free betatron oscillation with rotating phase
    - non-moving BPM readings → faulty BPM
    - tests calibration factor and/or optics
  - aperture scan to checks abs. BPM offsets and insures proper machine protection functionality:
    - Orbit is not a “play-parameter” for operation, except at low intensity. (‘Playing’ with the orbit will result in quasi-immediate quench at high intensity.)
IR2
IR3
e.g 'bump in arc'
Potentially:
< 6.7s
Na [σ]
~7.5σ
secondary halo
6.7s
5.7s
closed orbit
TCP & TCS
MKI
TDI
1 R. Steinhagen, “Closed Orbit and Protection”, MPWG #53, 2005-12-16

---
Aperture e-Blow-Up
Aperture Measurement using controlled Emittance Blow-Up
Three methods to establish whether the closed orbit is within 6.7σ of the available mechanical resp. dynamic aperture:
Scan using emittance blow-up:
  - Increase beam size in a controlled	way while measuring the beam size.	(e.g. using transverse damper and synchrotron light monitor/IPM)
  - Once particle loss above given threshold:
    - → store last beam size measurement
  - “Is beam size ≥ 6.7 s0 ?” (s0: beam size at injection)
    - Yes:	→ mechanical aperture ≥ 6.7 s → orbit is safe
    - No:	→ mechanical aperture ≤ 6.7 s → orbit is un-safe
      - rework orbit reference (compare with old reference....)
ε0→
72∙ε
aperture
particle loss
→stop ε blow-up
beam@inj
blown-up beam
Orbit
offset

---
Aperture Measurement using Tune/Aperture Kicker Magnet
N=100 turns
s(s)
3∙s(s)
Scan using tune/aperture kicker:
  - likely to create larger beam loss transients (easy BLM detection)
  - indicates aperture location assuming “hitting aperture → losses at down-stream quadrupole” dependence
  - filamentation → emittance blow-up → need to dump and re-fill beam
  - tune kicker provides only 1 σ oscillations @ 450 GeV (⇄ 3 kV)
  - aperture kicker:
    - intrinsically dangerous/un-safe
    - not and ad-hoc instrument

---
Aperture COD
Aperture Measurement using closed orbit dipole magnets
Scan using two COD magnets (currents: I1 & I2) with π/2 phase advance:
  - Scan (assuming global aperture of ~ 7.5σ):
    - φ = 0→2π requires ~25 seconds @7σ, per transverse angle
    - propose to measure at four transverse angles: 0o, 45o, 90o, 125o
  - Increase amplitude (COD currents) till orbit shift ≈ 6.7σ
  - Loss does not exceed predefined BLM threshold if COD settings@ 6.7σ:
    - Yes:	→ mechanical aperture ≥ 6.7 s → orbit is safe
    - No:	→ mechanical aperture ≤ 6.7 s → orbit is un-safe
  - additional feature: compare measured with reference BPM step response (xco= 0-3σ)
    - → rough optics check (phase advance and beta-functions)
aperture
φ = 0 → 2π
I1=Imax∙sin(φ)
Imax
φ
ideal orbit
s
I2=Imax∙cos(φ)
x/√β [σ]
Amp.: 3σ→7σ

---
Intermediate Summary:
Controlled e-blow-up/kicker scan:
may check both planes at the same time
relatively fast measurement
reliability/robustness of beam size measurement/blow-up is an issue
no information on injection optics
Tests rather dynamic than mechanical aperture if adyn < amech
Destructive measurement
  - beam has to be dumped after scan
  - cannot be used for collimator setup
  - increased beam loss during extraction
COD Betatron oscillation scan:
non-destructive measurement	(could be done to check during each injection)
rough information on injection optic
Independent information on planes
checks only one plane at a time
What to do if on COD is down?
  - spares: longer measurement
requires ~30 s for a scan at 7s
Required:
  - inhibit injection during scan
  - COD setting reset after scan
All three methods:
  - Determine the available aperture
  - should be performed with low-intensity beams
  - need time and exclusive control of the machine
in order to minimise the need for too frequent aperture scans:
  - → perform above checks only when exceed given window

---
Indicators whether Aperture Scan is required I/II
BPM orbit surveillance
Propose to perform two procedural steps for each fill:
A: Initial check whether Orbit is safe:
  - 1. After Pilot injection: scan aperture with retracted collimators till either the assumed mechanical aperture is reached or beam loss is triggered
    - eliminates “dead”, calibration, wrong gain mode BPMs for 'HIGH-SENSITIVITY'
    - estimates BPM offsets and tests safe aperture model with an accuracy of better than one r.m.s beam width.
    - verification of correct injection optics (orbit response)
  - 2. After intermediate beam injection: collimators in nominal positions w.r.t. above measured global aperture and scan till a pre-defined beam loss (pattern) is reached
    - eliminates “dead”, calibration, wrong gain mode BPMs for 'LOW-SENSITIVITY'
    - verifies that primary collimators/absorbers are set correctly → Partial assurance that we setup the system properly....
      - Potential bump scans to determine location of aperture
  - 3. save “safe BPM reference” current settings → xref = “SAFE SETTING”
B: Continuous Monitoring:	if ( |xmeas.- xref| < Δxtol) {...}
    - FALSE: potential orbit bump detected
    - TRUE: Orbit is safe
no
yes

---
Indicators whether Aperture Scan is required I/II
Magnet Current Surveillance
Iref(..)=Imeas.(..)
yes: Orbit Safe
no: perform aperture scan
Aperture scan:
→ Orbit safe!
Save COD reference
settings Iref(..)
[...]
Proposed Procedure:
  - A: Initial check whether Orbit is safe:
    - aperture scan (ε blow-up, betatron-oscillation)
      - Potential bump scans to determine location of aperture
    - Save “safe COD reference” current settings → Iref(...) = “SAFE SETTING”
  - B: Each cycle:
    - Compare with actual current reference Imeas(..):
if (|Imeas(..) - Iref(...)| < ΔItolerances) {...}
      - FALSE:	Orbit may contain potential bumps	→ State A
      - TRUE:	Orbit can be considered to be safe → State B
no
yes
time

---
Summary
Current Surveillance:
Pro's
Can be used to check before first injection
Can run in parallel to orbit FB operation
Con's
Less sensitive to complicated orbit bumps
No precise & simple 'ΔI → Δx' transfer function available
depends on machine optic, energy
CODs create not only bumps but compensate, ground motion, decay & snap-back, multipole field errors, ..
Aperture scans + BPM Surveillance:
Pro's:
Easy to check with circulating beam
Less dependent on machine optics
Sensitive to most orbit manipulations
Con's:
erroneous BPMs
No information before injection
affected by systematic BPM uncertainties
Potential cross-talk with orbit feedback
N.B. Tolerance levels (“SAFE SETTINGS”) should include margin for:
Compensation of closed orbit and optics uncertainties = “natural effects”
BPM system uncertainties
OFB operation (crossing/separation bump, injection/extraction steering, ...)

---
additional slides

---
Machine Protection: Closed Orbit Uncertainties at Injection
LPR501 specification1:
  - nom.: (Dp/p)max ≈ 10-4	0.25 σ (MD: max ≈ 3.7 s)
  - b2+b3∙Dx decay: (Db/b)3s ≈ 2.5%	0.03 σ
Moon/sun tides2 (Δp/p ≤ 5.0∙10-5)	0.14 σ
Main Bends, random b1≈0.75 units34 (dipole kick)	0.11 σ
Random ground motion5 (10 hours)	~0.3 – 0.5 σ
Systematic ground motion drifts:	~?? σ
MCB hysteresis6	0.01 σ
MCB ±8V/±60A PC stability7 (16bit ADC)	0.10 σ
Total (abs):	~0.9 - 1.1 σ (max: 4.6 σ)
→ May become an issue for (close to) nominal operation
1: M. Giovannozzi: FQWG Meeting on 8th of March 2005
2: J. Wenninger: “Observation of Radial Ring Deformation using Closed Orbits at LEP”
3: M. Haverkamp, “Decay and Snapback in Superconducting Accelerator Magnets”, CERN-THESIS-2003-030
4: FQWG-Homepage: http://fqwg.web.cern.ch/fqwg/
5: RST: “Analysis of Ground Motion at SPS and LEP, implications for the LHC”, AB note to be published
6: W. Venturini: “Hysteresis measurements of a twin aperture MCB orbit corrector”, 19th October 2005
7: Q. King, L. Ceccone: private communications
M.

---
Example: Tolerance and COD Constraints
Mechanical aperture:	Na = n σ (e.g. n=7.5)
Deductions:
  - Collimation:	6.7 σ
  - Momentum correction
  - Known uncertainties:	1.1 σ
  - Unknown:	~?? σ
safe window for dynamic closed orbit modifications: ~ “- 0.3 σ”???
  - Evident: aperture check required!
Possible MCB tolerance levels:
  - ... 1 σ orbit excursion using CODs one needs e.g.:
    - All CODs with a r.m.s. kick of ~ 1.4 mrad ↔	≈ 0.07 A@450 GeV
    - 3COD bump: 2x ~12 (-0.1) mrad ↔	≈ 0.5 (0.05)A@450 GeV
  - → Vicious bump: smaller strengths and larger local displacement possible!
  - ... 1 σ orbit excursion through dispersion one needs (Δp/p ≈ 4∙10-4):
    - Coherent shift of all MCBH CODs	≈ 0.5 A@450 GeV
→ MCB current change of 0.5 A is likely to cause a orbit bump/shift of 1 σ.

---
Continuation of Interlock Scheme through Ramp
Scheme may be extended through the ramp till squeeze:
  - Similar effects as in injection that perturb the orbit dynamically:
    - Snapback (= inverse of Decay), ground motion,...
  - But: effect of each dipole (deflections) depends on energy:
    - Interlock window and its centre has to be scaled with energy:
      - 0.5 A/σorbit @450 Gev → 7.8 A/σorbit @7 TeV
Continuation through β*-Squeeze seems to be tricky:
  - CODs do not compensate only ground motion/decay
  - Squeeze induced orbit shifts due to systematic (mis-)alignment of the orbit inside the insertion quadrupoles. If not corrected:
    - Squeeze induced orbit drift up to 30 mm ↔ 100 σ!
→ No simple window to subtract squeeze induced COD changes from those creating bumps.

---
Known Error Sources: BPM dependence on
bunch length σb, intensity nb	(σf: filter time constant)	and	integrator temperature changes ΔT,	filling pattern, ...:
bunch intensity
bunch length
DAB temperature