MAC 2007-12-06
Beam Commissioning Meeting 2008-12-16
miscellaneous slides, status and comments on:
LHC (Beam 2) Commissioning
- BPM, Q, Q'
Instrumentation and Diagnostics -
Ralph J. Steinhagen for the BI-QP team
Accelerator & Beams Department, CERN

---
Outline
For those who have been nice...
Tune Measurements
Coupling Measurements
- Chromaticity estimates
  - Injection tune shifts
  - Q resonance width & Qs side-bands
Something to think about/follow up...
- Residual LHC beam noise and	misalignment estimates
  - BBQ and BPM resolution

---
LHC Base-Line Q/Q' Diagnostics Overview – Q/C-
BBQ Use-Cases Abstraction
- Three independent BBQ Tune/Coupling diagnostic chains available per beam:
  - PLL based acquisition - commissioning pending!
    - one measurement at high/reduced acquisition frequency, targets:
      - 100 Hz for feedbacks (driven by need to reduce feedback latencies)
      - 1 Hz for general purpose logging
    - expert: high frequency data, event synchronised and buffered (post-mortem, PLL setup), typical length: 5 min ↔ < 1 MB of data
    - main use: monitoring/logging, feedbacks, fill-to-fill studies, ...
  - FFT based acquisition – 'periodic' (FFT1) – B2 fully commissioned
    - one measurement every 1 second starting from first-injection
    - intended use: monitoring/logging, (feedbacks), fill-to-fill studies, ...
  - FFT based acquisition – 'on demand' (FFT2) – B2 fully commissioned
    - n-measurements synchronised to an external event (BPM, BQ, ...)
    - intended use: expert diagnostics, detailed studies, ...

---
Present Commissioning State
- BBQ systems for B2 including excitation and correction commissioned
  - One important stepping stone in getting the beams circulating
- Next few slides document how we got there...
  - N.B. Colour coding: 'blue frames' = B1 data & 'red frames' = B2 data
Very first turn B2 (B1 similar)!
first circulating beam...

---
Sep. 10thBeam 2 Injection Tune – 14 Turn Data
- After adjusting first two turns (no RF, QH ≈ .44, QV ≈ .28)
  - Transient in raw (turn-by-turn) data:	BBQ intrinsic discharging once beam is gone
- Observations: only 14 turns – could the big spectra 'humps' indeed by the injection Q's?
  - vertical spectra is cleaner → decided to trim 'Δqv=-0.1' and observe change
ver. raw data - zoom
BBQ specific discharge
transients at beam-out
~14 turns

---
Beam 2 Injection Tune – 14 Turn Data – Qv Trim
- no RF capture , QH ≈ .5 → .315, QV ≈ .24, observation:
  - Programmed 'ΔQH=-0.2' seen as expected (LSA bug fixed, courtesy M. Lamont)
  - Moving from the half-integer resonance → 300+ turns (still no RF capture)
LSA Settings (= deviation from reference): ΔQH = - 0.05, ΔQV = - 0.2
ΔQH

---
Beam 2 Injection Tune vs. Trim History
- Tune trim vs. measurement fits (w.r.t. Qx=0.32 & Qy=0.28):
  - Horizontal correlation:	ΔQx = (0.96 ± 0.16)·Qx(trim) + (0.03 ± 0.03)
  - Vertical correlation:	ΔQy ≈ X·Qx(trim) + 0.16
    - Scaling 'X' off due to QD polarity error (fixed by Mike the same day)
- N.B. significant discrepancy in between individual data sets
- 'Space Domain' commissioning of feedback control loop (RealTime & TuneViewer)
  - time-domain pending (quadrupole circuit time constants, etc.)

---
Present Commissioning State
... lots of first: coupling measurement
- Measured coupling |C-| ≈ 0.07
  - Compatible with the assumed magnetic field error model at that time (0.06)
- Coupling wasn't corrected though...
  - Needed for nominal injection tunes (Qx = 0.28, Qy = 0.31)

---
Present Commissioning State
... Tune Phase-Locked-Loop Commissioning
- … made the best of the absence of beam in the LHC → used the LHC-PLL installation in the SPS for further tests
  - same interfaces/controls/server/operational GUI as LHC
  - Verified Beam-Transfer-Function (BTF) measurement and PLL logic
- To be tested: real-time display for PLL, LHC-RF interfaces (radial modulation)
- Since BBQ HW is fine for B2 (B1) and that the logic is correct (SPS test): remaining PLL commissioning should take less than one shift/beam.
zoom V
PLL tracking
BTF Scan

---
Chromaticity via Injection vs. Circulating Tune Shift
- Continuous radial modulation (trim) was not fully available/commissioned
- Re-use measured SPS-to-LHC injection energy mismatch !?
  - Measured tune shifts 2009-09-12 (inj. 01:03:52 & circ.: 02:17:46)
    - ΔQx = +0.006 & ΔQy = +0.014
  - ΔQ & side-bands incompatible with earlier meas. Δp/p ≈ 10-3 (2008-09-10)
    - details on sector-to-sector difference and evolution over time → Jorg
hor. spectra
ver. spectra
beam injection
circulating beam
beam injection
circulating beam
ΔQx
ΔQy

---
Chromaticity via Tune Resonance Width I/II
- Some comments on Q', modulation index and tune width of the BTF
  - Turn-by-turn oscillations can be approximated by (n: turn)
Tune/Qs side-band amplitude (Jn: Bessel f.):
  - linear over a wide range of Q'
  - However: Qs not always visible	→ only upper limits in this case
  - Simple estimates for non-linearities
    - ωs: direct spectra observable
    - Δp/p ≈ 10-3: from bunch RF length	(courtesy T.Bohl)
color white { %DELTA z(n) `=` z_0 cdot sin ( 2%pi cdot left[ Q_0 cdot n + {{Q'} over {%omega_s}{{%DELTA p} over {p}}} cdot sin(%omega_s n) right] + %varphi_{%beta} ) }
color white { cos(%omega_c t `+` B sin(%omega_m t)) `=`sum from{n = - %infinite} to {+ %infinite} {J_n(B) cdot cos((%omega_c + n %omega_m ) t)} }
color white { S_n(Q') `=` J_n left( {{Q'} over {%omega_s}} {{%DELTA p} over p} right) }

---
Chromaticity via Tune Resonance Width II/II
- 2008-09-12 (01:03++)
  - Qs = 70 ± 2 Hz (frev = 400.788963 Mhz, UT = 8 MV)
  - Estimates: Q'H ≈ Q'V ≈ 34
    - Settings: Q'H = 2.0, Q'V = -30
    - Asymmetry due to amplitude detuning
      - anti-symmetric (left/right avg.)
  - ~ consistent over several injections
  - N.B. AB-RF found Qs to be 60 Hz	(difference unclear, same spectra)
- changed drastically from Thursday to Friday	(machine was magnetically recycled)
- Injection mismatch fit:
  - Injection mismatch is likely < 10-4
  - Compatible with above Q' estimates	and observed tune shifts (previous slides)
  - further analysis pending (SDDS data)
A(Qx/y)
A1(+Qs)
A1(-Qs)
A2(+Qs)
2Qs

---
Beam 2 - Typical Circulating Beam Spectra
- Horizontal and vertical tunes were usually seen without further excitation
  - Typical signal-to-noise: 10-20 dB
    - FFT1 (continuous system, logging) was slightly more sensitive (+ ~ 5 dB)
  - Sufficient for monitoring & steering for the given beam configuration (single pilot)
Actually, this was a bit of a surprise...
n·2Qs

---
LHC Beam Noise & BBQ Resolution Estimate
- Difference
  - S/NH ≈ 36 dB, S/NV ≈ 42 dB (16382 turns)
    - FWHM ≈ 0.0007 → Amplification = 227
      - Q'H ≈ Q'V < 12
  - Damper kicker (2.5% of 2 μrad @450GeV)
    - Hor. tune amplitude ≈ 185 μm
    - Ver. tune amplitude ≈ 200 μm
- → BBQ noise floor estimates (2·109 p/bunch):
  - horizontal:	< 3 μm
  - vertical:	< 2 μm
- → Residual tune oscillations (quite large):
  - horizontal:	≈ 30 μm (sources?)
  - vertical:	≈ 15 μm (sources?)
- Note: BBQ resolution scales with bunch intensity (1st order)	→ noise floor expected to be ≤ 10 nm for nom. bunches (based on SPS exp.)
  - N.B. Need to correlate this with absolute BPM amplitudes

---
LHC Beam Position Monitor – Turn-by-Turn Stability
- B1 Injection Test on 2008-08-10
- Found 2 (B1)/ 12(B2) polarity/mapping errors – fixed immediately once spotted
  - no additional erroneous BPMs found with circulating beam (injection test paid off)
No obvious time structure from one injection to the next
→ dominated by the 'white noise' floor of the BPM acquisition electronic
Residual min/max trajectory drift is compatible with BPM noise estimate (see below).
r.m.s. turn-by-turn noise: ≈ 200 μm
as expected from lab and electronic design for the given intensity (2·109 protons/bunch)

---
LHC Beam Position Monitor – Orbit Stability B2 – LHC Day 1
Residual injection orbit stability (orbit feedback/radial loop off)
- Effective LHC B2 orbit stability about 5 um → understood (next slide)
- Small oscillations/drifts in point 2 and 4 → also understood (next slide)
horizontal plane B2
vertical plane B2

---
LHC Beam Position Monitor – Orbit Stability B2 – LHC Day 1
Residual Noise Sources
Effective LHC B2 orbit stability about 6 μm, two known sources:
  1. turn-by-turn noise predicition → orbit r.m.s.: ≈ 6 μm (150-200μm, 1024 turns average)
    - However: should be the same for all arc BPMs (same aperture)
  1. Residual noise of the COD power supplies, expectation: 5-10 μm orbit r.m.s.
- Small drifts in point 2 and 4 → thermal drifts (switched off SX4 climatisation)
  - Known from earlier lab measurements
  - Fix: 'somebody' gets a scarf for Christmas & local crate temperature control
- Exact source of the transient orbit spikes is unknown
  - lasts up to two seconds
    - → too slow for an BPM electronics related spike (visible on the whole LHC)
    - (maybe) to fast for COD power-converter transients
  - a forgotten injection/tune/...? kicker magnet?
beam data
crate temperature
temperature-position
correlation (lab)

---
LHC – Orbit Stability – Systematic Transient
- ..at two culprits, one in IR2 the other in IR8 (betatron-oscillation beating)
  N.B. appears to be triggered by the SPS super cycle
- Some likely but excluded sources:
  - individual CODs: fit requires to many sources to explain the seen pattern
  - Injection septa: only one per beam and either in IR2 or IR8 (B2!)

---
Conclusions I/III
– Things done
- Base-line FFT tune acquisition commissioned for B2
  - used to establish circulating beam
  - tested polarities, gains, timing, all detectors alive
  - tested RF damper polarities, rough amplitude calibration
    - Now LHC's baseline exciter for Q measurements
  - tested semi-automatic Q and Q' correction schemes (via LSA)
  - tested MKQ trigger & kicker response (synchro-delay adjustments pending)
- BPMs/Orbit Feedback:
  - good BPM readings, permitting fast commissioning of circulating beam
    - practically all BPM triggered with intensities down to ≈2·109 protons
    - noise floor: COD power supplies (5-10 um), residual BPM 'white noise' (6 um), thermal BPM drifts (~35 um/°C, to be fixed)
    - Only few calibration & mapping errors found after injection tests!
      - We are lucky and should probably play the lottery more often!
      - Few noisy pick-ups electronic chains remain to be check/replaced
  - Data concentration and error/fault filter operational
  - Commissioned/tested about 250/1060 CODs with beam (ongoing)

---
Conclusions II/III
- Things to be (Re-) Done
- Full commissioning of B1 FFT1 & FFT2 BBQ systems
  - first turn works (all detectors alive), plane pending
  - otherwise same procedure as for B2:
    - damper polarities, amplitude calibration, ...
- Full commissioning of B1 and B2 BBQ Phase-Locked-Loop Systems
  - pre-requisite for first ramp! However: if no surprises: < shift/beam
- Test of (semi-) automated Q' & C- measurement and correction procedures
  - after SPS tests: LHC-RF radial modulation
- Feedbacks
  - 750/1060 COD polarity and optic checks with beam pending
  - Quadrupole & sextupole circuit mapping/polarity checks with beam
  - test of > 1300 power-converter real-time inputs (AB/PO)
 → Semi- (or even fully) automated FB on Q/C- is probably fastest/easiest to setup
Training of LHC operators & EIC's	(ongoing, some have never seen/measured/corrected Q/Q' and even less C-)

---
Merry Christmas and a Happy New Year!!!
2008 and initial LHC commissioning were fun...
Thanks a lot for this and see you in 2009!

---
additional supporting slides

---
BI's Wall-Current and Head-Tail Monitor
- Tested that detectors are alive and trigger on given timing event
  - Some software tests/adjustments pending
    - one full acquisition presently results in about 1 GByte of data
    - optimisations in the pipe-line
      - optimised memory usage (Java/JDataViewer)
      - optimised/simplified GUI for the WCM
    - Otherwise: same functionality/state as SPS Head-Tail system (bunch length, intensities, HT modes, chroma estimates, ...)
sum signal
difference signal

---
LHC Beam Position Monitor – LHC Day 1
The LHC BPM System at It's Best I/II
Very first turn – Beam 1
Courtesy J. Wenninger
Very first turn – Beam 2
Courtesy J. Wenninger

---
LHC Beam Position Monitor – LHC Day 1
The LHC BPM System at It's Best II/II
Could reconstruct LHC B1 optic on the few 10% level using only 50 turns
- Nearly all BPM triggered and gave	useful readings
  - LSA concentrator hick-ups	→ relying on FIFO read-out using	YASP
- Vertical beta-beat (blue) vs. model (pink)
  - Surprisingly large: 100%
  - further analysis/correction	proposal pending (R. Tomas)
phase-beating
beta-beating
Courtesy V.Kain
Courtesy V.Kain
beta-beating sector 18
Courtesy V.Kain

---
LHC Orbit Feedback Controller & Service Unit
- Tested data concentration of 120 front-end systems, mapping, etc....
  - Worst case latencies shown to be less than 20 ms (small cross-talk with LSA's CMW-get call)
- Tested first-order BPM error/fault detection scheme
- Now default data source for YASP (orbit, CODs, statuses) and 100k turn GUI (statuses)
- Example: B2 sector test – beam as seen/published by the OFC