Feasibility of (semi-) automated Tune Control in the PS
LHC Beam Commissioning Working Group, 2009-10-20 2009-10-27
Status of Tune, Chromaticity,
and Coupling Measurements
– Take 2 –
Ralph J. Steinhagen, BE-BI
for the BI-QP team: A. Boccardi, M. Gasior, S. Jackson,
P. Karlsson*, R. Steinhagen
*left CERN

---
Outline
- Base-line LHC Q, Q' and C- diagnostics
  - Status Quo: what was available in '08 is also in '09
    - BBQ FFT-based Systems: continuous, on-demand
      - hardware re-tested, RBAC access maps, ...
    - Partially: semi-automated Q' measurement
- New functionalities and not commissioned items in 2008:
  - Tune-PLL (though tested in the SPS)
  - Radial (de-)modulation → continuous Q' measurement
    - Q' expected to be more critical than Q
    - Prerequisite for any Q' monitoring even more Q'-FB

---
Back-bone: Base-Band-Q Principle on a Slide
BBQ detector
BBQ front-end
- Basic principle: AC-coupled peak detector
  - no saturation, self-triggered, no MTG timing required, no gain changes between pilot and nominal beam
    - Measured resolution estimate: < 10 nm → ε blow-up is a non-issue
- One of the turn-key systems in the LHC
  - ... some redundancy: 8 systems available vs. 2 needed

---
LHC Base-Line Q/Q' Diagnostics Overview – Q/C-
Use-Cases Abstraction
Three independent BBQ Tune diagnostic chains available per beam:
  - FFT based acquisition of Q,Q'... – 'periodic'	– tested in 2008
    - one measurement every second (8192 turns ↔ ~0.7 seconds)
    - intended use: monitoring/logging, (feedbacks), fill-to-fill studies, …
      - post-mortem provides beam oscillation for the last ~ 22 seconds
  - FFT based acquisition of Q,Q'... – 'on demand' – tested in 2008
    - n-measurements synchronised to an external event (BPM, BQ, …)
    - intended use: exp.-diagnostics, detailed studies, semi-automated Q'
  - PPL based acquisition of Q, Q'...	– t.b. commissioned in 2009
    - one measurement at high/reduced acquisition
      - 25 Hz for feedbacks, 1 Hz for general purpose logging
    - main use: monitoring/logging, feedbacks, fill-to-fill studies, …
      - However: by itself, no Q' diagnostics
→ most people in the CCC will probably use this device

---
LHC BBQ 'on-demand' System
Mode of Operation:
- FFT based Q acquisition using either
  - simply no excitation! - yielded sufficient data in most cases in '08
- ...if necessary: fall-back to one of the following excitation methods:
  - Chirp-type excitation using the 'RF transverse damper' ↔ Q-PLL
    - for (local) coupling measurement, Qh ↔ Qv mapping, …
  - Single-turn kick using the 'MKQA' (aka. 'tune kicker' via MTG trigger)
    - for special machine studies, measurements involving BPMs or HT, injection

---
Semi-Automatic Q' Measurement
here: SPS Example
- TuneViewer GUI further stores a set of machine settings (LSA) :	Q/Q'-reference, trim settings, radial loop, E, ...
  - Enables comparison/re-verification: Q(')-vs-Δp/p, Q(')-vs-trim, …
- While there is some automatisation (auto-Δp/p trim missing), this remains a cross- or sanity-check only. → nom. requirements: ΔQ'res ~ a few units/s
  - Limited: DB access, high-level data retrieval → The rationale for a Q/Q' PLL
FIDEL perf. assess.
Δp/p []
vertical tune shift [frev]

---
Q Phase-Locked-Loop Scheme on a slide
G_{Beam}(%omega) = color blue {R(%omega)} cdot e^{i color red {%varphi(%omega)}}
beam response
reference signal
BBQ
Trans. Damper/
Tune Tickler
R(fe)∙cos(2πfe-φ)
A∙sin(2πfe)
X
fLP
X
fLP
Rect.
2
Pol.
NCO
phase loop
ampl. loop
R(ω)
φ
φ
ILP
QLP
QLP
ILP
rect2polar
sin(2πfe)
cos(2πfe)
R(ω)
Gpre(s)
zinput(t)
Gex(s)
zexciter(t)
Δf
Δa
beam response signal
90°

---
Q-PLL Commissioning
Example: PLL Setup – Step I (HW lag compensation)
- Essentially BTF and compensation consists of the adjustment of four parameters, preferably during injection plateau (stable tune and chromaticity)
  - 1st step: verify necessary excitation amplitude and plane mapping
  - 2nd step: verify long sample delay (once per installation, constant)
    - full range BTF (will be partially done also without beam)
    - count ±π wrap-around → number of delayed samples

---
Example: PLL Setup – Step II (beam phase compensation)
Measure dφ/df slope ( ~ front-end non-lin. phase and kicker cable length)
Adjustments of the locking phase (tune-peak – phase matching)
dφ/df
Δφ

---
Example: PLL Setup – Step III → Ready for Q/C-/Q' Tracking
Beam-Transfer-Function → PLL lock
- Above step may need to be repeated several times
  - see additional slides on, what can break the loop
- provided absence of “surprises”, initial PLL setup with beam can be quite fast
- Including verification of circuit mapping and polarities:
  - ~2-4 half-shifts with per beam per feedback loop
Q/Q' trims
switch on PLL

---
Q' through RF momentum modulation based method
- There are multiple but similar detection techniques:
  - modulation below Qs → classic schoolbook example
  - modulation above Qs → Brüning's and/or McGinnis' method
- LHC RF power permits only slow modulation (J. Tückmantel)
Q' = {color red {%DELTA Q}} over {color blue {%DELTA p/p}}
slow modulation
fast modulation
Q' diagnostic &
FB operation

---
Q' through RF momentum modulation based method
Controllability of Q' depends on ability to track the tune both accurately & fast
  - intrinsic to this problem:
  - LHC expectations (nominal, expect '09 to be about a factor of five less):
    - Tune:	ΔQ/Δt|max < 10-3 s-1
    - Chromaticity:	ΔQ'/Δt|max < 2 s-1
→ Chose to tackle the LHC Q' measurement in the high accuracy limit:
  - very small but slow Δp/p modulation while tracking Q with a PLL
    - fmod:	0.5 Hz	(setup)	→ 2.5 Hz	(nominal)
    - Δp/p:	~10-4	(setup)	→ ~10-5	(nominal)
%DELTA Q_{res}^{(,)} cdot %DELTA t_{res} = const.
“slow” compared to Q/Q' drifts
e.g. in the SPS/RHIC/CPS/PSB

---
Q'-PLL Commissioning I/II
– LHC RF Frequency Modulation – tested
- RF frequency modulation tested in collaboration with OP/RF
  - N.B. necessity also for radial loop (freq. limits are hard-coded), OFC output:
- At some point of time:
  - Systematic logging of modulation state (there is no fast FGC read-back)
  - Synchronisation with injections: 'on→off→on' at each injection
- Time estimate: ~1-2 half-shifts net (assuming no surprise)

---
Q'-PLL Commissioning II/II
Modulation Amplitude: Δp/p ≈ 1.85∙10-5
tune
max
ΔQmod
min
Q'/Q
- Will commence with a peak-detection based Q' de-modulation
  - re-iteration necessary to optimise Q-PLL bandwidth > fmod
- Time estimate: ~2-4 half-shifts with per beam per feedback loop
(tracking transients: ΔQ' feed-down on ΔQ (non-centred orbit) ΔQ/Δt >> ΔQ'/Δt → SPS specific, LHC: ΔQ/Δt|max < 10-4/s)

---
Summary
- Base-line LHC Q, Q' and C- diagnostics
  - Status Quo: what was available in '08 is also in '09
    - BBQ FFT-based Systems: continuous, on-demand
      - hardware re-tested, RBAC access maps, ...
    - Partially: semi-automated Q' measurement
      - GUI features, cross-checks
  - Most features have been tested without beam as part of the dry-runs	→ only minor re-commissioning expected (tests), 1-2 half-shifts/beam
- New functionalities/not commissioned items in 2008:
  - Tune-PLL (though tested in the SPS) → 2-4 half-shifts/beam
  - radial (de-)modulation → continuous Q' measurement → Q'-FB
    - RF radial loop/modulation → 1-2 half-shifts/beam
    - should be commissioned done prior to first ramp for diagnostic not necessarily FB reasons → 2-4 half-shifts/beam
→ Need real beam to see which functionalities, conveniences & safety features are actually needed for day-to-day operation

---
– Additional supporting slides –
Why we need time for commissioning the Q-PLL:
Phase-Locked-Loop Locking in the Presence of
Coupled Bunch Instabilities, Synchrotron Side Bands and
Tune Width Dependences

---
Advanced PLL Lock issues
Residual Tune Oscillations (e.g. HT instabilities)
- adds vectorial to the carrier signal:
  - excitation amplitude (carrier signal):	A
  - noise in time (frequency) domain: σt (σf)
  - Equivalent number of turns:	N
matrix{ %sigma(%varphi) # %=% # alignl { arcsin left({%sigma_{f} over A}right)} # %=% # alignl {arcsin left(sqrt{2 over N}{%sigma_{t} over A}right)} ## % # % % approx % # alignl {sqrt{2 over N}{%sigma_{t} over A}} # % # % }
for small noise
to signal ratios
Fourier Spectra:
Wavelet Spectra:
σ(φ)
A
σf
φ

---
Advanced PLL Lock Issues
Coupled Bunch Instabilities
- Coupled bunch effects can hamper lock
  - possible causes: impedance driven wake fields, e-cloud, beam-beam, ...
Mechanism (impedance):
- Possible remedy:
  - Detector selects and measures only one (/first) representative bunch
phase response
amplitude response
κ2(s)
κ1(s)
κn-1(s)
E
//
G1(s)
G3(s)
...
G2(s)
Gn(s)
E
E

---
Advanced PLL Lock Issues
Synchrotron Sidebands: PLL locks on the largest peak
Option I: gain scheduling
initial lock: open bandwidth to cover more than one side band (PLL noise ~ chirp)
    - side-bands “cancel out”, strongest resonance prevails
once locked: reduce bandwidth for better stability/resolution
Option II: larger excitation bandwidth, multiple exciter or broadband excitation(FNAL)
initial lock
fBW
once locked
fbw

---
Advanced PLL Lock Issues
Tune Width Dependence I/III
- Reminder:
  - optimal PLL Settings (1/α ~ PLL bandwidth/tracking speed):
D(s) = K_P + K_i 1 over s ~~~ with ~~~ K_p = color magenta K_0 {%tau over {color red %alpha}} ~&~ K_i = color magenta K_0 { 1 over {color red %alpha}}
K0

---
Advanced PLL Lock Issues
Tune Width Dependence II/III
- Optimal PLL parameters (tracking speed, etc.) depend - beside measurement noise – on the effective tune width.
- Intrinsic trade-off:
  - Optimal PI for large ΔQ ↔ sensitivity to noise (unstable loop) for small ΔQ
  - Optimal PI for small ΔQ ↔ slow tracking speed for large ΔQ
- Can be improved by putting knowledge into the system: “gain scheduling”
Tune width change →
change of phase slope (K0)

---
Advanced PLL Lock Issues
Exploitation: Tune Width Measurement using PLL Side Exciter
Resonant phase change ↔ tune width change
→ “free” real-time tune footprint measurement
→ measurable dependence of ΔQ ~ Q'
driven resonance:
tan(%varphi) approx {%DELTA Q cdot %omega_Q%omega_D} over {%omega_Q^2 - %omega_D^2}
Q
Q-ΔQ
Q+ΔQ
2ΔQ ≈ 0.002 « 2Qs

---
LHC Base-Line Q/Q' Diagnostics Overview – Q/C-
Betatron-Coupling Measurement
- No orbit, Q, Q' feedback without control of betatron-coupling
- FFT/PLL measures eigenmodes that in the presence of	coupling are rotated w.r.t. “true” horizontal/vertical tune
  - A1,x: “horizontal” eigenmode in vertical plane
  - A1,y: “horizontal” eigenmode in horizontal plane
- Decoupled feedback control:
  - qx, qy	→	quadrupole circuits strength
  - |C-|, χ	→	skew-quadrupole circuits strength
χ
color red {r_1 = A_{1,y} over A_{1,x}} ~~and~~ color red {r_2 = A_{2,x} over A_{2,y}} newline newline alignl % drarrow ~~~ abs{C^{-%}} = abs{Q_1 - Q_2} cdot {{2 sqrt{r_1 r_2}} over {(1 + r_1 r_2)}} ~~and~~ %DELTA = abs{Q_1 - Q_2} cdot {{(1 - r_1 r_2)} over {(1 + r_1 r_2)}}
first implemented and tested at RHIC/
tested/operational at CERN
R. Jones et.al., “Towards a Robust Phase Locked Loop Tune Feedback System”, DIPAC'05, Lyon, France, 2005

---
LHC Base-Line Q/Q' Diagnostics Overview – Q/C-
Betatron-Coupling Measurement (Real-Beam Data)