2010-03-10 LHC Machine Committee
Status of the Investigations related to
The Broad-Band Perturbation Source(s) in the Vicinity of the Nominal Tune Working Points
Or
'The Hump'
Ralph J. Steinhagen, BE-BI
Special thanks to: M. Gasior, G. Arduini and the OP crew

---
Overview and Summary
- Beam spectrum issues affecting beam diagnostics and operation
  - UPS' 8 kHz line et Co. → W. Höfle et al.
  - Residual tune stability (Q' and other higher-order diagnostics)
    - contribution of RQT[D/F] circuits only 10%
    - further investigation pending...
  - Broad frequency “hump” driven beam excitation
    - Better/more systematic understanding of symptoms
    - Could eliminate some circuits as pot. source by switching them 'off'.
    - No single source responsible for this effect has been identified
    - Collimator at nominal settings will make the effect more apparent

---
Effects seen so far I
- There are at least three++ 'humps', with approx. base-band frequencies:
  - #1 @ ~ 0.185 frev , #2 @ ~ 0.302 frev (vertical tune), #3 @ > 0.333 frev, and
  - #4 & 5 @ ~0.25 & ~ 0.37 frev (much smaller and possible harmonic of #)
- Example: Qv set below 'hump' (red) and after Qv trim on top of 'hump' #2 (blue):
  - Driving of the tune resonance clearly visible → beam size growth → losses
vertical tune
#1
#4
#3
#5
#2

---
Effects seen so far II - Absolute Amplitude
- Assuming single dipolar pertubation → kick ~ 1 nRad kick only
  - a non-issue if the present tune working point wouldn't be exactly on it
Hump #2
400 nm

---
Effects seen so far III – Correlation between Humps I/II
- If structure '#5' is a true second harmonic of '#1' → width difference would give an indication on the base-band origin of the effect
  - Central frequency #1: 0.185 frev or ~2 kHz
  - Shifting the tune out this region would help for the diagnostics
#1
#4
#2
#3
#5
2nd harmonic
4th harmonic ??

---
Effects seen so far III – Correlation between Humps II/II
- Detailed correlation between Hump #1 & #5:
  - likely second harmonic
  - Perturbation #2 (~0.3, vertical tune) could be the fourth harmonic?
    - Would also explain why it is much broader than the others
    - need to move tune off the present tune working point for further studies
fhump#5 &2 * fHump#1
4 * fHump#1
fHump#1
fhump#5
fhump#1

---
Effects seen so far IV
- Structure of the perturbation depends on the observation time-scale, e.g.
  - 0.1 Hz b→ broad 'hump', or
  - 10 Hz acquisition BW	→ narrow-bandwidth line with	shifting mean frequency
- Here, 'Hump' at 0.16 frev:
1024 turns @10Hz
1024 turns @0.1Hz
1024 turns @10Hz
1024 turns @0.1Hz

---
Effects seen so far V – B1/B2 Correlation
Hump on Beam 1 is correlated with the one in Beam 2:
correlation factor = 0.895207
frequency change spectra
1/f reference
BBQ frequency res. limit
for 1024 turns @10Hz

---
Effects seen so far IV – Energy Scaling
- Amplitude seems to approximately scale with energy (-8dB reduction)
  - excludes some effects (e.g quad. vibration)...	… but not all (e.g. quad. current noise)
  - tune spectra before (450 GeV) and after (1.18 TeV) the ramp #6:

---
Vertical Tune Scan across 'Hump Domain'
- The observed excitation frequency are real and cause a blow-up of the vertical emittance
  - 10 % beam size blow-up within about 5 minutes
  - beam is eventually intercepted at an aperture bottlenecks (e.g. TDI or TCDQ)
    - → later collimator would intercept this at an earlier stage
vertical tune frequency
Vertical tune amplitude
Vertical beam size (BSRT)

---
Beam Size Growth and Effect of Power Converter
- Verified effect on the hump for following circuits:
  - Both MSI's, transfer lines, RSS, RCO, RCD and vertical 60A orbit correctors → No effect!
However, whilst effect is visible on both beams, the vertical plane of B2 seems to be more affected:
vertical beam size B2
vertical beam size B1

---
Effect on Beam Life-Time
- Each transient causes some short term beam-life loss but eventually recovers
  - Again: B2 beam-life time much poorer than for B1
FastBCT based beam life-times with minimal collimation:
  - Be aware: these life-times tell you how much intensity is kept in the LHC but not in which shape (e.g. transverse/long. bunch sizes)!!
Beam 1 vs. Beam 2

---
Facts and Figures of 'Hump' Investigations
Not one but at family (at least 3) of different perturbations
- Seen already in 2009 (and 2010)
  - Amplitudes are in the few hundred nanometre range
  - Effect scales down with energy (2009 ramps)
  - Either 'hump' or 'fast shifting line' depending on observation time-scale
  - Correlated between Beam 1 & 2, – however – while seen on both beams, hump effect on beam-life time is more apparent for B2
- Additional studies in 2010 revealed no effect on 'hump' regardless of:
  - Tune or chromaticity changes
  - Single or two beam operation
  - Switching 'off'/'on' circuits: MSI's, transfer lines, RSS, RCO, RCD and vertical 60A orbit correctors
  - If B1/B2 RF frequencies are unlocked
  - If B1/B2 RF frequencies are set apart
  - If damper (ADT) power driver being switched 'off'

---
How to proceed?
Two options the LMC should decide whether:
Find and mitigate the perturbation source – the “clean solution”
  - Other circuits/systems: RCS, MS, RF, effects of He flow-rates/orbit
  - More exotic sources: triplet vibrations, beam screen, vacuum pumps	→ mechanical vibrations in the > 3 kHz range?!?
  - However, we may need soon to move to effective operation with higher intensities
Shift the tunes to another working point (e.g. .45/.46) – the “practical approach”
Hump Domain
Hump Domain

---
Reserve Slides

---
Impact
The “clean solution”	(if hump not identified soon)
- This does probably not impact 3.5 TeV ramps/operation with a few bunches, However:
- Poor life-time with closed collimators
- Limits the intensity we can store and accelerate nominal beam safely
The “practical solution”	(provided beam is stable at 0.45/0.46)
- Buys us some time until we found the 'true' hump source
- Tune/Orbit not an issue with the given diagnostics and controls
- Non-local beta-beating correction may need to be redone

---
Enlarged Tune Diagram up to 10th order
Hump Domain

---
- Effect of trimming RF voltage from 8MV → 4MV → 8MV
  - Only preliminary observations → need to redo these more systematically