Title
ABP-LCU Meeting 2011-03-08
Some Notes on:
Continuous LHC Beta-Beat Measurements
– Status and Prospects for 2011 –
R. J. Steinhagen, A. Boccardi, E. Calvo Giraldo,
M. Gasior, J. L. Gonzalez, O. R. Jones, BE-BI

---
Outline
- Motivation – LHC dependence on known & constant beta-function
  - Machine Protection and Collimation, Physics, Squeeze Diagnostics
  - various existing techniques: 'kick'-type excitation & BPMs,	K-modulation & Q-PLL, Closed-orbit-response (LOCO)
    - do not achieve required resolution, and/or
    - not compatible with nominal LHC operation (ex. levels/beam intensities)
- The aim of the continuous beta-beat measurement studies at the LHC was to
  - provide a proof-of-feasibility for the measurement technique, and
  - to assess magnitude and time-scale of the LHC lattice changes.
- Continuous Beta-Beat system working principle
  - difference to BPM-based acquisition
  - Fundamental constraints and limits
  - LHC installation
- Some examples taken at the SPS and LHC

---
Compromised Machine Protection
Local Orbit Bumps & Beta-Beating
Combined failure and local orbit bumps:
Combined failure and local beta-beating:
- Limits maximum safe intensity and minimum β* in the LHC
  - Mitigation: tighter collimator settings (but implies less aperture → poorer life-time)
IR2
IR7
e.g 'bump in arc'
Potentially:
< 6.7s
Na [σ]
~7.5σ
primary halo
6.7s
5.7s
closed orbit
Orbit-FB
TCP & TCS
MKI
TDI
IR2
IR7
triplets
B) “Secondary” coll.
becomes primary
A) Potentially
< 6.7s
Na [σ]
~7.5σ
6.7s
5.7s
closed orbit
Cont. β-Beat
TCP & TCS
MKI
TDI

---
Collimation Performance Limitations & Constraints on β*
- Two beta-beat components:
  - Static-global	→ AC-dipole driven + BPMs (R. Tomas et al.)
    - absorbed by the beam-based collimator alignment procedure
  - Dynamic-local	→ continuous beta-beat system (BI, IPAC'10)
    - check whether these requirements are kept in a fully dynamic case → initial installation around the primary collimators in IR7
Nominal collimator settings also imply maximum um-level beam excursions before scraping the beam
L_{max} approx {{1} over {4 %pi}} cdot {{color red {N_{max}} cdot n_b f_{rev}} over {%beta^{% * % } %epsilon}}
color red {N_{max}} leslant {%tau_{min} cdot R_q cdot L_{dil.}} over %eta
Collimation inefficiency vs. β-beat
MAC Dec 2004
nominal:
Δx≈35 μm@coll
need to operate here!
courtesy R. Assmann
Coll. system
version ~ 2002
Collimation inefficiency vs. orbit error
courtesy R. Assmann
peak-to-peak orbit error [σ]

---
Limitations on Squeeze Diagnostic
Squeeze involves > 45 individual magnetic strength settings (Optics), so far: no continuous check on effective optics during/at the end of individual steps
- “Classic” methods may not reach/be compatible with nominal requirements
  - K-modulation induced Q-Changes:
    - Limit: knowledge on quadrupole transfer function	(hysteresis, D&S, β|max ≈ 4.2km & ΔQmax<10-3 → Δk/knom<5·10-5)
    - Betatron-coupling, ...
    - Only local (& slow) measurement
  - Kick + turn-by-turn analysis of BPM (phase and/or amplitude), limits:
    - Potential particle loss (beta-functions at triplet) & emittance blow-up
    - Systematic phase errors, amplitude detuning/Landau damping
      - large kicks may probe phase advances (dynamic aperture) which may not be representative for nominal beam operation
      - beam will be collimated at 6 sigma (kick amplitudes < 1.2 mm @7TeV)!
    - … not ideal for continuous monitoring/regular operation (ε blow-up).
  - Closed orbit response analysis (LOCO):
    - resolution/performance compatible with nominal operation
    - Limit: scan requires several minutes per IP (full scan: ~2 OP-shifts)
%DELTA Q ~approx~ {1 over {4%pi}} cdot %beta(s) cdot %DELTA k(s)

---
Betatron Function via Phase-Advance Measurement
- Long history at CERN. Original idea dates back to AB-BI report (doctoral thesis)	P.Castro, Luminosity and Betatron Function Measurement at [..] LEP, CERN SL/96-70 (BI)
- … beating in amplitude related to beating in phase:
Phase sampling:
Beta-Beat reconstruction (FB/Control would work with phases):
{{%DELTA%beta} over %beta}(s) ~=~ {{1} over {2`sin(2%pi Q)}} lint { %beta_k } cos(2 cdot abs {%mu(s)- %mu(a)} - 2 %pi Q) %DELTA k(a)`da
%mu(s) := int csub {0} csup{s} {1 over {%beta(a)}} da
{{%DELTA %mu} over {%mu}} (s) ~ sim ~ {{%DELTA %beta} over {%beta}} (s)
Δφ
-Δφ
Case I:
Δμ12 =45° - Δφ, Δμ13 =90° - 2 Δφ
0
Δφ
Case II:
0
0
Δμ12 =45° + Δφ, Δμ13 =90°
{%DELTA %beta_1} over {%beta_1} ~=~ {cot (%DELTA%mu_{12}^{meas.}) `-` cot (%DELTA%mu_{13}^{meas.})} over {cot (%DELTA%mu_{12}^{theo.}) `-` cot (%DELTA%mu_{13}^{theo.})}
{%DELTA %beta_2} over {%beta_2} ~=~ {cot (%DELTA%mu_{12}^{meas.}) `-` cot (%DELTA%mu_{23}^{meas.})} over {cot (%DELTA%mu_{12}^{theo.}) `-` cot (%DELTA%mu_{23}^{theo.})}
{%DELTA %beta_3} over {%beta_3} ~=~ {cot (%DELTA%mu_{23}^{meas.}) `-` cot (%DELTA%mu_{13}^{meas.})} over {cot (%DELTA%mu_{23}^{theo.}) `-` cot (%DELTA%mu_{13}^{theo.})}
N.B. Phase-Beating usually used for correction!
45°
45°

---
Beta-Beat Sensitivity and Error Estimates
IR optic
Residual resolution/systematic error
  - ARC optics: requires error below ~1°
  - IP optics: requires error below ~0.02°
N.B. Plots have logarithmic z-scale!
{%DELTA %beta_1} over {%beta_1} ~=~ {cot (%DELTA%mu_{12}^{meas.}) `-` cot (%DELTA%mu_{13}^{meas.})} over {cot (%DELTA%mu_{12}^{theo.}) `-` cot (%DELTA%mu_{13}^{theo.})}
arc optic
%DELTA%mu_{1i}^{meas.} := %DELTA%mu_{1i}^{theo.} + %DELTA%varphi_{1i}
45° optic
Δφ12≈ 176° (CMS/ATLAS)
operational range

---
Beta-Beat Measurement Error Sources I/II
Statistical Phase Noise
- Statistical noise adds vectorial to the carrier signal:
  - excitation amplitude (carrier signal):	A
  - noise in time (frequency) domain: σt (σf)
  - Equivalent number of turns:	N
matrix{ %sigma(%varphi) # %=% # alignl { arcsin left({%sigma_{f} over A}right)} # %=% # alignl {arcsin left(sqrt{2 over N}{%sigma_{t} over A}right)} ## % # % % approx % # alignl {sqrt{2 over N}{%sigma_{t} over A}} # % # % }
for small noise
to signal ratios
Delta 1010 intrinsic phase noise@1Hz
Best case BPM+kick:
S/N=1mm/0.2mm &
1024 turns
σ(φ)
A
σf
φ

---
LHC Tune Diagnostics Instrumentation – Direct-Diode-Detection
GHz
High-/low-pass filter
→ μs group-delays
kHz
- Basic principle: AC-coupled peak detector1
  - intrinsically down samples beam spectra: GHz → kHz ('Base-Band-Tune Meter')
    - Base-band operation: very high sensitivity < 10 nm/turn → ε blow-up is a non-issue
  - AC-coupling removes common-mode → only relative changes play a role
    - capacitance keeps the “memory” of the to be rejected signal
  - robust: no saturation, self-triggered, no gain changes to accommodate single vs. multiple bunches or low vs. high intensity beam
- However: BBQ ≠ Beam Position Monitor
  - Fundamentally different acq. techniques but yielding same 'phase-advance information)
  - (Analogue: TF measurement using step generator and scope vs. network analyser)
1M. Gasior, “The principle and first results of betatron tune measurement by direct diode detection”, CERN-LHC-Project-Report-853, 2005

---
Beta-Beat Measurement Error Sources II/II
Base-Band Operation and Systematic Phase Errors
- Sources – usually depend on observation/excitation frequency
  - Systematic delays:
    - Pick-up to acquisition system cable length (e.g. 100 m@ QAC=0.25 frev)
      - SPS: Δφ ≈ 2° LHC Δφ ≈ 0.5°: Δβ/βsys.≈ 3-10% (45° lattice)
    - However, is suppressed for relative beta-beat measurements
  - Low-frequency pre-processing and analogue front-end asymmetry	(mostly HP/LP-filters → μs-level group delays )
    - Delta 1010 – analogue pre-filter:	Δφ ≈ 7° (measured)
    - BBQ front-end: Δφ ≈ 10° (measured, here: only Chebychev stage shown)
    - Systematic drift: < 0.1° → will be further reduced
%DELTA%varphi [deg] ~=~ 360° cdot {{%DELTA%tau}{f}}
Qac
frev

---
2010/11 Test Setup in the SPS and LHC
- KISS digital acquisition: HP Proliant 16”, 1U + M-AUDIO Delta 1010
  - 8 analogue inputs/outputs, 16”, 1U
  - frequency response: 20Hz-22kHz, +/-0.3dB
  - >100 dB dynamic range/S/N ratio
  - THD: 0.00072% (A/D), 0.00200% (D/A)
  - N.B. til-date: no single-event upsets despite being	next to the primary B1 collimators
Tests with beam in the SPS & LHC confirm that there	is no obvious cross-talk in between the regular LHC	WBTN (orbit) and the diode-based continuous	beta-beat acquisition electronics.
allows simple filtering and post-processing in audio domain
BBQ-FE
Q diag./beta-beat
BPM
30++ dB isolation
in between ports
3dB/splitter
DAB64x
DAB64x
DAB64x
WBTN-FE
DAB64x
orbit

---
Example: Beta-Beat/LHC BPM Prototype System in the SPS-LSS5
βv≈100 m
βv≈100 m
βv≈100 m
βv≈20 m
βv≈100 m
βv≈100 m
Measurement (markers), sinusoidal fit (solid line):
BPMB.513
BPMB.515
BPMB.517
BPMB.518
BPMB.519
BPMB.520
{%DELTA %beta_1} over {%beta_1} ~=~ {cot (%DELTA%mu_{12}^{meas.}) `-` cot (%DELTA%mu_{13}^{meas.})} over {cot (%DELTA%mu_{12}^{theo.}) `-` cot (%DELTA%mu_{13}^{theo.})}
{%DELTA %beta_2} over {%beta_2} ~=~ {cot (%DELTA%mu_{12}^{meas.}) `-` cot (%DELTA%mu_{23}^{meas.})} over {cot (%DELTA%mu_{12}^{theo.}) `-` cot (%DELTA%mu_{23}^{theo.})}
{%DELTA %beta_3} over {%beta_3} ~=~ {cot (%DELTA%mu_{23}^{meas.}) `-` cot (%DELTA%mu_{13}^{meas.})} over {cot (%DELTA%mu_{23}^{theo.}) `-` cot (%DELTA%mu_{13}^{theo.})}
1P.Castro, Luminosity and Betatron Function Measurement at [..] LEP, CERN SL/96-70 (BI)
BPMB.517
BPMB.518
BPMB.519
Δμ12
Δμ13
beam
Δμ ≈ 90°
Δμ ≈ 90°
Δμ≈45°
Δμ≈45°
Δμ≈45°

---
QE.603/QE.604 induced β-Phase-Advance Beating
QE.604 (β = 20m!!) – trims:
0A → +50 A → -50 A → 0 A
QE.603 (β = 103m) – trims:
0A → +50 A→ -50 A → 0 A

---
Example: SPS LHC1 Cycle-to-Cycle Stability
In between two coasts...
LHC1
injection
plateau
injection
plateau
LHC1

---
Further Exploitation Possibilities
- System can be further exploited for fast and transparent measurements of physics affecting Δβ/β that earlier required significant amount of beam time
- Example: vertical off-momentum β-Beat:
  - Continuous radial modulation: Δp/p ≈ 1·10-3 @ 1 Hz
  - One full measurement data set every second!
  - N.B. Step in phase → off-centre horizontal orbit in lattice sextupoles

---
LHC Continuous Beta-Beat Measurements Setup
- Located in RR73, the minimum installation without pulling additional cables
- Pick-ups: BPM.7L7.B1 → BPMWC.6L7.B1 → BPMW.5L7.B1
  - phase-advance in between of Δμ≈ 45°
  - dual-plane → 6 channels
- Present installation using 3dB-Splitters works fine for a few (<6-8) pick-up locations but does not scale well (costs) for massive deployment	(dominated by HF cabling, connector, mechanics, etc...)
  - Re-used default BBQ front-ends (not optimised for phase stability)
    - Non-issue for relative beta-beat change measurements
    - Was/can be cross-calibrated (once) against standard BPMs
primary collimator

---
LHC Beta-Beat during the Energy Ramp I/III
– Raw BPM-to-BPM phase-advance measurement
- Perfectly pre-cycled machine, off-resonance excitation, < μm excitation level
  - excellent phase resolution, reduces with energy (N.B. const. kick strength)

---
LHC Beta-Beat during the Energy Ramp II/III
– Reconstructed Local Beta-Beat
- Excellent fill-to-fill reproducibility of about 1% – provided machine underwent a standard magnetic pre-cycle and no quenches have occurred.
- Complemented also by Rogelio's reproducibility assessment

---
LHC Beta-Beat during the Energy Ramp III/III
– Evolution during a “less-perfect” Ramp
- 3/8 main dipole circuits being pre-cycled to 2 kA instead of the default 6 kA.
- Percent-level correction of the transfer function of one of the warm quadrupole magnet in the vicinity of the test setup
Still, small compared to required dynamic beta-beat of Δβ/β|max< 20%

---
LHC Beta-Beat during Squeeze
Squeezing from β* = 10 m → β* = 2 m in all four IPs
- Nodes at optics matching points & leakage of squeeze of about 5% in IR7
- For the time being considered as small and compatible with present collimation requirements for low-intensity beams in the LHC.
- N.B. Meas. much noisier due the reduced signal-to-noise ratio during the β*-squeeze of only 16 dB (reduced excitation strength at top energy + small bunch intensity)

---
Conclusions
- The aim of the continuous beta-beat measurement studies at the LHC was to
  - provide a proof-of-feasibility for the measurement technique, and
  - to assess magnitude and time-scale of the LHC lattice changes.
- Continuous beta-beat measurement system could achieve a 1% resolution
  - only limited by the maximum off-resonance excitation power, and
  - for excitations being kept below a micro-meter	→ transparent for nominal LHC operation.
2010 measurements seem to confirm that fill-to-fill beta-beating is reproducible within 1% – provided machine underwent a nominal pre-cycle
- Present SPS/LHC installation using 3dB-Splitters works fine for a few pick-up locations but does not scale well (costs) for massive deployment (dominated by HF cabling, connector, mechanics, etc...)
- If there is some interest/requirement: should and needs be specified as part of a future BPM system at an early stage, e.g. SPS MOPOS renovation & future LHC BPM upgrade

---
additional supporting slides

---
Beta-Beat Sources
- Beta-Beat Sources
  - Quadrupole gradient and Momentum errors
  - Feed-down due to off-centre horizontal orbit in lattice sextupoles
Requirements: Brüning, Fartoukh, LHC Project Report 501

---
Compromised Machine Protection via Orbit Bumps
Combined failure: Local orbit bump and collimation efficiency (/kicker failure):
- To guarantee two stage cleaning efficiency/machine protection:
  - Local: TCP must be >0.7s closer than TCS w.r.t. the beam → Orbit FB
  - Global: no other object (except TCP) closer to beam than TCS
→ Orbit bumps may compromise function of machine protection/collimation
→ tackled by LHC Orbit Feedback
IR2
IR7
e.g 'bump in arc'
Potentially:
< 6.7s
Na [σ]
~7.5σ
primary halo
6.7s
5.7s
closed orbit
TCP & TCS
MKI
TDI

---
Compromised Machine Protection through Beta-Beat
Combined failure: beta-beat and collimation efficiency
“Collimator gap must be 10 times smaller than available triplet aperture!”1
  1. β-Beat reduces required protection: Δβ/β ≈ 20 % → 20% tighter collimator settings
  2. β-Beat reduces cleaning performance
IR2
IR7
triplets
A) Potentially
< 6.7s
B) “Secondary” collimator
becomes primary (here: Δβ/β = 1)
Na [σ]
~7.5σ
6.7s
5.7s
closed orbit
TCP & TCS
MKI
TDI
~ 0.15
~ 0.6
a_{coll}~leslant~ a_{triplet} `cdot` sqrt{%beta_{coll} over %beta_{triplet}} `cdot` left({A^{max}_{primary}} over {A^{max}_{secondary}}right)
1 R. Assmann, “Collimation and Cleaning: Could this limit the LHC Performance?”, Chamonix XII, 2003

---
Performance Limitations & Constraints on β*
N.B. C = βtrip· β*
β-beat meas. +
RT-Feedback?
IR Upgrade
LHC Orbit Feedback