Title
2011-07-15 Mini-Chamonix Workshop
Orbit Stability Prospects
Ralph J. Steinhagen for BI-QP
special thanks to: R. Jones, J. Wenninger

---
Good and bad orbits in CMS
Achieved Stability vs. Tolerances
Q: Can the Orbit Stability further improved in the IRs for 2010?
H plane
Fill 1895
0.7 sigma
Outlier fill 1898
1.4 sigma

---
Achieved Stability vs. Tolerances
Long-range collimator requirements are effectively peak-to-peak tolerances
1σpp@'TCT↔TSCG' translates to 250 μm or 0.5% at the given BPMs!!
Target requirements are beyond the initial BPM design (1998)
Known systematic on temperature, intensity and bunch filling pattern
Several improvement have been and will be put in place to mitigate these
Still, day-to-day calibrations vary by 200-300 μm (~7 ADC bins)
remaining uncertainty of the calibration & system stability
this is the error one should expect if calibrations are skipped for >24h
Present performance is in line with the initial BPM system design
Noteably, achieved 1 σ reproducibility vs. allocated 2.5 σ tolerances	→ can these be re-distributed/accounted in a different way?
Triplet ↔ TCSG horizontal-margin loss (courtesy J. Wenninger):
1σ
0.6σ
Real outlier on B2
IR5
IR1
May → June

---
Orbit Correction & Feedback Strategy I/II
Presently we deliberately limited the overall correction bandwidth and locality
  1. localised bumps are explicitly removed, i.e. the orbit control is not applied on a per BPM or collimator basis but on the average over a given region.
  2. Orbit-FB bandwidth is (artifically) limited to below 0.1 Hz:
There is enough margin to further minimise these transients through more regular feed-forward and/or adaptive bandwidth scheduling
Squeeze
B1
Collisions
Ramp
B2
Interlock Limits

---
Orbit Correction & Feedback Strategy II/II
In principle, a more local control can be achieved but makes the corrections more sensitive and dependent on performance and errors of individual BPMs
non-singular
LHC BPM eigenvector #521 l521= 1.18•100
one of many patterns required
for a local control at the TCT, IR6
↔ no redundancy

---
BPM Improvements
- Removed LSS intensity cards → provides larger overlap of sensitivity ranges (probably a non-issue for targeted larger bunch intensities)
- 'Synchronous orbit' mode e.g. triggering on non-colliding bunches can further reduce filling-pattern dependences and spurious triggers due reflections for directional coupler BPMs (BPMSes)
      → basically there, but needs further integration (i.e. injection sequencer)
Temperature stabilised racks: massive undertaking of removing, disconnecting, installing and reconnecting 32++ existing racks, cooling water infrastructure, 2200 fiber connections → requires a long shutdown
Provided the presently achieved 200-300 μm reproducibility is not sufficient:
- More robust BPM electronics → non-trivial, but being looked into:
  - Diode-based Orbit acquisition
  - BPM signal commutators to remove systematic offset drifts
- additional redundancy* in critical locations:
  - additional acquisition chains on the same pick-up
  - Additional pick-ups!!
*N.B. SL sources have for this reason about 2-4x the BPM for the same phase advance

---
Conclusions
- Achieved measured fill-to-fill orbit stability of about ≤ 1 σ over the past two month of physics which was better than the allocated 2.5 (/1.6) σ margin between the TCT and dump protection...
  - Could one consider leveraging this by basing the tolerances on the actually achieved rather than specified beam parameter stability?!?
  - Orbit interlock de-facto enforces these tight tolerances
- Orbit stability ultimately limited by the performance and BPM systematics
- Little margin to gain on BPM performance this year – any major accuracy improvement would require additional hardware and machine modifications, i.e. temperature controlled racks, additional acquisition chains & pick-ups.
- Nevertheless, there is some margin to improve certain specific items:
  - feed-forward corrections and adaptive feedback bandwidth → squeeze
  - 'synchronous-orbit' → bunch-filling pattern and spurious triggers that plague the directional couplers in the IRs

---
Additional slides

---
Residual DAB Calibration Stability
From LSA... (compensated for DAB reference temperature & coefficients)
9.3 units
↔ 200-300 μm

---
Residual DAB Calibration Stability
Correlation with Temperature

---
LHC BPM Bunch Filling Pattern Dependence
Largely compensated by choosing the proper calibration mode, small asymmetries remain since true filling pattern contains e.g. gaps to accommodate injection and dump kicker rise-times

---
Diode ORbit system functional diagram
Diode ORbit Acquisition System
Functional Diagram
Primary application: beam-based col. jaw centering using in-built buttons
- Excellent μm-level resolution and stability
- Still, no “silver bullet” solution (yet) due to important non-linear systematic for off-centre beams → require further investigation

---
Orbit Stability during one LHC Fill
- Orbit stability during physics < 5 μm over 15 hours (Orbit-FB 'off')
  - new high-accuracy diode-based beam position monitor system: Δxres < 0.5 μm
Reference changes at ramp start
and start of squeeze

---
Residual LHC BPM Dependence on Intensity II/IV
High-Sensitivity Mode
arc12 B1
IR1 B1
BPMSW.1L1
IR1 B2
arc12 B2

---
Residual LHC BPM Dependence on Intensity III/IV
Low-Sensitivity Mode (standard operation)
- Better 'B1 vs. B2' symmetry for LSS BPM after intensity card removal
  - Only a few specific channels dropping out a earlier … to be investigated
LSS1.B2
LSS1.B1