2011-12-18
Head-Tail DAQ Upgrade Meeting
Ralph J. Steinhagen,
Beam Instrumentation Group, CERN

---
The Large Hadron Collider LHC
The Large Hadron Collider LHC
Installed in the LEP tunnel, 27 km, Depth of 70-140 m
the Alps
Lake of Geneva
Sector 34
Jura mountains
LHC ring

---
Accelerator energy (GeV)

---
LHC dipole magnet
27 km Circumference – 1232 LHC dipole magnets
7 TeV ↔ B field 8.3 Tesla	↔ 11.8 kA @ 1.9 K (super-fluid Helium)
two-in-one magnet design → ~ two accelerators
Operating challenges:
Dynamic field changes at injection
Very low quench levels (~ mJ/cm3) in an environment that stores MJ → GJ

---
Motivation – HeadTail Oscillations
What we love to see also in the SPS/LHC
Intra- and inter-bunch beam motion is one of the observables of particle instabilities
e.g. J. Gareyte, “Head-Tail Type Instabilities in the PS and Booster”, CERN, 1974
- PS: 120 ns bunch length ↔ less demanding in terms of bandwidth
- SPS/LHC: bunch length down to 1 ns → requires GHz analog bandwidth
T H
transverse
longitudinal
20 ns/div
E
s
T H
T H
τ
Δp/p
ωs
1
2

---
Classical Head-Tail Instability Detection
Implemented/tested at CERN-SPS, Tevatron, LHC:
- Long strip-line BPM (60 cm, to avoid signal-reflection mixing)
- Σ-Δ hybrid (removes common mode signal)
- Fast-sampling to resolve internal bunch structure
  - ~ ns bunch length → GHz scope bandwidth
- Need to compensates for non-beam effects:
  - pickup- & hybrid response,
  - cable dispersion, …
  - cable reflection, imperfect impedance matching
  - electrical offsets
A
180°
Hybrid
Σ
Δ
B
Surface
Tunnel

---
Head-Tail Motion Signal-Spectra Simulation
- Higher-order HT instabilities
- Can be detected e.g. via:
  - time-domain: counting number of	zero-crossing, rising/falling-edges
  - freq.-domain: standard peak search,	provides also indication for
    - mixed modes
    - HT mode strengths
Courtesy E. Metral
m=2
m=3
m=6
m=2
m=3
m=6
sum signal
sum signal

---
Head-Tail Motion Signal-Spectra Simulation
- Additional diagnostics: power spectrum is sensitive to bunch shape, bunch length, bunch intensity, longitudinal phases, …
  - But signal decreases significantly	→ amplification by 40 dB above 1-2 GHz
gaussian
cos2
parabolic
single shot noise floor

---
Head-Tail Signal Example SPS
Σ
Σ
Δ
Δ
animation courtesy B Salvant (2010)

---
Limits of Classical Head-Tail Monitoring Approach
What our ABP colleagues like to see (here: HT mode 'm=1'):

---
Digital Acquisition System Upgrade I/II
- First steps, tackle existing DAQ limitations, initial system was designed to:
  - track 1 bunch over 1000 turns	→ now need to track batches of bunches over 1000 turns
    - Requires more memory → more post-processing to reduce data rates
  - measure 'm=1' HT modes (~1 GHz) → need to go higher for 'm>1' modes
- Limited number of suppliers for systems with fbw>2 GHz bandwidth, all providing systems with >6 GHz bandwidth but with difference w.r.t. RAM:
    - Agilent (DAQs and Scopes): up to 1 GB/channel
    - LeCroy (Scopes only): up to 256 MB/channel
    - Tektronix (Scopes only): up to 128 MB/channel
    - Guzik (DAQ): up to 32 GB/channel
- Huge buffers simplify triggering and data selection but also make smart memory management, online and automatic post-processing mandatory, i.e.	“1 GB of data requires >10 seconds for read-out with standard Gigabit Ethernet link – no post processing yet” we ideally desire an answer/pre-analysis every ~30 seconds”
  - technically feasible but should be kept in mind during design stage

---
Digital Acquisition System II/II
- Gigabyte Sampling Buffers: The aim is not to systematically process, analyse and store the whole buffer but to allow data-mining in case of instabilities:
  - Use-case example 1: Unstable bunches or batches are not known in advance. However, the unstable ones and timing can be identified with e.g. FastBCT and other instruments after the instability occurred	→ can be used to narrow the range of the data to be retrieved
  - Use-case example 2: instrument could be used by several users with different diagnostics indicators at the same, e.g. 'user 1' monitors few bunches over maximum number of turns while 'user 2' acquires the first 500 full turns looking for bunch-by-bunch oscillations but at a reduced sampling frequency.
  - Use-case example 3: do not just fulfil the minimum required but keep specification open to allow future upgrades and R&D, i.e. present HT monitor was designed to measure Q' but not as instability monitor, larger buffer and bandwidth allowed the exploitation for other beam studies outside the scope during the design.	(N.B. small difference in price for going from 2.5 → 6 GHz, ~ 25% of total costs)

---
Integration options
Option A – using dedicated machine
bottleneck: Ethernet or increased costs/integration of 40 Gbit/s link
Option B – using VMware
- Much faster data transfer	→ limited only by PCIe x4 (x8)
- However: VMware PCI-Express bridge needs to be demonstrated
PCIe
Controls/
post-processing
Controls/
Post-processing
PCIe
DAQ
DAQ
Real-time Linux
MS Win7
MS Win7
Real-time Linux
1 Gbit/s

---
Reserve slides

---
Head-Tail based Q' Diagnostic I/II
- Instability can be exploited to give in estimate on Q' in the first place:
  - track two slices, 'head' and 'tail' in the bunch distribution	:	(tune: Q, long slice position: τ, synchrotron frequency: ωs, turn: n)
    - Phase difference of betatron oscillations:
%DELTA z_{HT} {size 10 (n)} `prop` sin(%psi_{HT} {size 10 (n)})
%psi_{HT}{size 10 (n)} `=`2 %pi Q cdot n+ %DELTA %phi_{%beta} ~~with~ %DELTA %phi_{%beta} `approx` Q' `cdot` {{%omega_0 hat %tau} over {%eta} cdot sin(%omega_s cdot n)} underbrace {%DELTA p/p modulation}
one synchrotron
period
bunch head slower than tail
bunch head faster than tail
bunch tail faster than head
bunch tail slower than head
long. bunch position