Title
LHC Beam-Beam Compensator Prototype
– Update –
Ralph J. Steinhagen
for and with input from:
O. Aberle, R. Assmann (Collimation), A. Bertarelli, A. Dallocchio,
S. Fartoukh, R. Jones, J.-P. Koutchouk, F. Bertinelli, D. Perini,
A. Ravni, T. Rijoff, S. Redaelli (Collimation), R. Veness,
J. Wenninger (MPP), F. Zimmermann (ABP lead), M. Zerlauth

---
Motivation for Installing a BBC Prototype in the LHC I/II
- Passed several Milestones
Initial proposal based on to J.-P. Koutchouk's note: CERN-SL-2001-048-BI
Since, SPS wire-wire and RHIC beam-wire experiments demonstrated that:
  1. “detrimental wire effect on life-time can be compensated by another wire”
  2. Benchmark of numerical tool chain → indication of what to expect at LHC
- Further tests require a true long-range beam-beam limited machine...	→ proof-of-principle requires BBC prototype into machine before HL-LHC
~9.3σ

---
LHC Beam-Beam Compensators Specification I/III
- Reservations around IR1&IR5, LHC-BBC-EC-0001:
  - Min. LRBB → BBC phase advance: Δμ ≈ 2.6° (→ 3.1°)
  - Symmetric beta-function: βx/y≈ 1000 m (for β*= 0.55 m)
    → Prototype with nominal parameters not feasible during LS-1 (MPP, Cleaning,..).
Compromises in favour of an early proof-of-concept tests to guide and	to gain lead-time for nominal system at HL-LHC:
  1. Operation close to MP envelope:
    1. need to embed wire in collimator jaw-type structure – preferred
    2. Operate within shadow of TCTs → ineffective w.r.t. beam-physics
  1. Limit nominally 8 BBC units to two:	BBC.B1-H replacing TCL.xR1.B1 & BBC.B1-V replacing TCT(P).xL5.B1
  2. Wire parameters:
    - Solid wire radius of ~ 1mm → 1kW power dissipation
    - sub-σ level of hor./ver. position control
    - Nominal scheme: I = Ipeak · √2π · σs · nparasitic = 72 … 350 Am (max.)
    - Pulsed wire to accommodate differences for PACMAN bunches → not practical at this stage → stick to DC compensation only

---
Proposed Prototype Layout after LS-1
- Choice of replacing TCTP/TCL...
  - minimises the MP risk w.r.t. asynchronous beam dumps,
  - reuses existing collimation infrastructure, and
  - allows testing with nominal (/ATS) optics after LS-1.
BBC
BBC
x2
x2
Nominal
Prototype
TCL.B1 (Cu)
BBC
BBC
x2
x2
TCT(P).B1 (W)
~105 m
B1
B2
20 mm
clearance
y
x
W
Cu

---
Example: SPS Prototype Design
Design functionally tested w.r.t. BPM response, integration etc.
Main required modifications: wire-in-jaw, larger buttons → cable/water routing
Ch. Boccard et al. DIPAC'11, CERN-BE-2011-023 BI

---
Preliminary Ansys Results (Axel Ravni, BI-ML) I/II
350 A through
Cu wire Ø=1mm
0.1mm Ceramic Insul.
Tungsten block
Cooling@20°C
Finite-Element and analytic estimates agree for given (perfect) conditions
to be further studied → more specific model and lab-prototype test in progress.
20 mm
clearance
y
x
W
Cu

---
Proof-of-Concept: Wire-in-Jaw Embedding & Cooling using commercially available THERMOCOAX solution (A. Ravni)
Prototype to be tested in March → then in || integration into W-jaw of TCTP&TCL

---
TCTP and Wire-in-Jaw Design I/II
- Can re-use nearly 100% of existing TCTP design.
- Remaining challenge: finding space for the wire current feed-through amongst the cooling circuits and BPM button feed-throughs.
Courtesy Luca Gentini, EN-MME

---
Not a green-field design – leverage EN-MME experience:
TCTP and Wire-in-Jaw Design II/II
Gretchen Frage: do we wait until the lab prototype tests are conclusive or do we start with the design/production right away in March?
TCTP cross-section
to be added
for BBC
Prototype
Courtesy Luca Gentini, EN-MME

---
Summary and Status
Necessary technical infrastructure planned to be installed during LS-1 (powering, girders, water, cables, etc.) → ECR and integration in progress
- Mechanical feasibility, material and vacuum compatibility tests
  - mechanical and electrical constraints, vacuum compatibility	→ lab mock-up test to validate design (Axel Ravni, BI-ML) → March'13
 → After/in || wire-in-jaw prototype mods of existing TCTP design (A. Bertarelli)?
- Impact on machine impedance (E. Metral et al.)	→ BBC is similar/the same as the TCTP from an RF point of view
- Beam cleaning and robustness simulations (FLUKA) – not started yet, tbd.
- Medium term action items that are not scheduled yet:
  - Add. R&D and beam instrumentation
  - BBC prototype construction
  - Pre-installation prototyping and HW integration tests (Lab-cycling)

---
Reserve slides

---
LHC-BBC Prototype – Proof-of-Concept after LS-1 I/II
BBC Prototype

---
LHC-BBC Prototype – Proof-of-Concept after LS-1 II/II
Crossing angle with average separation of 12 (nom. LHC) → 7.1σ (LR-limited)
present LHC
proof-of-concept

---
Preliminary Cost Estimates and Planning - DRAFT

---
Physical Space IR5
Requires Horizontal BBC
reserved location IP → 105 m
Excluded by
LR beam-beam simulations
(thesis T. Rijoff)
TCT and roman pots
Between Q4 and Q5